## Slide 1: ELEC-E8423 - Smart Grid Supergrids – 41
Benjamin Mehu
Simon Mottet
19.03.2019

## Slide 2: Introduction
Context
Technology
Social, Economic and Political challenges
Projects
Notes: Context : Explication du systeme existant et des évolutions, introduction des énergies renouvelables
Technologie : Comparaison AC et DC, prix sur longue distance, aspects techniques, infrastructures,
Architectures possibles, combinaison
Mise en pratique : Risques, changement pour les exploitants, conduit réseaux, responsabilités des pays
Projets passes, actuels et futurs :

## Slide 3: Context
The Electric Power Industry
In the past :
Stable & mature sector
Well know operation
Not so much innovation
Polluting generation
Now & in the future :
New Production Technology
Lots of innovations
Clean supply of electricity
Need more flexibility
Notes: For a long time, the electric power industry was seen as a stable and fully matured
sector, which was operating well without much innovation.
Over recent decades, the situation has changed drastically, with a rapid development and innovation process.
There is a strong interest from the general public for a cleaner and cheaper supply of
electric energy
The consequences are a fundamental changes in the generation and transmission of electricity

## Slide 4: Context
Renewable potential in Europe
- Wind potential
- Solar potential
- Load center
Notes: A strong increase in generation from renewable is expected in europe, principally from solar and wind.
Best sites for wind power plant : north sea region, western part of europe
Best sites for solar power plant : around sea mediterranean
Big challenge => localisation of production
Comparaison with the past = new challenge
-challenge : gene/conso are not simulaneous
-market challenge : more flow In transmission syst and more vairable
For all those reasons : supergrid

## Slide 5: Technology
DC : Converters: (Thyristors/IGBT), HVDC breakers, filters, 2 conductors
AC : Higher transmission towers, Shunt reactors, 3 conductors
Lower losses for long distances
Source: ABB
Source: ABB
Notes: Development of supergrids is directly linked with development of HVDC technology.
But why should we use direct current ?
The main reason is that for longer distances total lines cost become smaller.
First we can look to investments cost. Actually, investments for DC converter stations are higher because they should include:
Of course converters such as high power thyristor or IGBT and also large filters to flatten the DC current.
But the price for AC lines infrastructures is higher than DC lines, because transmission towers are bigger.
Furthermore, AC lines produce reactive power, so it is necessary to compensate it with shunt reactors, which are very expensive, and the longer is the distance, the bigger they are.
Losses are also higher in AC because of the number of conductors, we need only 2 in DC and 3 in AC. For example for a 2000 km long and 800kV line, losses are estimated to be 5% for DC and 10% for AC.

## Slide 6: Technology
Connect asynchronous power grids
Converter stations are expensive
Multi-terminal DC grid
Meshed DC grid
Independent DC lines grid
Source: IEEE
AC/DC grids topologies
Notes: Creating a super grid does not mean replace every AC grids.
The idea is to connect different asynchronous AC grids and to make the transfer of energy easier.
There you can see several AC/DC grids topologies.
The first one is the cheapest and the easiest one because it deals only with one frequency and one DC grids.
We can increase the reliability of this grid by adding backup connections as you can see in the second example with this meshed grid.
The last example is the most complex one because it deals with several DC grids, with different voltages, and is of course the most expensive because we need more converter stations. But it could be the best way to have a robust and reliable grid.
Now we can have a look on how to connect AC and DC.

## Slide 7: Technology
Line- commutated converter
Thyristors
Lower station losses, higher converter ratings
Harmonic distortions, bigger AC and DC filters
High power flow
Voltage-source converter
IGBT
Reactive or active power absorption, Better "black-start" capability
Cost
Connection of low power grids
Adapted to multi terminal connections
Source: IEEE
Notes: It exist two types of HVDC converters: LCC and VSC, they have their own benefits and drawbacks.
LCC uses thyristor technology and VSC uses IGBT, the main difference is that it is possible to control switching of IGBTs.
Those switches can be controlled by pulse width modulation, so it make possible to absorb reactive and active power.
Higher converter ratings of an LCC system leads to lower station losses, that’s why LCC are often used to connect high power system.
The problem of LCC system is that it cant be connected to small AC sytem because harmonic pollution can lead to commutation problems .
VSC is more appropriate to multi terminal connection between AC system because two electricity systems connected by the DC link are electrically separated. Furthermore, when one of these systems experiences a blackout, this system can be restarted through energy transfer by the DC link.

## Slide 8: Social, Economic and Political challenges
Social issues : Not in my back-yard phenomenon
Economic : 4 W's matters
Political organization : Differents law & organization. Futures of TSO ?

## Slide 9: Projects
1954: HVDC line between Sweden and Gotland island
Mercury arc valves - 100km, 20MW/100kV
Jinping – Sunan, China : Thyristor, 7.3GW, 2000km, 800kV, 5kA DC
Most powerful VSC line :
France – Spain: 2.8GW, 65 km, 2x320kV
Source: INELFE
Notes: To end this presentation we wanted to talk about few projects and compare them to the first HVDC line, to prove that research and development about materials offers new possibilities.
So, the first HVDC cable opened in 1954 in Sweden. It was created to link Gotland Island to Sweden which were separated by 100km of water. During 30 years they used mercury arc valve to convert AC to DC. It was a 20MW and 100kV cable.
Nowadays the most powerful line is in China and uses LCC technology. This is a 2000km long UHVDC power line which transport clean power from hydro station in central-western china to the highly industrialized coastal area in eastern China. Its power is 7.3GW, it is more than 300 hundreds time the Sweden to Gotland Island cable.
The most powerful line using VSC technology links France to Spain, its power is 2.8 GW and strengthen the european power grid. It transmit around 3% of all the power transmitted between France and spain and the goal is to be 10% in the next few years.

## Slide 10: Conclusion
Supergrids :
  Improve security of power supply
  Increase penetration of renewables energies
  Directly linked with HVDC development
Many challenges :
  Regulatory
  Financial
  Political
Notes: To conclude about this subject we can say that the main points you remember about our presentation are that supergrids :
- Improve the security of power supply
- Increase penetration of renewables energies
And are directly linked with HVDC development
But it exist many challenges such as regulatory, financial or political challenges.
Thank you for your attention, now if you have any question please ask

## Slide 11: Source material used
https://www.ieee.org/content/dam/ieee-org/ieee/web/org/about/hvdc_grids_for_european_transmission_system.pdf
https://spectrum.ieee.org/energy/the-smarter-grid/chinas-ambitious-plan-to-build-the-worlds-biggest-supergrid
http://publications.lib.chalmers.se/records/fulltext/242743/242743.pdf
https://spectrum.ieee.org/energy/the-smarter-grid/lets-build-a-global-power-grid