## Slide 1: ELEC-E8423 - Smart Grid 23. Communication solutions for Smart Grid
Tero Koivunen
Sami Pitkäniemi
16.04.2019
ELEC-E8423 - Smart Grid

## Slide 2: Introduction
An electric grid without adequate communications is simply a power distributor.
Inclusion of two-way communications that the power grid is made "smart“.
Presentation overview:
  Smart grid communications architecture
  Communication technologies involved
  Challenges & standards
  Conclusions
ELEC-E8423 - Smart Grid
Investing Finland, 2016

## Slide 3: Smart grid communication
In Smart Grid, data should go
wherever energy goes.
There are many communication
solutions.
However, different parts of SG
have different requirements.
SG communication can also be represented according to a NIST - model
(National Institute of Standards and Technology)
Kalabachi, 2016
Obogo et al, 2017

## Slide 4: Smart grid communications architecture
ELEC-E8423 - Smart Grid
Smart grid communications network is divided into many network areas.
Smart grid end-to-end communication architecture have different domains: end-user premises, transmission grids and distribution grids and generation.
ESINA,2016

## Slide 5: Smart Grid Communication Requirements
Application | Data (kbps) | Latency | Rel. (%) | Coverage (km)
Advanced Metering Infrastructure | 10-100 per node | 5 s - several hours | 99.0-99.9 | 5-10
On-demand meter reading | >100 | <5 s | >99 | 5-10
Multi-interval meter reading | >100 | <4 hours | >99 | 5-10
Demand Response Management | 14-100 | 500ms - min | >99 | 5-10
Pricing | 10-100 (depends on application) | <1min | >98 | 5-10
Grid-To-Vehicle | 9.6-56 | 2s - 5 min | 99.0-99.9 | 10-100
Vehicle to Grid | 5-10 | <1min | 99.0-99.9 | 10-100
Distribution Automation | >18 | <1 sec | 99.0-99.9 | Up to 10km
Distributed Energy Resources | 9.6-56 | 300 ms - 2s | 99.0-99.9 | 10 - 100
In addition, all applications need a high security.
Table data source: LI et al.: SMART CHOICE FOR SMART GRID: NB-IoT, IEEE INTERNET OF THINGS JOURNAL, VOL. 5, NO. 3, JUNE 2018

## Slide 6: Current Communication standards for SG
No “one size fits all” solution
Utilities have several private networks
Current “smart” features are tacked on using public internet
Communication standard | SG Segment | SG Applications
Power line communication | HAN/NAN | Distribution Autimation, AMI
Optic Fibre | HAN/WAN | Core/Backhaul infrastructure
ADSL/DSL | HAN/NAN/WAN | AMI,SCADA,DA
WIFI | HAN/NAN | DA,AMI,DER,DRM
Cellular/GSM/GPRS (2G,3G,3.5G,4G) | HAN/NAN//WAN | Distribution Substation
LTE-A | HAN/NAN//WAN | SH Wireless surveilance, SCADA,WASA
ZigBee | HAN | Home, Automation, AMI,DRM,DER,DA
Bluetooth | HAN | Home Automation
WIMAX | HAN/NAN//WAN | Distribution automation, (DA),AMI,DER
Satellite | HAN/NAN//WAN | AMI, DA, SCADA
LoRa | HAN/NAN//WAN | Home Automation, AMI
Sigfox | HAN/NAN//WAN | Home Automation, DA
RPMA | HAN/NAN//WAN | AMI,DRM,DA
NB-IoT | HAN/NAN//WAN | AMIU,DRM,DA
LTE Cat-1 | HAN/NAN//WAN | SG Wireless Surveillance, SCADA,DER,DRM,DA
LTE-M1 | HAN/NAN//WAN | SCADA,DER,DRM,WASA,DA
Table data source: Ogbodo et al. “Cognitive Radio Based sensor network in smart grid: Architectures, Applications and Communication Technologies”
IEEE ACCESS, 2017, Doi: 10.1109/ACCESS.2017.2749415

## Slide 7: 5G future
More radio resources
Machine to machine communications
Flexible
Nokia 5G Future Presentation

## Slide 8: Challenges and standards
Challenges
  Lack of required interoperability standards.
  The technology of existing communication networks in power grid are decade-old.
  Meeting the latency requirements for mission critical applications majorly in WAN.
  Concerns related to cyber security and data privacy.
  Meeting the requirements of various emerging models in the grid.
Standards
  IEEE P2030 - Guide for Smart Grid Interoperability of Energy Technology and Information Technology Operation with the Electric Power System (EPS), and End-Use Applications and Loads
  IEEE P1901 - Standard for high speed communication devices via electric power lines, often called broadband over power lines (BPL)
  IEC 62351 - Power systems management and associated information exchange - Data and communications security
  IEC 62056 - Electricity metering data exchange
  PLC G3 - Powerline communications standard that will enable the smart grid vision
  IEC 61850 - Communication networks and systems for power utility automation
  All the standards required for smart grid communications in various applications and domains can be traced from IEC webstore - http://smartgridstandardsmap.com/
ELEC-E8423 - Smart Grid

## Slide 9: Conclusions
Interoperability is a key element in smart grid and this can be achieved by communications systems.
The communications network system is divided into three major parts according to the location and requirements.
One has to select the required communication technologies (among various available wired and wireless) based on the application requirements (5G is simplifying this).
Interoperability is still a major challenge and extentensive research required.

## Slide 10: Source material used
MARKET OPPORTUNITIES IN THE SMART GRID SECTOR IN FINLAND 2016 , https://www.investinfinland.fi/documents/162753/197730/White+Paper+Smart+Grid/880e1f5b-a78f-4294-bfed-a8037cfa0a9c
Yasin Kablachi, 2016, “A Survey on Smart metering and smart grid communication”, Renewable and Sustainable Energy Reviews 57 (2016)302–318, available at http://dx.doi.org/10.1016/j.rser.2015.12.114
Ogbodo et al,2017, “Cognitive Radio Based Sensor Network in Smart Grid: Architectures, Applications and Communication Technologies”, IEEE Access, Vol 5 19084 - 19098 available at http://dx.doi.org/10.1109/ACCESS.2017.2749415
ENISA, “Communication network interdependencies in smart grids”, 2015 Available at https://www.enisa.europa.eu/publications/communication-network-interdependencies-in-smart-grids
Trends in Utility Smart Grid Communications Management, GTM Research White paper, 2013. Available online at: https://www.ericsson.com/assets/local/news/2013/9/trends-in-utility-smart-grid-communications-management.pdf
Nokia presentation,2016 available at https://www.itu.int/en/ITU-D/Regional-Presence/ArabStates/Documents/events/2018/RDF/Workshop%20Presentations/Session1/Nokia_5G_ITU%20Workshop%20Alger%2014%20Feb%202018%20NC.pdf