## Slide 1: ELEC-E8423 - Smart Grid 16. Demand response of industrial loads
Joel Unha
Miika Vanhanen
12.03.2019

## Slide 2: Introduction
Industrial sector has almost half of the
Finnish electricity consumption (85 TWh)
The largest industrial electricity consumers are partly integrated to demand response system but there is still unused potential
Forest industry has a lot of flexible loads already in balancing power markets and fast disturbance reserves
New potential demand response possibilities can still be identified for example in chemical industry
Chart: Share of total electricity consumption %
| Industry and construction | Households and agriculture | Services and public consumption | Transmission and distribution losses
Share % | 47.2 | 28.1 | 21.4 | 3.2

## Slide 3: Characteristics of industrial demand response
Industrial demand response can react to either electricity market price or frequency of electricity network
Participation in Fingrid’s demand response markets requires good adjustability, high power capacity and fast activation response
Two-way data transfer
Automation
Metering
Example of demand response capable
loads in a paper mill
Demand response information exchange and signal diagram

## Slide 4: Demand response market places
Market place | Type of contract | Minimum size | Activation time | Activating frequency
FCR-N | Yearly and hourly markets | 0,1 MW | 3 minutes | Several times a day
FCR-D | Yearly and hourly markets | 1 MW | Linearly of partly linearly within 5 s / 50 % and 30 s / 100 %, when f under 49,9 Hz OR single step activation 5 s when f under 49,7 Hz / 3 s when f under 49,6 Hz / 1 s when f under 49,5 Hz | Several time per day – per year
aFRR | Hourly market | 5 MW | Must begin within 30 s of the signal's reception, must be fully activated in 2 minutes | Several times a day
Balancing power market (mFRR) | Hourly market ​ | 5 MW​ ​ | 15 min​utes ​ | According to the bids, several times per day - per year
Balancing capacity market (mFRR) | Weekly actions ​ | 5 MW​ ​ | 15 min​utes ​ | According to the bids, several times per day - per year
Fast disturbance reserve (mFRR) | Long-term contract | 10 MW | 15 min​utes | About once a year
Day-ahead market | Hourly market | 0,1 MW | - | -
Intra-day market | Hourly market | 0,1 MW | - | -
Strategic reserves | Long-term contract ​ | 10 MW | 15 min​utes for DSR, 12 h for power plants | Rarely

## Slide 5: Demand response potential of industry
Industry sector | Peak load | Peak load of flexible loads
Paper industry | 3180 MW | 790 MW
Metal industry | 680 MW | 410 MW
Chemical industry | 510 MW | 359 MW
Other industries | 28 MW | 10 MW
Industry in total | 4370 MW | 1559 MW

## Slide 6: Benefits of industrial demand response
Industry has high demand response capacity  good for profitability and markets
Demand response decreases energy consumption
Peak load demand can be cut  electricity price goes down (expensive and high emission production decreases)
The stability of electricity networks is maintained more effectively
The key point  demand response must be profitable for participating industry companies

## Slide 7: Issues of industrial demand response
Industrial processes are integrated systems and thus changing electricity loads may cause harm for the total process
Shutting and restarting of process machinery may result in increased production costs and diminished quality or loss of products
Incentives for industry companies are needed
Motivating personnel to accept demand response might be challenging due to possible challenges in the process
A lot of further R&D and piloting is needed for more efficient demand response

## Slide 8: Conclusions
Potential of industrial demand response is high but it has not been fully utilized at the moment
Increasing of profitability and R&D is important
For every industry sector, possible DR loads must be identified separately (and possible issues must be considered)

## Slide 9: Source material used
Give the list of references used for the presentation preparation
https://www.sciencedirect.com/science/article/pii/S2210670713000632#fig0005
https://www.stat.fi/tup/suoluk/suoluk_energia_en.html
https://www.fingrid.fi/en/electricity-market/demand-side-management/market-places/
https://dspace.cc.tut.fi/dpub/bitstream/handle/123456789/25157/V%C3%A4%C3%A4n%C3%A4nen.pdf?sequence=3
https://www.vtt.fi/inf/julkaisut/muut/2005/PRO3_P3017_05.pdf
http://butler.cc.tut.fi/~repo/Opetus/Projektityot/Jesse_Ruotsalainen_Kysyntajousto_sahkomarkkinoilla.pdf
https://aaltodoc.aalto.fi/bitstream/handle/123456789/32435/master_Niemel%C3%A4_Antti_2018.pdf?sequence=1&isAllowed=y
https://www.ceer.eu/documents/104400/-/-/3244d854-f6ed-aeb6-9941-6ad22658e799
http://www.smartenergytransition.fi/tiedostot/murrosareena-polku2-sahkon-kysyntajousto.pdf