## Slide 1: ELEC-E8423 - Smart Grid Thermal heat storages for daily and seasonal use
Edwin Kowalczyk
Oscar Lindblom
02.04.2019

## Slide 2: Introduction
Intermittent character of RES creates danger to grid stability, thus part of energy produced has to be curtailed.
There are various ways of storage the surplus of the electricity generation, one of them are power-to-heat technologies.

## Slide 3: Introduction
The main idea of Thermal Energy Storage (TES) systems is to store thermal energy (heat or cold) in some form of medium.
Thermal energy storage involves the storage of heat in one of three forms;
- Sensible heat,
- Latent heat,
- Thermo-chemical heat storage.

## Slide 4: Daily storage technologies
Water tanks (hot and cold)
Well developed and commercial technology
Used in combination with wind and solar energy sources
Heat pump
Provide high coefficient of performance (COP)
Can feed both heating and cooling networks
Collect thermal energy from thermal sources, for example waste water, flue gases, or surplus heat

## Slide 5: Daily storage technologies
Molten Sands
Stored energy can be consumed as electrical
Andasol-3 storage has a capacity of 1 GWh
Storage capacity: 7,5 hours
Hot Tank Temperature about 400 °C
In the picture: Project Andasol-3 (Spain)

## Slide 6: Demand for long-term storage systems

## Slide 7: Seasonal storage technologies
Underground thermal storage:
      Boreholes
      Cavern storage
      Construction based technologies
Surface and above storage:
      Pit storage
      Large-scale thermal storage with water
      Earth-bermed buildings

## Slide 8: Seasonal storage technologies
HELEN rock cavern seasonal energy storage facility
Rock storage facility which would utilize sun-heated surface water
Total capacity of 300 000 m3 located 50 m underground
In summer it would collect warm seawater which would be used in the winter as a source for energy pumps
Heat pumps would additionally also use excess heat from buildings
Residential area to be completed by 2030, already starting this year

## Slide 9: Conclusions
TES is needed to fully integrate RES into the power system.
There is a demand for; daily, weekly and monthly (especially in cold locations) storage systems.
Seasonal storage is great for areas with proper seasons.
Energy is easy to store as heat.

## Slide 10: Source material used
Power-to-What? – Environmental assessment of energy storage systems https://pubs.rsc.org/en/content/articlelanding/2015/ee/c4ee03051f#!divAbstract
Average monthly hours sunshine, Helsinki, Finland
https://weather-and-climate.com/average-monthly-hours-Sunshine,Helsinki,Finland
Renewable energy production of Finnish heat pumps
https://www.vtt.fi/inf/pdf/technology/2014/T164.pdf
AndasolSolar PowerStation
https://en.wikipedia.org/wiki/Andasol_Solar_Power_Station
https://www.helen.fi/en/news/2018/Seasonal-energy-storage-facility-is-planned-for-the-Kruunuvuorenranta-rock-caverns/?fbclid=IwAR3MfIDn3SbL_9KOp9onHRAplPm_eQ0IeqgFqYMaa7Qo4jIJ4epKuk1GXxQ
http://www.lsta.lt/files/events/100602-03_EHP_Briuselis/Sesija%204/5_Dirk_Mangold.pdf?fbclid=IwAR0h083rGbyhFUxhTorvpJQmpFbZFY7CYn70nDdc3gYK_yiavuJeh0lv8FE