## Slide 1: ELEC-E8423 - Smart Grid Power markets in Nordic Countries: Day ahead market and intra-day balancing
Ahmad Elberry, Abdelghani Aljayyousi
05.03.2019

## Slide 2: Introduction
Scope of the presentation
Day ahead market explanation
Merit order curve
Grid balance
Transmission
The need of intra-day balancing market
The Intra-day market
key terms:
The whole sale price of electricity
Marginal cost of generation (€/MWh)
Transmission system operator
congestion

## Slide 3: Day ahead market- Elspot
It is the main arena for trading power. Where, contracts are made between seller and buyer for delivery of power the following day
A consumer evaluates its energy need and price for the following day, hour by hour
Generator decides its deliver energy capacity and cost rate hourly
Each order includes the exact electricity volume (MWh/h) at a specific price rate (€/MWh) for every hour in the next day that one is prepared to buy or sell
The whole sale price of electricity (selling price) equilibrium settles where the curves of supply and demand intersect.
Spot-trade is the day before delivery where, offers are given up to 12-36 hours before delivery. The trade for next day closes at noon.
whole sale price

## Slide 4: Merit order curve
Marginal cost
The cost to produce a unit of electric energy: fuel and variable O&M costs
Profit
Profit=o
whole sale price
Higher cost generators are not used and must wait when demand may get so high as to need them as well
Economic dispatch
The system operator (an operator that transmits electrical power from generators over the electrical grid) meets the forecasted demand by dispatching generators based on their selling price for electricity, with the lowest cost generators being dispatch first, followed by higher and higher cost generators
Notes: Condensing plants like Coal power plants

## Slide 5: Grid balance
As a result some condensing plants shutdown and the investors tend to invest less in such plants which will greatly affect the security of the grid which will be dominated by the intermittent and volatile renewable sources

## Slide 6: Transmission
There is a limit to how much power a transmission line can carry, and when that limit is reached, the line is said to be congested.
At these times, generation closer to the given load needs to be dispatched even if it is higher cost.
So transmission congestion forces system operators to dispatch generation not just for the entire grid, but also at areas within the grid in order to meet local demand that cannot be brought in from elsewhere.

## Slide 7: The need of intra-day balancing market
Because of the unplanned incidents like intermittency of wind and solar power , power plants’ technical problems
Why Has The Sun Suddenly ‘Turned Off’ ?!

## Slide 8: Intra-day market-Elbas
The generation scheduling and energy procurement starts at the previous day before the day of delivery. By noon of this day, the traders make bids of supply and demand, which are then summed into ascending and descending order of price, respectively. The point where these two summation curves intersect, defines the power price for all the deliveries at that specific hour. As a result of this trading is the fixed power price for each of the next day 24 hours, the Elspot price. Closer to the operation hour, the power balance can then be complemented by Elbas market. Here the prices are set based on pay-as-bid basis for all transactions. Hence, in this intraday market the prices vary continuously. The Elbas market closes one hour prior to the hour of delivery. Those imbalances which have not been settled by Elbas trade are then subjected to the prices in balancing power (regulation power) market of the TSO.
Physical market Power transactions |  | Specific operating Hour | Balancing in Real time
ELSPOT | ELBAS | REGULATION POWER MARKET | Primary Reserves 1s-3min
12-36 hr | 1-32 hr | 15 min – 1 hr | Real time
Day Ahead | Intra Day | Intra Hour | Secondary Reserves 15 min
Also bilateral transactions & Demand Response |  | Hourly Balance management & Demand Response | Releasing Primary Reserves

## Slide 9: Conclusions
The effect of the whole price of electricity on the grid balance
The need to enhance and increase the capacity of the interconnections between the northern countries to avoid congestions
The intraday market is becoming increasingly significant as the share of volatile wind and solar power is increasing in the energy mix,

## Slide 10: Source material used
Power Cut? How the EU Is Pulling the Plug on Electricity Markets by Carlo Stagnaro Chapters 1-6
https://www.e-education.psu.edu/ebf483/node/584
https://www.nordpoolgroup.com/the-power-market/Day-ahead-market/
https://www.nordpoolgroup.com/Market-data1/Intraday/Volumes/ALL/Hourly/?view=table
https://www.nordpoolgroup.com/Market-data1/#/nordic/map
https://www.fingrid.fi/en/grid/electricity-system-of-finland/transmission-management/

## Slide 11: Questions

## Slide 12
Thank you