## Slide 1: ELEC-E8423 - Smart Grid Compressed Air Energy Storage (CAES)
Joona Hulkkonen
Matias Österbacka
2.4.2019

## Slide 2: Introduction
Basic concept of CAES plant
Different types of processes for compression and discharge​
Potential as an energy storage method
Already existing C​AES plants
Conclusions

## Slide 3: Concept
Ambient air is compressed and stored to an accumulator and used to operate a combustion-turbine when energy is needed
Functions similar way as a conventional gas-turbine peak-load power plant
Very similar to a pumped-hydro plant in terms of applications, output and storage capacity
Compression process heats the air and expansion cools the air
Heat loss can be compensated by burning natural gas or storing and using the heat from compression
Underground aquifers, solution-mined salt caverns and mechanically formed reservoirs in rock formations are cheaper accumulators compared to the aboveground built accumulators
Another option is a vessel with flexible walls deep underwater and hydrostatic pressure pushes the air aboveground
(Wang et al. 2017)

## Slide 4: Different types of CAES systems
Diabatic
Heat is dissipated with intercoolers as waste into the atmosphere
42-55% efficiency
Adiabatic
Heat from the compression is stored and later used to heat the expanding air
Approximately 70% efficiency in practice
Isothermal
Air temperature is kept close to a constant during compression and expansion (e.g. slow compression and discharge)
Low power installation
Efficiency estimated to be around 70-80%
Chen et al. 2013
Rogers et al. 2014

## Slide 5: Potential Shares of energy storage technologies
Currently the by far biggest energy storage form is Pumped Hydro Storage.
It is reliable, has relatively low cost and can store energy for a long period of time.
Word’s energy storage capacity [MW]
IEA 2014

## Slide 6: Potential Power and discharge times of ES-technologies
CAES has the potential to store energy in a large scale like PHS.
PHS is becoming exhausted as an energy storage system due to the lack of favorable geographical sites. (Sternberg & Bardow, 2015)
Scientific focus has strongly shifted to CAES, especially to the development of AA-CAES (Sternberg & Bardow, 2015)
(Energy storage sense)

## Slide 7: Potential Cost range and potential locations
CAES costs are also in the same range as PHS.
Cost estimates differ a lot by source but are roughly 1000$/kW for diabatic and 1300$/kW for adiabatic CAES.
Possible salt caverns mostly in middle and southern Europe.
Potential salt caverns in Europe
Bykov, 2018
Wang et al. 2017

## Slide 8: Projects In operation
Location | Type | Power | Year | Accumulator
Huntorf, Germany | Diabatic | 290 MW, >2h | 1978 | Salt cavern
McIntosh, USA | Diabatic | 11 MW, >26h | 1991 | Salt cavern
Hokkaido, Japan | Diabatic | 2 MW | 2001 | Rock cavern
Toronta, Canada | Adiabatic | 0.7 MW | 2015 | Underwater balloons
Chen et al. 2016, Bykov 2018

## Slide 9: Conclusions
Compressed Air Energy Storage (CAES) is an energy storage method in which air is compressed into to a tank and released later spinning a turbine.
Lots of promise on Adiabatic CAES which does not require any external fuel.
Huge potential since it can store great amount of energy for a long period of time.

## Slide 10: Source material used
Wang, J. et al. 2017. Overview of Compressed Air Energy Storage and Technology Development. Energies. Vol.10:7. p. 1-22. doi: 10.3390/en10070991
Rogers, A. & Henderson, A. & Wang, X. and Negnevitsky, M. 2014. Compressed air energy storage: Thermodynamic and economic review. doi: 10.1109/PESGM.2014.6939098
Chen, H. & Zhang, X. & Liu, J. & Tan, C. 2013. Compressed Air Energy Storage, Energy Storage - Technologies and Applications. IntechOpen. ISBN: 978-953-51-0951-8.
D. Swider. 2007. Compressed Air Energy Storage in an Electricity System With Significant Wind Power Generation. IEEE Transactions on Energy Conversion. Vol. 22:1. p. 95-102. doi: 10.1109/TEC.2006.889547
Kouksou, T. & Bruel, P. & Jamil, A. 2014. Energy storage, applications and challenges. Solar Energy Materials and Solar Cells. Vol. 120. p. 61-63. ISSN 0927-0248. doi: 10.1016/j.solmat.2013.08.015
Sternberg & Bardow 2014. Power-to-What? – Environmental assessment of energy storage systems. Energy Environ. Sci., 2015, 8, 389. DOI: 10.1039/c4ee03051f
BINE Information Service, Compressed air energy storage power plants: http://www.bine.info/fileadmin/content/Publikationen/Englische_Infos/projekt_0507_engl_internetx.pdf
Energy storage association: http://energystorage.org/compressed-air-energy-storage-caes
Energy storage sense: http://energystoragesense.com/energy-storage-technologies/
IEA 2014: https://www.iea.org/tcep/energyintegration/energystorage/