## Slide 1: ELEC-E8423 - Smart Grid Solar farms, their local grids and connection to the power system
Tommi Asp
Aku Forsström
22.05.2019

## Slide 2: Introduction
Solar Farm: -Collection of solar panels on land in order to generate electricity to feed into the grid. -Nowadays PV efficiency is around 20%, and with Concentrated systems around 30%.
-Solar heat plants also considerable choice with 70-90% efficiency.
-Produced energy is highly depended on the geographical position
Areas of solar farms: 1,6*104 m2 1 MW crystalline solar panels without trackers
2,4*104 m2 1 MW thin film solar panels without trackers
“Solar farms, their local grids and connection to the power system”

## Slide 3: Installed capacity and energy market share
The growth has slowed down considerably in Europe since 2011 but growth in China, Asia-Pacific and North America are increasing the global cumulative capacity, so that total of 600 GWh is expected to be reached by 2018
“Solar farms, their local grids and connection to the power system”
Global Cumulative Solar PV Installation Capacity
Estimated total percentage of the total PV production per total electricity demand
Notes: 7.3 euroopan decrease

## Slide 4: PV in the broader energy transition
PV is growing as a renewable energy source but to fulfil the temperature limit goals set by the world community, larger yearly volumes of PV need to be deployed in the coming years while limiting fossil-based energy
PV technologies can also work as catalysts for other energy efficient/green technologies
One of these are the EVs as can be seen from the correlation curve
This can work also in vice verse and with correlation with other factors such as growing popularity of green technologies and energy efficient lifestyles

## Slide 5: Grid Connected PV System
Small and intermediate systems (<500 kW) are usually connected to the distribution system
Large systems (>500 kW) are connected to the transmission system
Inverter:
-Maximum power point tracking (MPPT)
-Initiative operation and stop
-Anti-islanding functions
-Active voltage regulation function
-DC detection function
Inverter starts operation initiatively, when the output power of solar module reach the inverter required power
Inverters choose a best point of maximum voltage and current to produce maximum power from the solar cell module.
“Solar farms, their local grids and connection to the power system”
Notes: Deviation detection triggers adjustment of inverter reactive power output

## Slide 6: Plant control system
Supervisory control and data acquisition (SCADA) System:
SCADA is widely used in solar farms as they need fast sampling pace for the data gathered to optimize the power output as efficiently as possible
SCADA is used to minimize the operation and maintenance costs of a power plant by triggering alarms when oddities are detected
Data is gathered from the inverters, panels and other components of the system to calculate and compare to the optimum performance
“Solar farms, their local grids and connection to the power system”
Notes: The system monitors PV plant performance by means of a mathematical model initialized at installation with plant design data: PV panels' peak power, inverter specifications, manufacturer-provided electric parameters, number of strings, strings length, etc. The model is continuously fed with local weather data, and it calculates in real time the correct energy production at 100% plant capacity. The automatic comparison between the calculated and the real production figures - supplied by the data logger - gives a precise measure of plant performance and plant health every minute or less.

## Slide 7: Control of grid connected PV plant
1. Feedback from system give possibility to real-time controlling with PID-controller and for maximizing energy there is Maximum Power Point Tacking (MPPT), which is DC-DC converter.
2. Plant set point is determined by operator, grid demand and output potential.
3. Converters convert electricity to grid as much as possible to maintain setpoint. If there is overproduction, inverters are commanded to limit their themselves.
“Solar farms, their local grids and connection to the power system”

## Slide 8: Effects of PV Grid connected systems on a Distribution network
Reverse power flow: Net Production > Net Demand.
Overvoltage along distribution feeder: Reverse power flow leads to overvoltage along distribution feeder.
Voltage control difficulty: Due multiply supply point
Power Losses: If plant is long distance from load.
Phase Unbalance: Most inverters in residential PV system are single phase.
EMI-issuses: Due the high frequency converters.
Increased reactive power in grid: In PV system, inverters are openly operating at unity power factor to maximize active power generation. This reduce active power supply by the utility. However, reactive power is still same, thus, distribution transformer operate at low power factor and it reduces overall system efficiency.
“Solar farms, their local grids and connection to the power system”

## Slide 9: Conclusion
Global solar installation capacity is increasing but the installation capacity is decreasing in Europe somewhat due to wind power providing to be more profitable solution. This also some times due to reduced financial aid for PV
Control system goal is produce as much as possible high quality electricity in to the grid. This is maintain by measurement system, PID-controller, voltage control, and active power control.
PV facilities are the most reliable as large advanced controlled power plants, with battery systems. However, also straight grid connected system provide reliable solution, with lower efficiency rate.
“Solar farms, their local grids and connection to the power system”

## Slide 10: Source material used
Solar Power Europe, “Global Market Outlook for Solar Power 2017-2021”, Africa-EU Renewable Energy Cooperation Program(RECP),Available on: www.solarpowereurope.org
Dave jones, Dr.Alice sakhel,Matthias Buck and Dr.Patrick Graichen.2018. “ The European Power Sector in 2017”, Available on: www.sandbag.org.uk
Solar Inverter, Available on: www.solar.inverter.co
Danielle Silva, “SCADA Patterns & Best Practices for Utility Scale Solar PV – Power Plant Control”.
Ranon Satitpanyapan,” SCADA and Monitoring for Solar Energy Plant”, Bangkok,Thailand.
Davud Mostofa Tobnaghi.2016.” A Review on Impacts of Grid-Connected PV system on Distribution Network”
https://news.energysage.com/solar-farms-start-one/
http://www.suncyclopedia.com/en/area-required-for-solar-pv-power-plants/
IEA, “Snapshot of global photovoltaic markets 2019”, Available on: http://www.iea-pvps.org
“Solar farms, their local grids and connection to the power system”