## Slide 1: ELEC-E8423 - Smart Grid Demand response of EV loads
Paavo Hietanen,
Atte Hintikka
07.02.2018

## Slide 2: Introduction
Motivation
Fleet size expected to grow rapidly
  Currently in Finland: 15 499
  Goal for 2030: 250 000
  Globally 2030: 125 million
Large fleet might have a negative impact on economy and grid resiliency
  Uncontrolled charging may cause system load peaks -> degradation of power quality
  Extra demand charge could need to be utilized for load spikes in commercial charging areas
Collective charging could be approached by offering drivers a chance to buy their supply in day-ahead bidding
  Demand Response

## Slide 3: Technologies for EV demand response
Vehicle to Grid (V2G) technology
Different technology applications that utilize two-way chargers for EVs, allowing them to discharge their battery’s electricity back to grid
Strengths:
  Using EVs as distributed energy storages, enabling smoothing down of demand spikes
  Compensation to drivers when they sell unneeded electricity
  When drivers are able to sell their battery capacity beforehand, day-ahead markets can accompany surplus to calculations
Weaknesses/Difficulties:
  Extra stress on battery, reduced lifetime
  Requires centralized, smart control systems

## Slide 4: Technologies for EV demand response
(Aggregate) Virtual Battery
A virtual model of the whole EV fleet could be constructed which would allow day-ahead forecasting of total charging and day-ahead prices needs
Strengths:
  Controlling EV charging times with smart scheduled charging systems when the markets are optimal for the drivers
  Avoidance of load volatility
  Support for additional services, like V2G technologies
Weaknesses/Difficulties:
  Individual charging times are stochastic: Very difficult to forecast
  Computationally expensive to schedule charging and calculate capacity for each individual EV and the whole fleet at the same time

## Slide 5: Technologies for EV demand response
Home Energy Management Systems (HEMS)
Energy management systems that handle the energy consumption of various house-appliances in individual homes
Strengths:
  Similar price optimization capabilities as with the virtual batteries
  Support for various other house appliances that the driver may have
  Real-time control and signalling
Weaknesses/Difficulties:
  Usually centrally controlled by retail electricity providers (REPs) - are people willing to be “managed” from outside?
  Requires lot of bidirectional ICT connections between households, their appliances and REPs - information security issues?

## Slide 6: The market potential
High peak-valley gap is necessary
Large number of EVs can create a new System Peak period
Electric passenger cars and commercial EVs could be the main DR contributors
Smart charging could provide a higher value for grid than peak shaving
Photo: [7]

## Slide 7: Example
Honda offers demand response charging program to EV drivers in Southern California
Drivers can receive push notifications to remind them to plug in
Possible to earn 50$ per 2-month period
Plus a 50$ Sign-up fee
Not V2G, only smart charging

## Slide 8: Conclusions
Large fleet of EVs can cause challenges
It is important to get the EV owners to participate in the markets
Smart charging seems to be the most attractive option

## Slide 9: Source material used
[1] Teknologiateollisuus: Sähköinen liikenne tilannekatsaus, Q4 2018, On their website, Available: https://emobility.teknologiateollisuus.fi/sites/emobility/files/file_attachments/sahkoinen_liikenne_tilannekatsaus_2018_q4_20190214_jaettava.pdf
[2] IAEA: Global EV Outlook, On their website, 2018, Available: https://www.iea.org/gevo2018/
[3] Yingqi Xiong, Bin Wang, Chi-cheng Chu, Rajit Gadh: Vehicle grid integration for demand response with mixture user model and decentralized optimization. 2018. Available: https://www-sciencedirect-com.libproxy.aalto.fi/science/article/pii/S0306261918314508
[4] Hongcai Zhang, Zechun Hu, Zhiwei Xu, Yonghua Song: Evaluation of Achievable Vehicle-to-Grid Capacity Using Aggregate PEV Model. 2017. Available: https://ieeexplore-ieee-org.libproxy.aalto.fi/document/7463483
[5] Kotub Uddin, Tim Jackson, Widanalage D. Widanage, Gael Chouchelamane, Paul A. Jennings, James Marco: On the possibility of extending the lifetime of lithium-ion batteries through optimal V2G facilitated by an integrated vehicle and smart-grid system. 2017. Available: https://doi.org/10.1016/j.energy.2017.04.116
[6] Mohammad Ali Fotouhi Ghazvini, Gianluca Lipari, Marco Pau, Ferdinanda Ponci, Antonello Monti, João Soares, Rui Castro, Zita Vale: Congestion management in active distribution networks through demand response implementation. 2019. Available: https://doi.org/10.1016/j.segan.2018.100185
[7] Liu Jiang, Zhao Yongqiang, Kim Hyoungmi, The potential and economics of EV smart charging: A case study in Shanghai, Energy Policy, Available at: https://doi.org/10.1016/j.enpol.2018.04.037
[8] Utility Dive, Honda offers demand response charging program to EV drivers, 2018, Online magazine, Available at: https://www.utilitydive.com/news/honda-offers-demand-response-charging-program-to-ev-drivers/529045/