## Slide 1: ELEC-E8423 - Smart Grid Pumped hydro energy storages
Tomi Töyräs
Topias Zein
09.04.2019

## Slide 2: Introduction
Mechanical energy storage
Based on the gravitational
potential energy of water
Capacity:
185 GW installed
About 95 % of all storages
China has the most power capacity

## Slide 3: Applications
Energy balancing
helps to balance the power system  can be used when the renewable production is low
Load leveling
can be loaded in night hours  balance the load peaks
Large emergency reserve

## Slide 4: Pumped storage plant on surface
The most common in use
Discharge time: from hours to a few days
and response time: seconds to minutes
Plant sizes are between 100 – 3000 MW
Efficiency is 70 – 85 %

## Slide 5: Bath County Pumped Storage Station
Largest pumped storage plant in the world since 1985
In Virginia, United States
Storage capacity: 31 GWh
Rated power: 3 GW
Construction cost: US$1.6 billion

## Slide 6: Underwater reservoirs
Usage of pressure at the sea bottom
Power need  water is let in
Electricity production surplus  water pumped out
Used in conjunction with other renewables (e.g. offshore wind)
Sphere diameter ~ 25 m
Depth of 200 to 700 m

## Slide 7: Underground reservoirs
One or both reservoirs underground
Usable in flat regions
Usage of old mines such as coal
Can be cheaper than on surface pumped storage
Planned to be used in Pyhäjärvi metal mine

## Slide 8: Conclusions
+Advantages
Reliable technology
Long lifetime
Energy balancing
Emergency  large reserve
-Disadvantages
Needs specific location
Vast area
Issues with environment
High investment costs

## Slide 9: References
400 MW pumped storage hydro plan approved. Civil engineer [online]. Webvision, 2017 [cit. 04.04.2019]. Link: https://www.newcivilengineer.com/latest/400mw-pumped-storage-hydro-plan-approved/10015321.article
Pumped hydro storage plants with improved operational flexibility using constant speed Francis runners DOI: 10.1016/j.apenergy.2014.09.065.
Energy and Innovation Awards. Energy week [online]. Vaasa: EnergyVaasa, 2018 [cit. 04.04.2019]. Link: https://www.energyweek.fi/awards/
Electrical Energy Storage: IEC. Geneva, 2011. Link: http://www.iec.ch/whitepaper/pdf/iecWP-energystorage-LR-en.pdf
Sub-surface pumped hydro storage. Energy storage association [online]. 2018 [cit. 06.04.2019]. Link: http://energystorage.org/energy-storage/technologies/sub-surface-pumped-hydroelectric-storage
Locating Power Plants. Virgninia Places [online]. [cit. 03.04.2019] Link: http://www.virginiaplaces.org/ggs380/11powerplants.html
Data visualization. DOE Global energy database [online]. Sandia Corporation, 2018 [cit. 06.04.2019]. Link: https://www.energystorageexchange.org/projects/data_visualization
Ocean Renewable Energy Storage (ORES), DOI: 10.1109/JPROC.2013.2242411.
U.S. Grid Energy storage factsheet. Center for sustainable system [online]. Michigan, 2017 [cit. 08.04.2019]. Link: http://css.umich.edu/factsheets/us-grid-energy-storage-factsheet
Bath county pumped storage station. Dominion Energy [online]. Dominion Energy, 2018 [cit. 08.04.2019]. Link: https://www.dominionenergy.com/about-us/making-energy/renewables/water/bath-county-pumped-storage-station