## Slide 1: ELEC-E8423 - Smart Grid Prosumer / Consumers. Local energy resources and energy matching
Niko Korpela & Aaro Vaitomaa
26.03.2019

## Slide 2: Introduction
“A prosumer is a person who consumes and produces a product”
Local energy resources:
”energy produced at the site of consumption”
  Wind power
  Solar power
  Heat generation (Geothermal heat, fireplaces, biomass boilers)
Energy matching
  “maximizing RES production in built environment”
  Load management (balancing electricity supply by managing loads)
  Energy storages (time difference between production and demand peaks)
Notes: Let's begin by defining the term prosumer, just in case
On the local resources, we have focused mainly on electricity production, so heat is mentioned, but not went trough in detail
Then we talk about energy matching, why it's useful and how can it be done

## Slide 3: Local energy resources
Wind production
  Typical power output 400W-20kW depending on the size and conditions
Solar production
  Typical panel size around 3-10kW
  Total output depends on roof area, roof pitch etc.
Potential depends heavily on the geographical location
Notes: Local energy resources for example individual residential houses, like detached houses
Apart from geographical location, both of them depend heavily on environmental circumstances and also seasons

## Slide 4: Why energy matching is reasonable?
Selling back to grid is not very profitable
  Selling price<<buying price
  Transmission fees and taxes left for producer
  However, production cost per kWh decreases with higher capacity
Matching times of production and consumption
  Load side management
  Storages

## Slide 5: Load Side Management
Demand response by controlling loads
Critical loads excluded from the system
Air conditioning, clothes dryer, electric vehicles etc. offer largest potential
Load side management is not feasible without smart technology (IoT)
Different smart home solutions are already in the markets

## Slide 6: Load Side Management
https://electrical-engineering-portal.com/smart-load-management-strategies-to-save-energy

## Slide 7: Storages
Large scale batteries
Li-ion: Tesla Powerwall 14 kWh at pricepoint of 7300 €
Redox Flow Batteries 6,3 kWh at pricepoint of 6000 €
Electric vehicles
Contain 30-90 kWh batteries
Could be used for charging as well as discharging
Goal: Reduce peak demand and provide flexibility
Could reduce demand up to 8-32%, depending on the operation algorithm
Electricity consumption rises marginally due to losses
Do not yet provide true independance from the grid
Battery sizes low / too expensive to scale
Useful tool on local electricity matching
Notes: There are different ways to store electricity locally by individual consumers, two of the most feasible are: large batteries and also electric vehicles
Depending on the complexity of the operation algorithm of STORAGE --> Batteries possess a real value on smoothing out demand
These results are from a case, where the household had implemented solar panels as well!
Storage is in one way the electricity consumer, when it's not in use
Rise of consumption corresponds to more electricity based system emissions etc

## Slide 8: Implementation of smart technology
Notes: Taking into account all of the previously mentioned solutions, implementation could look something like this, in order to fully achieve the edvantages of local energy resources as well as energy matching.
So we have local resources, storage and grid, all connected to the consumer through an intelligent optimized system. Imported electricity from the grid also uses load management to fully optimize the entire system.

## Slide 9: Conclusions
Local electricity resources consists of wind and solar
Selling electricity back to grid is not a good business case
Energy matching increases stability and profitability of the system
Energy matching can be done
  By load side management
  With energy storages

## Slide 10: Sources
Wang, Caisheng, and M. Hashem Nehrir. "Power management of a stand-alone wind/photovoltaic/fuel cell energy system." IEEE transactions on energy conversion 23.3 (2008): 957-967.
Kelleher, J., and J. V. Ringwood. "A computational tool for evaluating the economics of solar and wind microgeneration of electricity." Energy 34.4 (2009): 401-409.
Pipattanasomporn, M., Kuzlu, M., Rahman, S. "An Algorithm for Intelligent Home Energy Management and Demand Response Analysis", IEEE Transactions on Smart Grid ( Volume: 3, Issue: 4, Dec. 2012 )
https://www.motiva.fi/ratkaisut/uusiutuva_energia/tuulivoima/pientuulivoima
http://www.arevasolar.fi/fi/aurinkopaneelit-omakotitaloon
https://www.tesla.com/fi_FI/powerwall
Hittinger, Eric. "Distributed generation: Residential storage comes at a cost." Nature Energy 2.2 (2017): 17006.
Fortum SmartLiving, http://lampopilotti.fi/
https://www.energy.gov/energysaver/installing-and-maintaining-small-wind-electric-system
http://www.springer.com/978-3-319-14882-3
https://electrical-engineering-portal.com/smart-load-management-strategies-to-save-energy
Brahman et Al. “Optimal electrical and thermal energy management of a residential energy hub, integrating demand response and energy storage system”. Energy and Buildings 90 (2015) 65–75
https://www.greentechmedia.com/articles/read/another-flow-battery-maker-tries-residential-in-germany