## Slide 1: ELEC-E8423 - Smart Grid Monitoring and control of secondary substations
Pauli Partinen
Mikael Aikio
16.04.2019

## Slide 2: Introduction
Reliability
Fault detection
Transformer condition monitoring
Power quality
Energy flow analysis
Voltage profile
Remote control
Increasing amount of renwable microgeneration will change the analysis of distribution network.
Distribution system is changing from a static to a dynamic system. Fast topology changes are mandatory for balancing the power system.
This can be achieved with large amount of remote controllability of the network.
Precise monitoring of network and fast fault detection is mandatory for minimizing the outages.

## Slide 3: Current situation
Massive amount of secondary substations in Finland. Most of
them are manually operated.
For example in Caruna network there is no real-time substation
monitoring. Real-time load values are calculated with summing
the node loads behind the transformer.
Only small part of secondary substations are equipped with
remote controlled switches. In these substations there is
possibility to add substation monitoring sensors because they
are equipped with Remote Terminal Unit (RTU).
Node 1 load
Node 2 load
Node 3 load
Total load of transformer

## Slide 4: Monitoring
Development began in 2002 by Vamp Ltd
Measured all LV side quantities
Calculated loading of the transformer and registered the abnormalities in power quality
Pilot project was carried out by Helen Sähköverkot Oy in 2008
Today there are many options for monitoring
HISTORY
Data aquired by SCADA:
Power quality
Currents
Switch status
Device condition (e.g. gas pressure & temperature)
Fault detection
SCADA = Supervisory Control And Data Acquisition

## Slide 5: Control
SCADA
Data acquisition
Data communication
Information or data presentation
Monitoring and control
Control is established via SCADA system.
SCADA system's databases and software programs offer a human machine
interface (HMI) to provide schematics, trending, diagnostic data and so on.
A Distribution Management System (DMS) is fed by SCADA and corporate archives with dynamic data.
DMS acts as a decision support system to assist the control room and field operating personnel with the monitoring and control of the electric distribution system.
The different SCADA and DMS solutions adopted have direct impact on:
Network representation
Devices configuration
Network management
Network operation

## Slide 6: Available solutions
Netcontrol
Netcon 100
Monitor & Control Unit
Arteche
adaTECH FRM
RTU
Netcontrol
NMS 100
Monitor & Control Unit
ABB
Prefabricated substations for SG applications

## Slide 7: Conclusions
Real-time time control of distribution network enables optimal power flow in all situations
Monitoring will improve reliability and power quality
Very large investments for distribution network are mandatory in future

## Slide 8: Source material used
https://www.researchgate.net/publication/224593600_A_comprehensive_secondary_substation_monitoring_system/download
http://www.cired.net/cired-working-groups/smart-secondary-substations
https://www.netcontrol.com/eng/products/substation-automation/secondary-substation-systems/netcon-100/
https://www.netcontrol.com/eng/products/substation-automation/secondary-substation-systems/nms-100/
https://www.arteche.com/en/products/secondary-substation-monitoring-rtu
https://new.abb.com/medium-voltage/modular-systems/compact-secondary-substations/css-applications/css-for-smart-grids