## Slide 1: ELEC-E8423 - Smart Grid Different market mechanisms for smart grid: bidding, real-time pricing, localized markets
Taneli Leiskamo Antti Hyttinen
12.3.2019

## Slide 2: Introduction: What is a smart grid market?
“Smart grid” is a combination of physical infrastructure (=hardware) and markets that control the usage of those resources intelligently (=software).
“Smart grid market” = Integration of existing markets, resources and new resources together. Designs:
- Option 1: Current markets + Co-existing market (TSO and DSO)
- Option 2: Current markets + Coordinated local markets (TSO-DSO platform or ISO)
- Option 3: Current markets + Peer-to-peer markets (Blockchain?)
A key feature of any smart market design is balancing with demand response. We look into:
- Incentive Based Programs (e.g Demand bidding)
- Price Based Programs (e.g Real Time Pricing)
Also using locational information for demand response is assessed
Notes: Market architectures in general are regulated or liberalized to some extent.
New “smart” elements:
Flexibility service provider
  Aggregation for BRP
  Independant aggregation
Localized bidding
Offer payments to customer to reduce their load
during system need or stress
Offer time-based rates of electricity directly to end users
to promote customer demand response

## Slide 3: Demand Bidding (Buyback) 1/2
General
One alternative for an incentive based demand response program
Customers bid flexibility on the whole-sale market
  → reduction of electrical load during a specific time
Bid price lower than the market price → accepted
mainly large customers (e.g. 1 MW and over)
If unable to follow curtailment → penalty payments
Special type of demand bidding in Emergency DR program
  voluntary, no penalty payments
Notes: Customers sell their flexibility on the whole sale market
If the bid is accepted, the customer is obliged to meet the reduction of power consumption
If not able to follow through  penalty payments
However, there is a special type of demand bidding

## Slide 4: Demand Bidding 2/2
BENEFITS | CHALLENGES
For Demand Response in general | 
Added income/bill savings for customers More choices for customers Overall lower market-price System reliability Avoided investments | Efficient market environment Optimal utilizarion – forecasting the resource Lack of experience
For Demand Bidding | 
Passive DR (price based) can create uncertainty → forecasting demand Demand bidding (active method) reduces this uncertainty | Privacy issues Concerns about load profiles and identities of bidders New bidding platforms are studied → e-g no third party needed for handling bids.

## Slide 5: Real-time pricing (RTP) 1/2
General
One alternative for price based demand response program
Historically, pricing of electricity has undergone many changes
  Flat tariffs, IBR, Time-Of-Use (night & day tariffs)
In RTP the price is determined according to the actual cost of electricity in the wholesale market.
Customers are informed day ahead or rolling basis
More real-time knowledge of prices → sophisticated decisions on consumption!
Notes: Reflects the actual situation of the market & power system
Customers/Consumers are motivated to decrease their electricity consumption during peak hours due to higher electricity price. This evens out daily variations of consumption.

## Slide 6: Real-time pricing (RTP) 2/2
BENEFITS | CHALLENGES
considered effective & direct DR program Consumer is able to save on electricity bill by adjusting consumption Awareness of the situation of the market & grid Total energy consumption may decrease | Somewhat harder to predict since big behavioural aspect Currently only a small portion of the benefit is returned to the consumer → smaller behavioural changes Metering system & transaction costs
Notes: Challenges:
Harder to predict -> causes uncertainty which already discussed in previous slide
Engaging is a large benefit for the system as a whole, but only small portion in actual savings for the customer  is the customer instead willing to pay the few extra bucks to use electricity however he/she desires.

## Slide 7: Localized markets 1/2
Basics: Why locational information and markets are needed?
  Energy transition and economic growth call for an electricity grid with more capacity, sometimes more quickly than infrastructure can be built or the added capacity is not economically optimal. → Use flexibility.
  In Finland there is currently little congestion in TSO grid or DSO grids
    Currently system operators can have direct control, bilateral contracts with individual parties or mFFR bids can have a rough locational tag
Locational (real time) info for smart grid markets is needed for:
  Aggregation and independent aggregation
  Congestion solutions
  Other ancillary services
“How to coordinate?”
Notes: The cost of grid stabilisation measures in Germany reached a €1.4bn last year (2017), a record high, according to the country’s regulator BNetzA. Total redispatch volume reached 20,439 gigawatt-hours in 2017, the agency added. This included about 10,200GWh of curtailment and some 10,238GWh of additional ordered capacity.

## Slide 8: Localized markets 2/2
Open questions:
  Order: “First fix congestion then balance?”
  Costs: “What about BRPs?” “What is the business model?”
  Market integration: “How incorporate smart markets to the current ones?”
  System operation: “Who has market responsibility?”
Clean energy package (draft):
  “services provided by storage facilities to the grid operators can be seen as alternatives to grid extension, and this should be reflected in the investment analysis.”
Example markets / development projects regarding DSO and DSO-TSO balancing markets are: INTER(R)FACE, GOPACS, NODES, ENERO

## Slide 9: Conclusions
Demand bidding increases electricity market efficiency and lowers the uncertainty caused by DR. However, one major issue is the lack of sufficient privacy.
Real-time pricing aims to decrease the peak demands through real-time electricity price changes, and consumers may save on their electricity bill. However, includes higher transaction & metering costs and higher uncertainty.
Localized markets utilizing flexibility are at the core of smart grids, but concepts are not yet fully mature
THANK YOU!

## Slide 10: List of references
Aalami, H.A. & Khatibzadeh, A. 2016. Regulation of market clearing price based on nonlinear models of demand bidding and emergency demand response programs. International Transactions on Electrical Energy Systems. Vol. 26(11). pp. 2463-2478. Cited 10.3.2019
Aalto university, 2019. John Millar. Course material: ELEC-E8406 Electricity distribution and Markets.
Albadi, M. H. & El-Saadany, E., 2008. A summary of demand response in electricity markets. Electric Power System Research, Vol. 78(11), pp. 1989-1996. Cited 10.3.2019
Chen, C. et al. 2011. An innovative RTP-based residential power scheduling scheme for smart grids. 2011. IEEE International Conference on Acoustics, Speech and Signal Processing. Prague. Cited 10.3.2019
Elering. INTER(R)FACE. [Online source]. Accessed 10.3.2018. Available:https://elering.ee/en/working-group-led-elering-receives-eu-horizon2020-funding-creating-unique-platform-electricity
Fingrid. Balancing markets. [Online source]. Accessed 10.3.2018. Available:https://www.fingrid.fi/sahkomarkkinat/sahkomarkkinoiden-tulevaisuus/askelmerkit-sahkomarkkinamurrokseen/pohjoismainen-tasehallinta-ja-uudet-pohjoismaiset-markkinapaikat/
Helen. Tehomaksu. [Online source]. Accessed 10.3.2018. Available:https://www.helensahkoverkko.fi/uutiset/2017/siirtohinnat-muuttuvat/#miten-tehomaksu-maaraytyy
Steriotis, K. et al. 2018. A novel behavioral real time pricing scheme for the active energy consumers’ participation in emerging flexibility markets. Sustainable Energy, Grids and Networks. Vol. 16. pp. 14-27. Cited 10.3.2019
Uludag, S. et al. 2015. Privacy-Guaranteeing Bidding in Smart Grid Demand Response Programs. 2015 IEEE Globecom Workshops. San Diego. Cited 10.3.2019
US Department of Energy. 2006. Benefits for Demand Response in Electricity Markets and Recommendations for Achieving Them. Cited 10.3.2019
USEF. Flexibility. [Online source]. Accessed 10.3.2018. Available:https://www.usef.energy/flexibility/