## Slide 1: ELEC-E8423 - Smart Grid Demand response in power system energy balance management
Teemu Manner
20.02.2019

## Slide 2: Introduction
Increasing share of intermittent renewable energy sources, such as wind and solar, has elevated the discussion around the potential of demand response.
This presentation aims to provide an overview of energy balancing management and discusses the role and potential of demand response in the power system

## Slide 3: Power balance
The balance between production and consumption is indicated by the frequency of the electricity grid which has a nominal value of 50.0 Hz
If production is higher than consumption, frequency increases
If consumption is higher than production, frequency decreases
Frequency variation requirements:
  In Finland, the nominal value of the frequency is 50 Hz, and the permitted range of the frequency is from 49.9 to 50.1 Hz.
  Requirements for the 10 s average frequency
    49,5 Hz – 50.5 Hz ; 99,5 % of the year
    47 Hz – 52 Hz ; 100 % of the year
  Defined in standard: SFS-EN 50160

## Slide 4: Variable renewable energy
Conventionally, the power balance has been sustained by adjusting the generation according to the demand
The share of renewable energy production has increased substantially in power systems and it is expected to keep increasing in the future
As the amount of inflexible renewable energy production increases in the grid, managing the demand becomes more important than before

## Slide 5: Reserves
Production and consumption are planned in advance by Fingrid and other market operators, but in practice there are deviations during each hour
To balance these deviations, Fingrid utilizes different kinds of reserves from reserve markets
Reserves are power plants and consumption resources which either increase or decrease their electric power according to the need of the power system

## Slide 6: Reserve markets

## Slide 7: Aggregators
Aggregators are relatively new actors in the electricity markets offering demand response in a new way. The main idea of aggregators is to bundle small-scale consumers and producers into larger units that can participate in the reserve markets

## Slide 8: Conclusions
The balance between production and consumption is indicated by the frequency of the electricity grid which has a nominal value of 50.0 Hz.
As the amount of inflexible renewable energy production increases in the grid, managing the demand becomes more important than before
To balance the deviations of production and consumption, Fingrid utilizes different kinds of reserves from reserve markets

## Slide 9: Source material used
https://energia.fi/files/881/Sahkontoimituksen_laatu_ja_toimitustapavirheen_sovellusohje_2014.pdf
https://www.fingrid.fi/en/electricity-market/demand-side-management/
http://energylive.aemo.com.au/Energy-Explained/Managing-frequency-in-the-power-system
https://brandondonnelly.com/2015/05/01/tesla-introduces-a-battery-for-your-home/
http://julkaisut.valtioneuvosto.fi/bitstream/handle/10024/161148/TEM_33_2018.pdf