## Slide 1: ELEC-E8423 - Smart Grid Fuel Cells as a Part of a Power System
Arber Haxhiu
02.04.2019

## Slide 2: Content of the Presentation
Introduction to fuel cells and hydrogen economy
Fuel cell applications in a power system
Main challenges in adoption of fuel cells
A potential global fuel cell hydrogen concept
Conclusions

## Slide 3: Fuel Cells Produce Green Energy from Hydrogen
Zero-Emission
High Efficiency
(>70% for CHP)
Reduced maintenance need
Low Noise
Figure from ABB Marine and Ports, Accessed 25.03.2019, Online: https://new.abb.com/marine/systems-and-solutions/power-generation-and-distribution/fuel-cell

## Slide 4: The Goal is to Produce Hydrogen from Renewables
Electrolysis from Renewables
Steam Reforming from natural gas
Figure from http://www.entura.com.au/rethinking-the-role-of-hydropower-in-australia/
Figure from http://www.digipac.ca/chemical/mtom/contents/chapter4/steamreform.htm

## Slide 5: Hydrogen and Fuel Cells Applications in a Smart Grid
Figures obtained from https://www.plugpower.com/wp-content/uploads/2015/05/Intelec2011_ReliOn_P081_IEEE.pdf
Reduce local GHG emissions
Peak load shaving
Back-up power
Storage for renewable energy
Frequency and voltage regulation
Building heating with fuel cell exhaust heat

## Slide 6: Hydrogen Storage One of the Main Challenges
300 – 700 bar
Energy Density
  ~1.2 kWh/kg (700bar)
  ~1250 kWh/m3 (700bar)
Compressed gas
Liquified
- 253℃ (atm)
0.3 - 3% boil-off per day
Energy density
  27.8 kWh/kg
  2200 kWh/m3
Figures obtained from https://www.energy.gov/eere/fuelcells/hydrogen-storage and http://www.mahytec.com/wp-content/uploads/2018/07/CL-DS3-Data-Sheet_MHT-Magnum-060318.pdf
In carrier
E.g. metal hydrides, Methanol, ammonia, etc…
Emissions e.g. COX or NOx
A reformer needed
Energy density (e.g. Methanol)
  3.9 kWh/kg
  5500 kWh/m3

## Slide 7: Hydrogen Has a Poor Volumetric Energy Density
30
20
10
kWh
gravimetric energy density
(kWh / kg)
Volumetric energy density
(kWh / dm3)
33.3
0.6
Gaseous Hydrogen (300 Bar)
Liquid Hydrogen (-253℃)
33.3
2.4
Liquid Natural Gas
13.5
5.8
Diesel
11.8
10.0
11.6
Heavy fuel oil
11.4
Methane
13.9
10.0
Methanol
5.5
4.4
5.2
Ammonia
3.9

## Slide 8: A Potential Future Hydrogen Concept
Figure obtained from https://meetingoftheminds.org/session/the-hydrogen-economy-future

## Slide 9: Conclusions
Hydrogen fuel cells offer significant potential in decarbonization of local power production
At the moment, main challenges lie in the high price of both hydrogen and fuel cells
Hydrogen and fuel cell technology is rapidly evolving, mainly boosted by subsidies
Tighter regulation is still needed to further advance fuel cell technology

## Slide 10: Source material
[1] R. O’Hayre, S. Cha, W. Colella and F. Prinz, Fuel Cell Fundamentals, 1st ed., Hoboken, John Wiley & Sons Inc., 2016.
[2] P. Rohith, J. Priolkar and G. Kunkolienkar “Hydrogen: An Innovative and Alternative Energy for the Future”, IEEE Sponsored World Conference on Futuristic Trends in Research and Innovation for Social Welfare, 2016, pp. 1 – 5.
[3] J. Blanchard, “Smart Energy Solutions Using Fuel Cells”, IEEE 33rd International Telecommunications Energy Conference (INTELEC), 2011, pp. 1 – 8.
[4] G. Soloveichik, “Regenerative Fuel Cells for Energy Storage”, Proceedings of the IEEE, 2014, p. 964 – 975.
[5] U. Bossel, “Does a Hydrogen Economy Make Sense?”, Proceedings of the IEEE, 2006, p. 1826 – 1837.
[6] J. Larminie and A. Dicks, Fuel cell systems explained, 2nd ed., Chichester: John Wiley & Sons Ltd., 2003.
[7] “Fuel Cells and Hydrogen for Green Energy in European Cities and Regions”, An online source, Accessed 30.03.2019: https://www.fch.europa.eu/sites/default/files/181123_FCHJU_Regions_Cities_Final_Report_FINAL.pdf