## Slide 1: ELEC-E8423 - Smart Grid Electric vehicles and their charging systems
Sami Herranen
Markus Kopiloff
24.04.2018

## Slide 2: Introduction
Finland’s target is to cut the traffic emissions by 50% by 2030
Today 7000 EVs in Finland
Target is to have 250 000 EVs in 2030
Domestic charging stations
1 500 000 car heating poles which could be utilized for EV charging
Dedicated charging station needed for long term usage
Public charging stations
Today 300 in Finland
Target is to have 25 000 in 2030
Public charging station network is intended to grow on a market-based basis by energy companies and other commercial actors
Construction is to be supported with subsidies
Sources: [1]

## Slide 3: Charging modes
Modes | Usage | Power (max) | Voltage | Charger
Mode 1 | Light vehicles | 2 (3,5) kW | AC, 1-ph | Uncontrolled, normal cable
Mode 2 | Slow charging | 7 (11) kW | AC, 1 or 3-ph | Cable with control unit
Mode 3 | Basic charging | 22 (43) kW | AC, 3-ph | Dedicated EV charger socket
Mode 4 | Quick charging | 50 (350) kW | DC | Special power charger
Charging control abilities:
Modes 1 and 2 uses normal household sockets and plugs for grid connection  no data pins
Modes 3 and 4 uses EV dedicated multi-pin sockets for communication between car and grid
1
2
3
4
Control unit
Sources: [2]

## Slide 4: Charging systems
Mode 1 to be used only for LEVs, not for EVs
Mode 2 meant only for temporarily usage as mode 3 is preferred choice
Public charging stations shall have smart charging abilities  mode 3 or 4
Standardized plugs and sockets for public chargers in Europe:
Basic and slow charging (AC) – Type 2
Quick charging (DC) – CSS Combo
Other types also exists e.g. US, Japanese and Chinese
Also wireless charging for EVs is under development
Induction charging pads for stationary charging
Induction charging roadways for charging-on-to-move
Schuko plug
Control unit
Sources: [1], [2]

## Slide 5: Charging of electric vehicle
Battery management systems (BMS) controls the charging operation
State of charge (SoC) and needed charging current
Operation shall be stopped if communication is lost
AC-DC conversion is done with on-board charger
Charging time depends from:
Charging power
Battery capacity and SoC
Temperature
Overall efficiency:
Ca. 78…88 % for Grid-to-Vehicle (G2V)
Ca. 64…72 % for Vehicle-to-Grid (V2G)
Car is the master and charger is a slave!
Sources: [1], [3], [4]

## Slide 6: Smart charging
Requires communication between EV and the grid
Connection to local or cloud based central system
Enables remote load management (power control)
Open Charge Point Protocol (OCPP)
Open standard to communicate with any charge point to any central system
To uniform systems regardless of the system vendor
Open Smart Charging Protocol (OSCP)
24-hour forecast of the available capacity
To prevent overloading the grid
Sources: [5], [6]

## Slide 7: Charging services
EV charging operators
Offers and operates charging stations and services
Public and domestic stations can be operated
Usage and payments e.g. with RFID tags
Multiple plugged EVs form ”a virtual power plant” to be utilized for demand response
Charging for EVs ↔ demand response for the grid
EV demand response is a two-way possibility:
  V2G  EV is power bank when low production
  G2V  EV is power sink for surplus production
Sources: [7]

## Slide 8: Conclusions
Standardization and subsidies to ease up propagation
Communication between EV and the grid is a key thing
Two-way demand response with smart charging

## Slide 9: Source material used
[1] J. Vesa. 2017. Sähköautojen lataus (Finnish). Presentation slides. http://www.tukes.fi/Tiedostot/pelastustoimen_laitteet/2017_Vesa_S%C3%A4hk%C3%B6autojen_lataus.pdf
[2] SESKO ry. 2018. Sähköajoneuvojen lataussuositus (Finnish). http://www.sesko.fi/standardit/standardoinnin_aihealueita/sahkoautot_ja_latausjarjestelmat/lataussuositus
[3] E. Apostolaki-Iosifidou, P. Codani, W. Cempton. 2017. Measurement of power loss during electric vehichle charging and discharging. https://doi.org/10.1016/j.energy.2017.03.015
[4] A. Genovese, F. Ortenzi, C. Villante. 2015. On the energy efficiency of quick DC vehicle battery charging. https://www.researchgate.net/publication/274316538
[5] Rexel Finland Oy. 2017. Sähköautojen latausjärjestelmä (Finnish). Presentation slides. http://www.nssoy.fi/uploads/NSS-sahkoteleturva-rexel.pdf
[6] Open Charge Alliance websites. Visited 18.4.2018. http://www.openchargealliance.org/
[7] Liikennevirta Oy. Visited 18.4.2018. http://www.virta.global/