## Slide 1: ELEC-E8423 - Smart Grid Thermal heat storages for daily and seasonal use
Hanni Sonkeri, Noora Jaakamo
25.4.2018

## Slide 2: Introduction
The main idea with Thermal Energy Storage (TES) systems is to store thermal energy (heat or cold) in some form of medium for long periods
Since the variable renewable energy becomes more used around the world, it’s important to have the ability to store energy
There are three different main types of TES:
Sensible heat storages
Latent heat storages
Thermo-chemical storages
The key parameters of thermal energy stores are their capacity, energy density, power rating (ability to discharge), efficiency (losses over time and with charge/discharge) and cost.
Notes: the availability and the need of renewable energy differs but still we need a way to increase the degree which can be utilized from the renewables (pois diasta - voi sanoa ääneen?)
The key parameters of thermal energy stores are their capacity, energy density, power rating (ability to discharge), efficiency (losses over time and with charge/discharge) and cost.17.

## Slide 3: Sensible heat storage
The heat is stored by changing the temperature of the storage medium
The storage medium (liquid or solid) can be among others: water, molten salts, rock beds, sand etc.
Usually depends on the medium’s heat capacity, the range of temperatures at which the store will operate and the volume available for it
The most widely used form for TES
Sensible heat storages and their medium have quite low energy density → need of large volume of storage medium
UTES
Notes: Easy to implement and relatively small costs
Sensible heat storage is widely utilized in concentrated solar power (CSP) applications where the use of TES enables a project to produce electricity well after the sun has gone down
Generally, the medium of choice in CSP plants with TES is molten salts, which can withstand extremely high temperatures.’’
According to the International Renewable Energy Agency (IRENA), nearly all new CSP plants operating or under construction are equipped with a TES system.
  Later on focusing on one plant exactly with CSP with a TES system

## Slide 4: Latent heat storage
Latent heat storages are based on a phase change (usually solid-liquid) of a phase change material (PCM)
They provide thermal energy at constant temperature
Over the last decade, researches have shown much interest in the use of PCMs both in daily and seasonal use
For seasonal storage purposes, there seems to be much potential in active solar storage. Solar collector is often connected with e.g. agriculture greenhouses or heat pumps

## Slide 5: Thermochemical storage
Chemical storage includes chemical reaction and thermochemical sorption storage
Chemical reaction:
A reversible reaction between two substances: endothermic decomposition and exothermic synthesis process
Two substances are stored separately during the storage period
Sorption storage:
Adsorption: Gas bonds to the surface of a solid, without creating a new material
Absorption: New compound is formed
Why?
  The thermal storage volume for 34m3 water equivalent (70C increase) is only 1m3 for chemical reaction storage
  Capable to conserve energy at ambient temperature as long as desired without heat losses
--> Has become a widely researched technology

## Slide 6: Crescent Dunes -project
Location: Tonopah, Nevada, USA
Technology: CSP with Molten Salt TES
Sensible heat storage
Project status: In commercial operation
110 MW plant
1100 MWh energy storage
10 hours of electricity at full load
40 years storage without any degradation
Notes: CSP - concentrated solar power
Generally, the medium of choice in CSP plants with TES is molten salts which can withstand extremely high temperatures.
Molten salts last there 40 years without any replacement or anything
There are quite many this kind of projects around the world

## Slide 7: Wind powered Thermal Energy Storage (WTES)
Concept of storing wind power direct to thermal energy (being conducted)
The rotating energy is converted to the thermal energy at the top of the tower by using heat generator
The thermal energy is then transferred to the base utility by heat transfer fluid
According to one study the cost estimation says that the energy cost of WTES is less than the conventional wind power, which must be supported by the backup plant and grid enhancement
Better and fuller energy harvest with WTES
Notes: Rest is the same as with the CSP
The backup for example for a time when there’s no wind → this can also be fossil fuel, which then produces a lot of emissions and so on
The energy can be harvested better when it’s not converted to the electricity directly.

## Slide 8: Sensible VS. Latent VS. Thermochemical Heat Storage
Sensible heat storage is the cheapest and simplest alternative, latent and thermochemical are costly - > latent heat and thermochemical storages are still mainly only used in research
As said, sensible heat storage has the lowest energy density, thermochemical highest
Sensible heat storage suffers significant heat losses, thermochemical has almost zero
Some hybrid systems have been researched
PCM modules + temperature changes
Higher storage density than normal sensible heat storage but less than a pure PCM system
Still on development stage

## Slide 9: Conclusions
For now, sensible heat storage is the most cost-effective one for daily and seasonal use
Lots of research is going on for all three heat storage options
The less space there is for the storage, the more expensive the storage gets

## Slide 10: Source material used
SolarReserve. Crescent dunes. Available: http://www.solarreserve.com/en/global-projects/csp/crescent-dunes. [Accessed: 20.4.2018].
Harvey A. 2017. The latest in Thermal Energy Storage. Power Magazine. Available: http://www.powermag.com/the-latest-in-thermal-energy-storage/?pagenum=3. [Accessed: 20.4.2018].
Cabeza L. Thermal Energy Storage. Strategic research priorities for cross-cutting technology. Available: https://hub.globalccsinstitute.com/publications/strategic-research-priorities-cross-cutting-technology/3-thermal-energy-storage. [Accessed: 20.4.2018].
Okazaki T. Shirai Y. Nakamura T. 20Concept study of wind power utilizing direct thermal energy conversion and thermal energy storage. Renewable Energy. Vol.83. Available: https://www-sciencedirect-com.libproxy.aalto.fi/science/article/pii/S0960148115003079. [Accessed: 20.4.2018].
SavEnrg. 2018. Phase change energy storage Technology. http://www.rgees.com/technology.php [Accessed 21.4.2018]
Xu J. 2014. A review of available technologies for seasonal thermal energy storage. Solar Energy. pp. 610-638. Available: https://www.sciencedirect.com/science/article/pii/S0038092X13002272#bb0515 [Accessed: 22.4.2018]

## Slide 11: Thank You! Questions?