## Slide 1: ELEC-E8423 - Smart Grid Prosumer / Consumers. Local energy resources and local energy matching
Miika Rajala, Joni-Markus Hietanen
20.03.2018

## Slide 2: Introduction
Prosumer = Consumer that also produces energy
Local energy resources:
  Wind power resources
  Solar power resources
  Heat generation (Geothermal heat, burning wood in a fireplace etc...)
Energy matching
  Load management (=demand response)
  Energy storages
Notes: Let's begin by defining the term prosumer, just in case
On the local resources, we have focused mainly on electricity production, so heat is mentioned, but not went trough in detail
Then we talk about energy matching, why it's useful and how can it be done

## Slide 3: Local energy resources
Wind production
  Typical power output a few hundred watts on small wind turbines
Solar production
  Typical panel size around 3-10kW
  Could cover 4-8% of annual electricity demand on detached houses
Potential depends heavily on the geographical location
Notes: Local energy resources for example individual residential houses, like detached houses
Apart from geographical location, both of them depend heavily on environmental circumstances and also seasons

## Slide 4: Why energy matching is important?
It is not profitable to sell energy to the grid
  Selling price<<buying price
Electricity buying should be minimum
Electricity consumption should be shifted towards the time of production
  Load side management
  Storages

## Slide 5: Load Side Management
Practically same as demand response
No demand response from critical loads
Air conditioning, clothes dryer, electric vehicles etc. offer largest potential
Load side management is not feasible without smart technology
Different smart home solutions are already in the markets

## Slide 6: Load Side Management
Demand response simulation for a 2500 sq ft home with different demand limits (a) No demand limit. (b) 8 kW limit from 5 p.m.–10 p.m. (c) 6 kW limit from 5 p.m.–10 p.m. (d) 4 kW limit from 5 p.m.–10 p.m.

## Slide 7: Storages
Batteries: Lithium-ion batteries on a larger scale
Tesla Powerwall 14 kWh at pricepoint of 7300 €
Electric vehicles, if increased in number
Contain 30-90 kWh batteries
Could be used for charging as well as discharging
Goal: Reduce peak demand and provide flexibility
Could reduce demand up to 8-32%, depending on the operation algorithm
Electricity consumption rises, since batteries have losses
Do not yet provide true independance from the grid
Battery sizes low
Is useful tool on local electricity matching
Notes: There are different ways to store electricity locally by individual consumers, two of the most feasible are: large batteries and also electric vehicles
Depending on the complexity of the operation algorithm of STORAGE --> Batteries possess a real value on smoothing out demand
These results are from a case, where the household had implemented solar panels as well!
Storage is in one way the electricity consumer, when it's not in use
Rise of consumption corresponds to more electricity based system emissions etc

## Slide 8: Implementation
Example of an implemention, taking into account most
relevant ways to fulfill energy matching.
Notes: Taking into account all of the previously mentioned solutions, implementation could look something like this, in order to fully achieve the edvantages of local energy resources as well as energy matching.
So we have local resources, storage and grid, all connected to the consumer through an intelligent optimized system. Imported electricity from the grid also uses load management to fully optimize the entire system.

## Slide 9: Conclusions
Local resources consist mainly of wind and solar
Energy matching is required if local production is aimed to be profitable
Energy matching can be done
  By load side management
  With energy storages

## Slide 10: Source material used
Wang, Caisheng, and M. Hashem Nehrir. "Power management of a stand-alone wind/photovoltaic/fuel cell energy system." IEEE transactions on energy conversion 23.3 (2008): 957-967.
Kelleher, J., and J. V. Ringwood. "A computational tool for evaluating the economics of solar and wind microgeneration of electricity." Energy 34.4 (2009): 401-409.
Pipattanasomporn, M., Kuzlu, M., Rahman, S. "An Algorithm for Intelligent Home Energy Management and Demand Response Analysis", IEEE Transactions on Smart Grid ( Volume: 3, Issue: 4, Dec. 2012 )
https://www.motiva.fi/ratkaisut/uusiutuva_energia/tuulivoima/pientuulivoima
http://www.arevasolar.fi/fi/aurinkopaneelit-omakotitaloon
https://www.tesla.com/fi_FI/powerwall
Hittinger, Eric. "Distributed generation: Residential storage comes at a cost." Nature Energy 2.2 (2017): 17006.
Fortum SmartLiving, http://lampopilotti.fi/