## Slide 1: ELEC-E8423 - Smart Grid Supergrids
Jori Valtakari
08.05.2018

## Slide 2: Introduction
What is a supergrid?
Benefits
Problems
Supergrid projects
Conclusions

## Slide 3: What is a supergrid? 1/2
AC not suitable for long transmission distances HVDC grid
In this context Super refers to:
  HVDC lines move large quantities of energy separate from the existing AC grid
  Larger geographical reach, possibly even a global supergrid?
  Better than the existing grid in terms of efficiency
No real standard for HVDC voltage level, 600+ kV could be reasonable

## Slide 4: What is a supergrid? 2/2
Possible HVDC topologies:
  Multi-terminal with tappings
    Simple but not really a “grid”
  Grid of independent lines
    Transmission line replaced with DC circuit with two converter stations
    A large number of converter stations required
  DC grid
    Meshed DC system with a number of connections to the AC grid
    The only “real” grid out of the three
    If redundancy required, only viable solution

## Slide 5: Benefits
Ability to utilize remote RES that would be otherwise economically unfeasible
Better renewable energy balancing
Reduced congestion in existing systems
East-West connections  balancing between different time zones

## Slide 6: Problems
Requires collaboration between multiple different countries
High investment costs
Ownership
Regulation due to cross border transfer
  All parties must comply on the technical specifications of the system
Technical
  AC system limited availability to “collect” the energy
  AC grid not oriented to support an offshore supergrid

## Slide 7: Supergrid projects
Desertec
  Harvesting solar power in the world’s deserts
  Transmission via HVDC
  The world’s deserts receive more energy in 6 hours than mankind consumes yearly
Gobitec
  Similar to Desertec but in the Gobi desert
The North Sea Offshore Supergrid
  HVDC lines under the North Sea
A global supergrid requires roughly 100 000 km of HVDC lines and over 115 converter stations

## Slide 8: Conclusions
Supergrids are an efficient way to transmit large quantities of energy
HVDC grid better option than HVAC grid
Global supergrid, utopia?

## Slide 9: Source material used
Blau, J. 2010. Europe plans a North Sea grid. IEEE Spectrum. Volume 47, Issue 3. pp. 12-13. DOI: 10.1109/MSPEC.2010.5421884
Bompard, E. Fulli, G. Ardelean, M. Masera, M. 2014. It's a Bird, It's a Plane, It's a...Supergrid!: Evolution, Opportunities, and Critical Issues for Pan-European Transmission. IEEE Power and Energy Magazine. Volume 12, Issue 2. pp. 40-50. DOI: 10.1109/MPE.2013.2294813
Desertec, 2018. The Desertec-Concept. [Online] Available at: http://www.desertec.org/the-concept [Accessed 7 May 2018]
Gobitec, 2018. Gobitec Initiative. [Online] Available at: https://gobitecdotorg.wordpress.com/the-conceptual-idea-behind-gobitec/ [Accessed 7 May 2018]
H,H. 2017. What is a supergrid? The Economist. [Online] Available at: https://www.economist.com/blogs/economist-explains/2017/01/economist-explains-10 [Accessed 7 May 2018]
Macilwain, C. 2010. Energy: Supergrid. Nature. Volume 468. pp. 624-625. DOI: 10.1038/468624a
Van Hertem, D. Ghandari, M. 2010. Multi-terminal VSC HVDC for the European supergrid: Obstacles. Renewable and Sustainable Energy Reviews. Volume 14, Issue 9. pp. 3156-3163. DOI: 10.1016/j.rser.2010.07.068