## Slide 1: ELEC-E8423 - Smart Grid DR in distribution network congestion management
Niklas Armila
Henri Huotari
27.03.2018

## Slide 2: Introduction
Scope of the presentation
Development of demand response
Distribution network congestion in the future
Real-time thermal rating (RTTR)
DR for network congestion and variable renewable energy (VRE)
Power component in distribution tariffs

## Slide 3: Development of DR
The electricity supply has been relatively constant (big utilities with high CF (e.g., nuclear))
Demand has been variable (seasonally, 24 hours)
  Time-of-use (TOU) tariff implemented by DSOs. Capacitive heat loads switched on gradually during nights to lower the peak powers, serving the distribution network and matching with the supply (no conflicts of interest)
With increasing amounts of VRE, also the supply becomes variable. Therefore, the flexible capacity lying behind the TOU tariff and control could be used more efficiently to decrease curtailment of VRE during high supply hours
  Could be implemented decentralized by consumers following price-signals (e.g., spot price) or other real-time data, or centralized by an aggregator
  However, network constraints have to be respected

## Slide 4: Network congestion in the future
Sizeable individual loads increasing the congestion in the future
Electric Vehicles (EV)
Ground-source heat pumps (GSHP)
Cases above will introduce mild increase to loads in the future
Some distribution transformers overloaded before the addition of GSHPs
Overload does not necessarily mean hardware failure
Might introduce voltage drops to end of a distribution network

## Slide 5: Real-time thermal rating (RTTR)
When network capacity to support high VRE output is inspected, traditional static rating (STR) of thermally susceptible components is used
Means often curtailing VRE output and thus limiting the benefits of DR
Instead real-time thermal rating (RTTR) could be used in combination of DR to reveal the real network capacity to support increased DG
For example, greater wind mean greater DG as well as greater RTTR for OH lines -> Greater network capacity -> Working in synergy
Case 1: DR is not used
Case 2: DR is applied with STR values for network
Case 3: DR and RTTR are optimally applied

## Slide 6: DR for network constraints and VRE
The optimal use of DR has to be evaluated between facilitating the integration of VRE and considering network constraints
Case 1: considering only network constraints
Case 2: considering both network constraints and costs of curtailment
The optimal amount of curtailment only a few percentages, and network investments should be feasible
(Mubbashir et.al. 2018.)

## Slide 7: Power component in distribution tariff 1/2
Including a power component in distribution tariff means moving from the typical (€/month + €cnt/kWh) to a (€/month + €cnt/kWh + €/kW) structure
  More possibilities for consumers to affect their electricity bill
  More cost-based distribution tariff
Flexible loads following cost-based price signals from both electricity markets AND network would lead us closer to a cost-optimal situation for the whole society (invisible hand)
The figure illustrates optimization of the use of flexible loads by an individual consumer according to:
  a) both electricity markets and peak demand
  b) peak demand
  c) electricity markets - worst case for the grid
(LUT, TUT. 2017.)

## Slide 8: Power component in distribution tariff 2/2
The figure illustrates a certain distribution networks distribution transformers (20/0.4 kV) relative loadings
  A combined optimization between the peak powers and electricity markets would save the distribution network from overloading, and yet some flexibility could contribute to the supply/load issue as well
Criticism:
  Getting consumers involved can be difficult
  The peak powers at 110/20 kV transformers would most likely still increase (less crisscross among the loads)
  Would lessen the availability of DR for VRE integration a lot
(LUT, TUT. 2017. Modified)

## Slide 9: Conclusions
The optimal utilization of DR has to be considered from the perspectives of different operators (TSO, retailers, DSOs, consumers, and aggregators)
The distribution networks often form “bottlenecks” between the need (VRE) and resources (flexible load & DR), which has to be respected
  The capacity can be somewhat extended by RTTR
  Further investments to the grid should be feasible with a high share of VRE
A power component in distribution tariffs for consumers could help steering the DR of flexible loads to respect the network constraints besides following market signals (DSOs could still control the loads directly in cases of emergency)

## Slide 10: Source material used
Mubbashir, A.; Millar, R. J.; Lehtonen, M. (2018). A Framework to Split the Benefits of DR Between Wind Integration and Network Management. IEEE TRANSACTIONS ON POWER SYSTEMS, VOL. 33, NO. 2. Available: http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=7961261
Mubbashir, A.; Merkebu Z D; Muhammad H; Amir S; Lehtonen M. (2017). Increased Utilization of Wind Generation by Coordinating the Demand Response and Real-time Thermal Rating. IEEE TRANSACTIONS ON POWER SYSTEMS, VOL. 31, NO. 5. Available:
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=7332246
TUT, TAMK, LUT. (2015). Kysynnän jousto - Suomeen soveltuvat käytännön ratkaisut ja vaikutukset verkkoyhtiöille (DR pooli): Loppuraportti.
Available: https://tutcris.tut.fi/portal/fi/publications/kysynnan-jousto--suomeen-soveltuvat-kaytannoen-ratkaisut-ja-vaikutukset-verkkoyhtioeille-dr-pooli(d8a7e38d-6533-417e-974c-8399326a55c6).html
LUT, TUT. (2017). Jakeluverkon tariffirakenteen kehitysmahdollisuudet ja vaikutukset. Available: http://www.doria.fi/handle/10024/143710
TEM. (2017). Matkalla kohti joustavaa ja asiakaskeskeistä sähköjärjestelmää. Älyverkkotyöryhmän väliraportti. Available: http://tem.fi/artikkeli/-/asset_publisher/alyverkkotyoryhman-valiraportti-matkalla-kohti-joustavaa-ja-asiakaskeskeista-sahkojarjestelmaa
Alanen, R.; Hätönen, H. (2006). Sähkön laadun ja jakelun luotettavuuden hallinta. Espoo, Finland: VTT.