## Slide 1: ELEC-E8423 - Smart Grid Wind Power Generation Variations and its Modelling
Hassan Iftikhar Bhatti
İsmet Tuna Gürbüz
08.05.2018

## Slide 2: Introduction
Wind Power: Wind power is the use of air flow through wind turbines to mechanically power generators for electricity. It gives variable power at the output but can’t be considered intermittent
It has some advantages as mentioned below;
Uses less land
Clean, produces no green house gas emissions
Consumes no water
487 GW installed capacity globally (2016)
150 GW installed capacity in EU with 12.5 GW new capacity (2016)

## Slide 3: Wind Power Generation Variations
It varies continuously and at all times
It can be considered as a variable , dynamic electric system
We need to consider it overall and examine the system
It can’t be considered intermittent and it is misleading
As it is distributed installation, shutdown of a single unit doesn’t affect the whole system
2 main categories to define the wind power variation are;
Short term variations
  i) Within the minute ii) Within the hour iii) Hour-hour
Long term variations
i) Monthly and seasonal ii) Inter annual variations

## Slide 4: Short Term Variations
Caused by;
Tower shadow (air stream is disturbed)
Wind shear (which makes the speed higher during upper part of rotation and lower during the lower part of rotation)
Turbulence (stochastic variations of wind)
P = Power (W) Power Coefficient V = wind speed (m/s)
A = Swept area of rotor disc() = Density of air(1,225 kg/
i) Within the minute
Fast variations (as a consequence of turbulence or transient events)
Quite small (due to the aggregation of wind power) and barely impact the system
ii) Within the hour
More significant for the power system
Should be considered for the demand fluctuations as well
Local variations are within +- 5% of installed wind capacity
Notes: Low Wind: The power is too small and no electricity is generated.
Normal Wind: Wind turbine catches the maximum power from wind.
High Wind: The power of wind energy is higher than the nominal power of wind turbine. Wind turbine absorps a portion of wind energy. Rated output power is maintained.
Strong Wind: Wind speed is too high for wind turbine. In order to protect the system, electrictiy generation has to be stopped.

## Slide 5
iii) Hour to Hour
Variations between forecast and actual wind energy production several hours ahead affect the scheduling of the power system
The variation in itself is not a problem; it is the uncertainty of how accurately the variation can be predicted that is significant
The uncertainty of wind power predictions should always be considered in relation to the errors in demand forecasts

## Slide 6: Long Term Variations
Occurs as a result of climate effects
Has no significant effect on daily system but important for long term planning
i) Monthly and Seasonal Variations
Important for electricity traders (for the future contracts wind power has a huge influence)
Important for power system planning
ii) Inter-Annual Variations
Important for long-term system planning
Standard deviations of variations in a normal distribution is around 6 percent.

## Slide 7: Effects of Variations
Aggregation of wind power over a large scale is needed
Modelling for future plans is needed
WF: Wind Power

## Slide 8: Modelling
Long Term Wind Power Modelling is based on Monte Carlo Simulation Methods
Monte Carlo Methods are commonly used for modelling inherent variability in systems of which a closed form analytical expressions cannot be obtained or is complex
Monte Carlo simulation is based on simulating the value of uncertain parameters using random number generators to determine the sampled statuses and estimating the outputs
After a large number of simulations (trials) are performed, it is expected that the probability distribution of the outputs will be obtained with a degree of confidence to the confidence interval
There are two viable modelling approaches. These are either statistical or physical models such as meteorological reanalysis models
The reanalysis models combine years of data (wind speed, solar irradiance, temperatures) measurements to numerical weather prediction (NWP)
However, the reanalysis models are not applicable for Monte Carlo simulations
On the other hand, the statistical models are applicable for Monte Carlo simulation studies

## Slide 9: Simulation Process for the Model
Retrieved from:
J. Ekström: Statistical Methods for Variable Renewable Energy Generation Modelling, 2018

## Slide 10: Conclusions
Wind power generation is variable due to the environmental and constructional effects
Variations in wind power generation has lots of effects on the whole power system (especially for future planning)
In order to estimate the future variances and shape the future planning of system according to it, some precautions and proper modelling is inevitable

## Slide 11: Source material used
S. Engström, H. Ganander , R Lindström: Short Term Power Variations in the Output of Wind Turbines, 2001
H. Holttinen: Hourly Wind Power Variations and Their Impact on the Nordic Power System Operation, 2003
H. Holttinen: Impact of Hourly Wind Power Variations on the System Operation in the Nordic Countries, 2005
L. Reichenberg: Dampening Variation in the European Wind Energy System, 2015
J. Farrell: Solving Wind Power’s Variability with More Wind Power, 2011, from http://www.geni.org/globalenergy/library/technical-articles/generation/wind/renewableenergyworld.com/solving-wind-powers-variability-with-more-wind-power/index.shtml
B. Banerjee, D. Jayaweera, S. Islam: Modelling and Simulation of Power Systems
J. Ekström: Statistical Methods for Variable Renewable Energy Generation Modelling, 2018
Understanding Variable Output Characteristics of Wind Power: Variability and Predictability, from https://www.wind-energy-the-facts.org/understanding-variable-output-characteristics-of-wind-power-variability-and-predictability.html