## Slide 1: ELEC-E8423 - Smart Grid Power and Energy Balance management in Micro Grids
David Sevsek
Olli Soppela
18.03.2018

## Slide 2: Introduction
Cluster of loads, storage devices and small generators
Autonomous networks connected to the public grid (point of common coupling=PCC)
Islanded or grid-connected mode
David Sevsek
Olli Soppela
Power and Energy Balance management in Micro Grids
Notes: Microgrids have received increasing attention as a means of integrating distributed generation into the electricity grid. Usually described as confined clusters of loads, storage devices, and small generators, these autonomous networks connect as single entities to the public distribution grid, through a point of common coupling (PCC). The figure illustrates a typical microgrid network. Microgrids comprise a variety of technologies: renewable sources, such as photovoltaic and wind generators are operated alongside traditional high-inertia synchronous generators, batteries and fuel-cells. Thus, energy is generated near the loads, enabling the utilization of small-scale generators that increase reliability, and reduce losses overlong power lines.
In islanded mode, the main goal of power management is to stabilize the system, in terms of frequency and voltage. In grid- connected mode, typical objectives are to minimize the price of energy import at the PCC, to improve power factor at the PCC, and to optimize the voltage profile within the microgrid. This work addresses grid-connected networks.

## Slide 3: Microgrid stability
David Sevsek
Olli Soppela
Power and Energy Balance management in Micro Grids
Notes: Thereby three categories of stability are distinguished:
1. Rotor Angle Stability: Ability of synchronous machines to hold the electromagnetic torque and the mechanical torque in an equilibrium.
2. Frequency Stability: The equilibrium between generation and loads must be ensured.
3. Voltage Stability: Mainly depends on the balance of reactive power demand and supply.
The inertia in a microgrid is very small. If there is a rotating generator in the system and there occurs an imbalance between the input mechanical torque and the output electromagnetic torque, a fast deceleration or acceleration of the rotor will occur. But in microgrids it is also possible that all generation units are connected with synchronised power electronic inverters. In this case the frequency is independent of rotating masses. Therefore the information and control system has to react quickly if an unbalance occurs in the system. If the power supply is too big, the batteries can be charged. Else if the power consumption is over the supply, shedable loads can be switched of to restore the power balance . Connecting or disconnecting of loads in isolated operation can be critical if they are big in relation to the installed generation capacity.

## Slide 4: Energy Management System (EMS)
David Sevsek
Olli Soppela
Power and Energy Balance management in Micro Grids
Notes: An energy management system (EMS) is a system of computer-aided tools used by operators of electric utility grids to monitor, control, and optimize the performance of the generation and/or transmission system.
The computer technology is also referred to as SCADA/EMS or EMS/SCADA. In these respects, the terminology EMS then excludes the monitoring and control functions, but more specifically refers to the collective suite of power network applications and to the generation control and scheduling applications.

## Slide 5: Hierarchical Control System
David Sevsek
Olli Soppela
Power and Energy Balance management in Micro Grids
Notes: Energy management in microgrids is usually thought of as a three-level hierarchical control system. The first control level, often called “primary” or “autonomous” control, consists of a number of local, autonomous controllers. Each controller governs a power electronics converter and is responsible to interface generators, storage devices, and loads with the microgrid . These controllers are the fastest, as they operate in the millisecond range, employing a droop control in islanded mode . A secondary control level employs a low-bandwidth communication to fix the frequency and amplitude of the microgrid’s units, restoring their nominal values. Finally, the tertiary control level, is related to the control of active and reactive power flow. This level of control is related to EMS and to the optimization of the microgrid resources and is the main subject of this work.

## Slide 6: General Power Quality Issues
Most common power quality balancing parameters include (:
RMS of the current & voltage
Phase synchronization between the waveforms of a multi-phase signal
Power factor
Frequency
Total Harmonic Distortion
Active (kW) & reactive power (kVAr)
Apparent power (kVA)
Active (kWh) & Reactive (kVArh) Energy
Power and Energy Balance management in Micro Grids
Picture by Mike Holt
David Sevsek
Olli Soppela
Notes: Grid Power Generation has set standards to harmonize the electric flow in the grid.
Varying loads and circuit compositions require power electronics to stabilize the inputs and outputs from grouped loads.
Power quality is done to minimize losses and to optimize the performance of the electric loads connected to the grid.

## Slide 7: Energy Balancing
Consumption pattern prediction is done with real time production data, smart metering, customer profiling & integrated weather data (Karlsen et al. 2014)
Demand management is done actively by automatic load switch-off.
Automatic Load Switch
Flow Battery System
Power and Energy Balance management in Micro Grids
David Sevsek
Olli Soppela
Micro-grids with intermittent energy production require energy storages in order to consume this energy during production shortages. Production rates have to be managed according to the demand by curtailing surplus generation. Frequency, voltage levels and waveforms are controlled with power electronics, such as frequency controllers, capacitors & inductors etc.
Notes: Supply and demand of electric energy is balanced with fast reacting generators and storages, demand prediction modeling and demand side management.

## Slide 8: Energy Storage
Energy storages can be used for power balance management, power quality management & electricity arbitrage in the micro-grids
Hydrokinetic Storage
CAES & LAES
Flow Batteries & Batteries
Potential future solutions
4. Synthetic Gases
Comparison of Energy Storage Technologies (Abbas et al. 2013)
Power and Energy Balance management in Micro Grids
David Sevsek
Olli Soppela
Notes: Most suitable grid scale energy storage methods are hydrokinetic storage and compressed air energy storage, which both require natural deposits to be cost efficient.
Artificial compressed air and liquid air storages can be done with higher initial costs.
Flow batteries and distributed battery networks are evolving to play a bigger role in the grid scale energy balance management.
In the future usage of synthetic gas production by electrolyzers may have a significant role in the power system. Currently its conversion efficiency is still non-competitive to the alternative storage methods.

## Slide 9: Conclusions
List three most important key points of presentation here
Microgrids facilitate the integration of distributed generation and enhance their controllability
In grid connected operation they can also help to improve the power quality of the utility grid
Energy storage, consumption prediction & demand management help to match demand and production curves
Power and Energy Balance management in Micro Grids
David Sevsek
Olli Soppela

## Slide 10: Source material used
Abbas A. Akhil, Georgianne Huff, Aileen B. Currier, Benjamin C. Kaun, Dan M. Rastler, Stella Bingqing Chen, Andrew L. Cotter, Dale T. Bradshaw, and William D. Gauntlett (2013)
- “Electricity Storage Handbook in Collaboration with NRECA”. DOE/EPRI, SAND2013-5131 Unlimited Release.. Availabe at: http://www.sandia.gov/ess/download/2565/
Bühler R (2010) - “Integration of Renewable Energy Sources Using Microgrids, Virtual Power Plants and the Energy Hub Approach“. EEH – Power Systems Laboratory Swiss Federal Institute of Technology (ETH) Zurich. Available from: https://www.ethz.ch/content/dam/ethz/special-interest/itet/institute-eeh/power-systems-dam/documents/SAMA/bis%202010/Bühler-SA-2010.pdf
Karlsen L. A. & Goodwin M. (2014) - “Evaluating prediction models for electricity consumption”. Faculty of Engineering and Science, University of Agder Teknova AS, Norway
Kundur P. , Paserba J. , Ajjarapu V. , Andersson G. , Bose A. , Canizares C. , HatziargyriouN. , Hill D. , Stankovic A. , Taylor C. , Van Cutsem T. & Vittal V. (2004)
- “Denition and Classication of Power System Stability”. IEEE Transactions on Power Systems, VOL. 19, NO. 2.
Lampropoulos I., Kling W. L., Ribeiro P. F., Willem J. & van den Berg K. (2013) - “History of demand side management and classification of demand response control schemes” Published 2013 in IEEE Power & Energy Society General Meeting. Available from: https://www.semanticscholar.org/paper/History-of-demand-side-management-and-classificati-Lampropoulos-Kling/3c9be775df807129df9bebee050b2dc2e77c1de9
Palizban O., Kauhaniemi K., (2014) - “Hierarchical control structure in microgrids with distributed generation: Island and grid-connected mode”, ScienceDirect, Available from: https://www.sciencedirect.com/science/article/pii/S1364032115000180
Raael Buhler (2010), Integration of Renewable Energy Sources Using Microgrids, Virtual Power Plants and the Energy Hub Approach, Available from: https://www.ethz.ch/content/dam/ethz/special-interest/itet/institute-eeh/power-systems-dam/documents/SAMA/bis%202010/Bühler-SA-2010.pdf
Yoash Levron et. al. (2013), “Optimal Power Flow in Microgrids With Energy Storage”, IEEE TRANSACTIONS ON POWER SYSTEMS, VOL. 28, NO. 3, AUGUST 2013 , Available from: http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=6469193
WANG X. et. al. (2016) - “Power balance control of Energy Storage Unit in Micro Grid based on distributed gradient algorithm”
Available from: http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=7554923&tag=1
Image sources:
Automatic switch image, slide 7: http://findgenerators.net/automatic-transfer-switch-find-info-on-automatic-transfer-switches-for-generators.html
Flow Battery image, slide 7: http://global-sei.com/products/redox/
Power and Energy Balance management in Micro Grids
David Sevsek
Olli Soppela

## Slide 11
Thanks!!!
Questions?