## Slide 1: ELEC-E8423 - Smart Grid Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Juha Piipponen
Joonas Saarela
05.03.2018

## Slide 2: Introduction
Demand Response
Energy use in residential buildings
DR potential in residential energy usage
Controlling of residential energy usage for DR
Conclusion
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 3: Demand response
Electricity production must meet the consumption
New renewable energy sources are highly variable
Solution is to shift loads from peak hours to low-demand hours
Rakennusksen kysyntäjoustomollinnuksen vaatimusten määritys, Kreetta Manninen
05.03.2018
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses

## Slide 4: DR in residential buildings
Frequency controlled primary reserves
Secondary reserves in disturbance
Power sink
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 5: Electricity use in residential building
Data: https://www.vattenfall.fi/energianeuvonta/sahkonkulutus/
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 6: Flexibility and load shifting
Loads can be divided into two categories:
  Critical loads
    Cooking, illumination
  Non-critical loads
    Heating
    Dish and clothes washing
Table in right represents the maximum time that the device use can be postponed
Get Smart, Lui et al 2010
Appliance | DR Potential (hr)
Washing Machine | 4
Clothes Dryer | 1
Dish Washer | 5
Water Heater – Storage | 3
Water Heater – Direct | -
Refrigerator & Freezer | 1
Air Conditioner | 1
Space Heating – Storage | 5
Space Heating - Direct | 1
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 7: DR Potential in residential energy usage
500 000 - 600 000 Electrically heated houses in finland
With AMR (Automatic meter reading) over 1000MW of heating energy could be utilized in DR
With smart management system 1800MW or more
Smart systems also includes possibilities to include other electrical devices to DR
Needs to be considered: Heat gains, comfort..
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 8: Controlling of energy usage for DR
Home electronic management system (HEMS)
AMR with load control
Manually
Other automatic system
ThereHome-käyttöliittymän suunnittelu ja
toteutus, Timo Haapio
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 9: Conclusions
Residential buildings has a massive potential in DR
Electrical heating in households in one of the biggest DR potential
With smart systems in households the potential could be increased especially in the future when amount of electrical vehicles is higher
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
05.03.2018

## Slide 10: Source material used
https://www.vattenfall.fi/energianeuvonta/sahkonkulutus/sahkolaitteiden-energiankulutus/
Sähkön kysyntäjouston toteuttaminen kotitalouksissa, Mikael Kauppinen, https://aaltodoc.aalto.fi/handle/123456789/20888
Kysynnänjouston pilottiprojekti, Ilkka Palola, There Corporation Oy
ThereHome-käyttöliittymän suunnittelu ja toteutus, Timo Haapio, https://www.theseus.fi/bitstream/handle/10024/73789/Timo_Haapio.pdf?sequence=1
Rakennusksen kysyntäjoustomollinnuksen vaatimusten määritys, Kreetta Manninen, https://www.doria.fi/bitstream/handle/10024/134517/Diplomityo_Manninen_Kreetta.pdf?sequence=2
Joseph Lui, Warwick Stirling and Henry O. Marcy, “Get smart,” IEEE Power and Energy Mag., vol. 8, no. 3, pp. 66–78, May 2010.
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses