## Slide 1: ELEC-E8423 - Smart Grid AMR – Systems in SG
Olli Vaniala
17.04.2018

## Slide 2: Automatic Meter Reading
Automatic meter reader is a device that automatically collects measurement data
The data is then sent to a data collection center to be analyzed
Most commonly used in household energy consumption measurement

## Slide 3: Metering in general
Meter reading used to be manual and an electrician would have to visit the meters to get the data
Network error location is slow
Meters easily tampered

## Slide 4: AMR in Households
In Finland a household AMR takes measurements every 15 minutes.
However, most AMR devices can be remotely called and they can remotely give fault data.
Measures phase voltage, current, power consumption, neutral and ground connection.

## Slide 5: AMR use in the LV-grid
In the low voltage grid, AMR is most used in households and transformers
In urban areas with parallel feeding they may be installed in the distribution cabinets
AMRs in distribution cabinets usually have remote disconnection capabilities
AMRs are most used for consumption and billing purposes in the LV-grid

## Slide 6: AMR use in the MV- and HV-grid
In the medium and high voltage networks AMRs are used to locate faults and measure conductor losses
Fault location data is used to disconnect the failed conductor
Phase voltage and loss can be used to measure conductor degradation
Consumption data gives more accurate data for network designing

## Slide 7: Conclusion
AMRs are used for billing, fault location and network designing
AMRs are most commonly located in transformers, substations, and consumer distribution boards

## Slide 8: Source material used
Tampere university - AMR – Not only for remote reading
www.kamstrup.com - Kamstrup AMR devices.
Products.kamstrup.com - Kamstrup 382M