## Slide 1: ELEC-E8423 - Smart Grid Demand response of industrial loads
Andreas Lund
Jussi Närhi
07.02.2018

## Slide 2: Contents
Introduction
Principles of demand reponse (DR)
Characteristics for DSM participation
Issues with industrial DR
Potential of industrial DR
Link to electricity markets
Conclusions

## Slide 3: Introduction
Demand for ’flexibility’ in power system increases
Industry sector ½ of all electricity in Finland
Varying possibilities for demand flexibility and response
  Large single users (e.g. paper mill)
  Complex industrial processes
  Depends on product value vs. compensation

## Slide 4: Principles of Demand Response
Demand Response (DR) or Demand Side Management (DSM)
Why?
  Improve demand & supply matching
  Avoid costly new investments in power plants
  Improve power system reliability
How?
  Affects demand profile and magnitude
  Different time scales (fast-slow)
  Affects power and/or energy

## Slide 5: Characteristics for DSM participation
The focus of demand-side load participation is primarily on the industrial sector due to
  inherently large loads
  existing sensors and metering technologies available
  existing staff of competing plant managers and energy buyers
For a load to have the ability to provide DSM, certain characteristics are necessary
  speed of response
  automation
  load directionality
  metering
  frequency of request
  geographic location of response

## Slide 6: Characteristics for DSM participation
These loads can also be classified as follows:
Main Process Load (MPL)
  process steps that are dedicated to the direct output of the facility through the handling or transformation of raw materials
Ancillary Process Load (APL)
  processes involved in supporting the main process loads
Environmental Process Load (EPL)
  processes required to provide a safe and comfortable working environment for the facility employees.
These each have inherent flexibility. In this case, flexibility is the availability of loads to move a portion of the consumption and is not specific towards any service.

## Slide 7: Issues and advantages with industrial DR
Energy-intensive industrial processes often run on continuous basis
Lack of storage, processes run according to customer plan
Integration of industrial processes to other sectors and businesses
Price risk already minimized (hedging, long-term contracts)
Not part of the core business
Investment costs in DR often much lower than gas turbine (supply)
Variable costs higher than with a gas turbine (supply)
Smart metering and data exchange equipment often available
Etc.

## Slide 8: Potential of industrial DR
Country | Sweden | Denmark | Norway | Finland | Estonia | Latvia | Lithuania | Total:
Peak [MW] | 27,000 | 6,100 | 24,000 | 15,105 | 1,550 | 1,368 | 2,200 | 77,323
Industry energy % | 36.8% | 33.1% | 43.7% | 47.0% | 32.0% | 28.0% | 40.0% | 40.6%
Industry flexibility, share of peak | 7.0% - 8.5% | 0.3% - 3.5% | 1.1% - 6.3% | 9.0% | 4.2% | 0.5% - 1.0% | 0.2% - 0.8% | 4.7% - 7.1%
Potential of Demand Response (DR) in industry varies by country and industry sector
  Finland: 9% of peak load (total DR potential <30%)
  grinderies in pulp and paper mills 6%; electrolyses, electric arc furnaces and rolling mills in metal industry 2%; electrolyses, extruders and compressors in chemical industry 1%; and mills in cement, lime and gypsum production 0.04%

## Slide 9: Link to electricity markets
FINGRID-operated demand flexibility
The price signals can be sent from the power market, intraday market, and regulatory power market after a Transmission System (TSO) Call, balancing markets or from tariffs.
In 2017, Fingrid enabled a model for independent aggregator in frequency containment reserves for disturbances, more pilots starting
Some companies offer demand response services for customers, e.g. Helen Oy offers DR for companies with flexible power consumption

## Slide 10: Conclusions
Industrial electricity use is significant, but demand response is limited by the special characteristics of the sector
Main advantage of DSM is that it is less expensive to adjust a load, than to build a new power plant or energy storage device
Potential of industrial DR in Finland is around 9% of the peak load
There are many markets with mechanisms to mobilize industrial DR in Finland and progress on this field

## Slide 11: Source material used
Give the list of references used for the presentation preparation
http://www.energy.ca.gov/2013_energypolicy/documents/2013-06-17_workshop/caiso_dr_workshop_materials/ENBALA-CommentsDR-EERoadmapWorkshop-SupportingDocumentation.pdf
https://dspace.cc.tut.fi/dpub/bitstream/handle/123456789/25157/V%C3%A4%C3%A4n%C3%A4nen.pdf?sequence=3
https://ac-els-cdn-com.libproxy.aalto.fi/S1364032112005205/1-s2.0-S1364032112005205-main.pdf?_tid=b13f0186-4f33-41e9-ac89-df3a723643c4&acdnat=1520779135_7733a9f1eba9f82f646248e7fe356dac
https://aaltodoc.aalto.fi/bitstream/handle/123456789/14087/master_Jokiniemi_Juuso_2014.pdf?sequence=1&isAllowed=y#page9
Energiateollisuus : Energiavuosi 2017Sähkö
A review of demand side flexibility potential in Northern Europe, Lennart Söder et al
Review of energy system flexibility measures to enable high levels of variable renewable electricity, Peter Lund et al