## Slide 1: ELEC-E8423 - Smart Grid DR limitations set by human comfort requirements. Heat gains, heating and cooling, and demand flexibility
Madia Safdar
06.03.2018
1

## Slide 2: Demand Response (DR)
Globally, power grids are facing a list of acute challenges such as
Aging infrastructure
Overloading of power transmission lines due to increasing demands
Growing expectation of customers comfort level
Substantial load growth with the emergence of electric vehicles.
This creates urgent need for the optimal utilization of power grid, and demand response programs answers to this need.
“Changes in electric usage by end-use customers from their normal consumption patterns in response to changes in the price of electricity over time, or to incentive payments designed to induce lower electricity use at times of high wholesale market prices or when system reliability is jeopardized.” [1]

## Slide 3: Demand Response (DR)
Changes in average price of electricity, depending on the connected power plant types and their operational costs. (Left Fig.)
Due to the changes in real time generation costs due to load variation, the electricity tariff changes over the 24/day. (Right Fig.)
Therefore, it is advantageous for all the stake holders (utilities, transmission operators, and end users) to avoid these peaks. This is done by shifting non-critical loads to off peak hours.
This is the main objective of demand response (DR), also called demand side management (DSM).
[2]

## Slide 4: DR limitations set by customers’ comforts
The goal of DR is not only to change consumption towards helping the grid, but also maintain the customer’s comfort uninterrupted.
DR programs are developed according to customer’s preferences, which are set as constraints along with other technical constraints in optimization algorithms and cost minimization is the objective function.
Higher the no. of constraints, less effective the demand response program will be.
It is impossible to deploy an effective DR program without smart customers.
e.g. Objective func.
e.g. Constraint
Notes: More example of contraints: a certain degree of heating and heat gain, a certain degree of cooling,

## Slide 5: Share of heating and cooling in total residential energy demand
[3]
Cost of district heating in Espoo (Fortum 2016) [4]
In residential sector, the heating and cooling devices are the most energy consumers.
The HVAC load has the highest share in household demand in Nordic countries annually.
The energy payments are mainly due to space heating or water heating at homes.
Following table shows the costs of heating, from Fortum oy.

## Slide 6: DR in heating and Cooling
Due to the slow thermal dynamics of well-insulated buildings in Nordic countries, the thermal masses of building structures act as a buffer and can provide considerable load shifting capability.
A lot of research is going on in this area, including Aalto University. Some key results from a master thesis (Mr. Sihvonen) and Doctoral Thesis (Mr. Ali) are presented in the next two slides.
Major challenge is to convince customers to deploy automated demand side management programs in heating or cooling while ensuring them that their comfort levels will not be compromised.
However, there is still an essential need to develop practical frameworks so as to motivate customers into shifting their energy consumption of the HVAC load to off-peak hours, while considering the comfort levels.

## Slide 7: Key ideas in implementing DR in heating and Cooling
Shifting the heat load of a domestic hot water tank
Shifting space heating from morning peak hours to a few hours earlier, essentially preheating the building, results in a reduced heat load during the DR event, possibly no change in actual energy consumption and small changes in indoor temperature during the demand response event.
Heating and cooling storage during off peak hours and using that storage during high electricity prices.
Established the idea of optimizing the HVAC load operation to obtain a balance between user comfort and energy expenditure.

## Slide 8: Energy cost reduction potential due to DR in space heating
Research Question: What is the load reduction potential of an average residential building for demand response purposes, particularly regarding heating?
In this research work, a building energy model was developed using IDA ICE software and optimization was done by using MOBO software.
The results indicated that during a typical winter and spring day, a significant energy saving was accomplished by using optimization, while taking care of customer comforts.
Energy cost of a residential building on a typical winter day in Espoo

## Slide 9: DR potential in HVAC Systems
A mathematical tool is developed to thoroughly investigate the upward DR and downward DR capability of the domestic HVAC load
Key goals were to manage the HVAC load such that maximum availability occurs during the DR event period without compromising on user preferences set as Technical and comfort Constraints
Downward DR
Upward DR
HVAC DR Potential for Up/Down Ramping

## Slide 10: Conclusions
The take-way of my presentation are,
There is a huge potential for deployment of demand response in space heating and cooling, which is limited by customer comfort levels upto certain extent.
An awareness needs to be spread to the customers to ensure them that demand response program will not compromise their comfort levels.
Practical efforts are needed in this regard to implement the demand side management program for space heating and cooling, along with customer’s collaboration.

## Slide 11: Source material used
U. S. Department of Energy, "Benefits of demand response in electricity markets and recommendations for achieving them," Feb. 2006.
www.nordpoolspot.com
http://energyreportslondon.co.uk/2016/03/31/tips-homes-energy-use/
Sami Sihvonen, “Optimization of demand response control strategies in Finnish city-owned buildings”, Master Thesis, Aalto University, May 2017
Mubashir Ali, “Domestic Space Heating Load Management in Smart Grid- Potential Benefits and Realization”, Doctoral Dissertation, Aalto University, October 2016.

## Slide 12: Thank you for your attention!