## Slide 1: ELEC-E8423 - Smart Grid Demand Response of EV Loads
Mark Nortamo
Andrej Solovian
13.03.2018

## Slide 2: Introduction
Electric Vehicle (EV) = Vehicle with electric machine, battery and powertrain
  Generic term
Battery Electric vehicle (BEV) vs Plug in Hybrid Electric Vehicle (PHEV)
Battery capacity 6-90 kWh:
  6 - 30 kWh for PHEV
  30 - 90 kWh for EV
Current status
1449 full EVs, in total 7000 EVs in Finland
257 000 in the Nordics
Future plans
250 000 EVs in Finland by 2030

## Slide 3: Potential of EVs and Demand Response
Significance of EVs for Demand Response, four main points:
EVs are controllable loads, charging can be
  shifted
  interrupted
  restricted
Demand Response works both ways:
  Instantaneous withdraw of power from the grid (G2V)
  Instantaneous supply of power to the grid (V2G)
Provides inertia to the system by acting as energy storage
  Compatible with the markets to optimize prices
Is geographically distributed
  Not a huge node of power sink in one place

## Slide 4: Potential of EVs for Demand Response
Year 2017: Current battery capacity, 105 MWh energy in EVs
  If 50 % of the cars available for energy charging/dumping
    If able to simultaneously charge with 10 kWh → 35 MWh
    Average charge power about 5 kW → 17.7 MW
  50 % available for energy discharge
    If able to simultaneously discharge 5 kWh → 17.5 MWh
    If discharge power 3.5 kW → 12.25 MW
Year 2030: 250 000 EVs in Finland (15 000 MWh)
  If 75% available for energy charging/storage/dumping
    If able to simultaneously charge with 30 kWh → 563 MWh
    If charging power (Tesla supercharger) 120 kW → 2 250 MW
  If 75 % available for energy discharge
    If able to simultaneously discharge 10 kWh each → 188 MWh
    If discharge power 5 kW → 94 MW

## Slide 5: Impact of EVs to the grid
Problem of additional loading
Current size of Finnish power system
~85 TWh
250 000 EVs would increase the load of power system by
~1TWh
Over the past eight years electricity consumption has decreased by
~8TWh
→ No significant impact on power demand or production → Huge increase in flexibility
Source: Fingrid

## Slide 6: Impact of EV to the grid
EVs can also be double harmful for grid if charging is uncoordinated
Enhancing the peaks of residential demand
Enhancing price peaks
In order to facilitate demand response, important to charge off peaks/with coordination, not to be taken for granted
Direct control approaches (smart charging)
Involves no active participation of EV owner
Electric Vehicle aggregators / Load Controllers, a smart device that controls EV charging for one or multiple/large number of EVs
Different parameters can be set, such as
  DSO load information
  DA pricing
  Balancing needs, etc.
Indirect control approaches
EV owner in control over EV charging, however
  is incentivized for charging on certain hours
  The charging can also be automated for certain hours, such as night hours

## Slide 7: Future implications
Every time you stop your car you connect it to the grid
Could be implemented as a bonus system where you recieve money if you allow the grid to control the charge and discharge
Customer comfort still priority
  The battery percentage never drops below 30%
  If customer is going to make a longer trip
Futuristic example of EV capabilities with smart control of charging

## Slide 8: Conclusions
EVs have to be used with Demand Response programs
Especially when the EVs will (hopefully) increase rapidly
To ensure stability and flexibility in the power system
To optimize EV loads from system perspective
EVs are significant resource for demand response
Work both ways, charge and discharge
Instantaneous response
Possess power system scale potential in the future for balancing and storing energy
As renewable energy sources become more available with their uncertain power output
EVs have no major impact on power system design or size
If control approaches are introduced for charging
Impact to power system demand is marginal

## Slide 9: Source material used
https://www.fingridlehti.fi/en/sustainability-with-electric-cars/
Aspects of Electric Vehicles and Demand Response in Electricity Grids. / Rautiainen, Antti .
Tampere University of Technology, 2015. 80 p. (Tampere University of Technology. Publication; Vol. 1327).
https://www.trafi.fi/tietopalvelut/tilastot/tieliikenne/ajoneuvokanta/ajoneuvokannan_kayttovoimatilastot/sahkokayttoiset_autot
https://www.helen.fi/uutiset/2017/V2G/
http://www.nature.com.libproxy.aalto.fi/articles/s41560-017-0074-z
Impact of uncoordinated plug-in electric vehicle charging on residential power demand, Nature Energyvolume 3, pages193–201 (2018), doi:10.1038/s41560-017-0074-z
https://www.fingrid.fi/sahkomarkkinat/kulutus-ja-tuotanto/
http://www.energiavirasto.fi/voimalaitosrekisteri
The role of electric vehicles in
smart grids, WIREs Energy Environ 2013, 2: 384–400 doi: 10.1002/wene.56