## Slide 1: ELEC-E8423 - Smart Grid Power markets in Nordic Countries: Frequency containment and frequency restoration reserves
Vinh Huynh
26.2.2018

## Slide 2: Introduction
Scope of the presentation:
Nordic power market challenges
Nordic balancing market
Types of frequency reserves
Fingrid’s reserve power plants
Explain the key terms:
Nordic energy market: Finland, Sweden, Norway & Denmark
TSO: transmission system operator

## Slide 3: 1. Nordic Power System - Main Challenges
Balancing the system: Production = consumption
System flexibility: RES, new connections to Cont.Europe
Security of supply: Generation & transmission adequacy
Frequency quality: Frequency = 50Hz
https://www.entsoe.eu/Documents/Publications/SOC/Nordic/System_Operation_Forum_011216_Stockholm_presentations.pdf
 Need for a solution to balance the system and maintain power quality!
Notes: factors that may disturb this balance, such as weather-related fluctuations in consumption, short-term changes in major industrial consumption, breakdowns in production facilities or power line outages or other grid component breakdowns. To be able to handle such unforeseen events, it is essential that there are sufficient reserves in the power system.

## Slide 4: 2. Nordic Balancing Market
Reserve
Market

## Slide 5: 3. Frequency Containment Reserves
Frequency Containment Reserve for Normal operation (FCR-N): constantly maintained for the frequency regulation of the normal state.
Frequency Containment Reserve for Disturbances (FCR-D): maintained to the extent that the power system can withstand.
 | Minimum size MW | Frequency change f | Activation time
FCR-N | 0,1 MW | ± 0,1 Hz | 3 min
FCR-D | 1 MW | under 49,9 Hz | 5 s / 50 % 30 s / 100 %

## Slide 6: 4. Frequency Restoration Reserves
Automatic Frequency Restoration Reserve (aFRR): aims to restore the frequency to 50 Hz in response to TSO’s signal.
Manual Frequency Restoration Reserve (mFRR): to cover the imbalances (MW) in TSO’s own area.
 | Minimum size MW | Activation time
aFRR | 5 MW | 2 min
mFRR | 10 MW | 15 min

## Slide 7: 5. FCR & FRR – Fingrid illustration
https://www.youtube.com/watch?time_continue=170&v=D51AVy5wByM
Notes: Momentary imbalances are initially regulated by primary regulation. If the imbalance continues for several minutes, secondary regulation will take over, thus freeing up primary regulation resources for regulation of new imbalances. Both primary and secondary reserves are activated automatically due to changes in the grid frequency. If further regulation is necessary, tertiary regulation (regulating power) will be activated which, correspondingly, will make secondary regulating resources available. Tertiary regulation is activated manually by the Nordic system operators.

## Slide 8: 6. Reserve power plants - Fingrid
Fingrid meets its mFRR obligation with own and leasing reserve power plants, which are not used for commercial electricity production.
https://www.fingrid.fi/en/electricity-market/reserves_and_balancing/reserve-power-plants/
 | Fingrid | Nordic
FCR-N | 140 MW | 600 MW
FCR-D | 220-265 MW | 1200 MW
aFRR | 70 MW | 300 MW
mFRR | 800-1100 MW | 

## Slide 9: Conclusions
Sufficient reserves are essential to handle unforeseen events in the Nordic power system
Frequency Containment Reserves (FCR): stabilize frequency
Frequency Restoration Reserves (FRR): return the frequency to its normal range (50Hz) and to release activated FCRs back into use.

## Slide 10: Source material used
Khartchenko, N., 2013. ‘Advanced Energy Systems’. 2nd ed. United States of America: CRC Press.
Fingrid. 2018. Market places. [ONLINE] Available at: https://www.fingrid.fi/en/electricity-market/demand-side-management/market-places/. [Accessed 26 February 2018].
Fingrid. 2018. Reserves and balancing power. [ONLINE] Available at: https://www.fingrid.fi/en/electricity-market/reserves_and_balancing/. [Accessed 26 February 2018].
Ek E. 2016. Nordic System Operation Forum. [ONLINE] Available at: https://www.entsoe.eu/Documents/Publications/SOC/Nordic/System_Operation_Forum_011216_Stockholm_presentations.pdf. [Accessed 26 February 2018].

## Slide 11: Questions….?
Thank you!