## Slide 1: ELEC-E8423 - Smart Grid Technical solutions in Micro Grids
Jani Sormunen
Daniel Lindberg
´17.04.2018

## Slide 2: Introduction
What is microgrid?
Lasseter: ”a system approach which views generation and associated loads as a subsystem”
Schwaegerl: “an integration platform for supply-side (micro-generators) and demand-side resources (storage units and controllable loads) located in a local distribution grid”
Laaksonen: “a part of a distribution network which has islanding capability and reduces outages so that the microgrid works as a part of future self-healing smart grids” [1]
Why microgrids?
  The amount of distributed renewable energy sources has increased in order to reduce greenhouse gas emissions
  Integration of microgrids can help balance the power in electricity grid and increase reliability and power quality while decreasing distribution losses
There are many different types of technical solutions to microgrids
Notes: So, what is a microgrid? There is no exact definition for micro grids but here is some examples how it is defined in different sources. Lasseter's definition is that the microgrid is "a system approach which views generation and associated loads as a subsystem", which is very broad view for microgrids.
Schwaegerl’s definition is that the microgrid is “an integration platform for supply-side (micro-generators) and demand-side resources (storage units and controllable loads) located in a local distribution grid”, this is slightly more accurate definition.
Laaksonen has added to these previous definitions that the microgrid is “a part of a distribution network which has islanding capability and reduces outages so that the microgrid works as a part of future self-healing smart grids”
As you can see, the definitions vary a little bit, but basically, microgrid is small part of distribution network that is capable of operating by itself or as part of the main grid. Microgrids also do not have specific size restrictions, meaning there are no minimum or maximum sizes.
So why microgrids should come part of the future distribution systems? Because the amount of distributed renewable energy sources, like solar and wind, has increased in order to reduce greenhouse gas emissions. This means that the power system is changing so that the generation does not come anymore from one single power plant, but instead of multiple generation units. These changes and the distributed energy sources enable microgrids. And they also need microgrid to work effectively.
Microgrids can also help in balancing the supply and the demand. Also, they can increase reliability of grid and decrease power losses in lines because transmission distances are shorter.
There are many ways to implement microgrids and next I will tell you more about those.

## Slide 3: Components of a microgrid
Distributed Energy Resources (DER)
  Distributed generation (DG)
  Storage systems
  Active loads
Point of Common Coupling (PCC)
  Link that connects the microgrid to the main grid
Physical network
Monitoring, communication and control system
  Enables demand response and proactive management of the system
[2]
Notes: First, we are going to take a look at the basic components of a microgrid. In that picture you can see those basic components of microgrid. It consists of distributed energy resources which includes distributed generation, storage systems and active loads. More information is coming in next slide.
Also point of common coupling plays major role in microgrids because it provides connection to main grid or with that microgrid can disconnect with main grid and then the microgrid can work in island mode.
Physical network provides connection between those distributed energy resources. I will tell you more about network implementation in following slides.
Monitoring, communication and control systems enables demand response and proactive management of microgrid.

## Slide 4: Distributed energy resources
Distributed generation
  Includes multiple small units, mostly renewable energy sources
  Most commonly used sources are PV, wind and micro-hydro
  Can also include non-renewables like diesel generators
Storage systems
  Balance power demand and generation
  Incerease stability, power quality and reliability of supply
  Main technologies are different batteries, TES, PHS, CAES and EV
Active loads
  Active loads have similar objectives as the storage systems
  Increases or decreases the amount of load based on production
Notes: Distributed energy recourses consist of distributed generation, storage systems and active loads. As mentioned before, distributed generation includes multiple small units, mostly renewable energy sources. Most commonly used are PV, wind and micro-hydro. Also some non-renewables are used like for example diesel generators which provides fast energy recourses when sun is not shining or wind is not blowing.
Storage systems is for balancing power demand and generation, as surplus energy can be stored and then used later when consumption is higher than generation. And with those the stability, power quality and reliability can be increased. Main technologies are different batteries, Thermal Energy Storage (TES), Pumped Hydro Storage (PHS), Compressed Air Energy Storage (CAES) and Electric Vehicles (EV).
And then we have loads, which are the components that consume the generated electricity. Active loads have similar objectives as the storage systems. So it is for balancing power demand and generation by increasing or decreasing the amount of load.

## Slide 5: Network
Overhead / underground cables
Different grid configurations: radial ring mesh
Distribution networks can be
  DC line
    No need to control frequency or reactive power, which leads to better power quality
    Length of grid can be longer since there is less losses
  50 Hz AC line
    Easier to connect to utility grid and adjust the voltage level
    More loads are usually operated in AC
  High frequency AC line
    New concept still under development
    Can reduce ripple current and filter harmonics
Different grid configurations [1]
[2]
Notes: Network of microgrid can consist of overhead lines or underground cables like any other network system.
Different grid configurations are also familiar from transmission or distribution networks. So, the grid can be radial, ring or mesh.
Energy transmission between different distributed energy recourses can be use DC or AC technology, both have their own advantages.
When the DC technology is used there is no need to control frequency or reactive power, so the power quality is better. Also, length of grid can be longer when the DC technology is used.
When the 50 Hz AC technology is used the microgrid is easier connect to utility grid and the voltage levels in microgrid is also easier to adjust. Also, most of the loads are operated with AC voltage, so rectifiers are not needed.
High frequency AC lines is new concept and still under development, so there is no real-life examples is it working technique for microgrids. With this technic ripple currents can be reduced, and harmonics can be filtered.

## Slide 6: Monitoring, Communication and Control
Monitoring and communication systems are important for power control and protection
Supervisory Control And Data Acquisition (SCADA) software and smart meters are essential for controlling and balancing of the system
Requires digital protective relays and circuit breakers to detect, isolate and repair faults
Enables demand side management, for example load shedding, and optimisation of the production as well as minimising operating costs
Communication and control network [3]

## Slide 7: Example cases
The Sendai Microgrid, Japan
First constructed as 4-year demonstration project from 2004 to 2007
Electricity is generated using
  2 x 350 kW natural gas engines
  50 kW of PV generation
  250 kW fuel cell
It is Multiple Power Quality Microgrid (MPQM)
  Loads are grouped into different categories based on power quality
Performed well during 2011 tsunami and earthquake
  Service loss of only few hours
Huatacondo, Chile
Microgrid project in Andes Mountains community of 150 residents
Electricity is generated using
  150 kW diesel generator
  22 kW tracking solar PV system
  3 kW wind turbine
Also includes 170 kWh battery
Has implemented Social SCADA for monitoring and controlling the system
  Helps the community to participate in decision making and maintenance
Notes: Technical feature MPQM: Class A, B1, B2, B3, DC, Normal
SCADA = Supervisory Control And Data Acquistion, gathers and analyzes the data
Social SCADA, where goal is to easily present information to users without technical background

## Slide 8: Current barriers
Technological issues
  Caused by multi-component configuration
  Can affect the durability and efficiency of different generation or storage units. Functionality of control and communication software may also suffer
Dual-mode operation
  Is the ability to function as part of the main grid and in island mode
  There are challenges when transitioning from one mode to another
  Grid-connected mode  Island mode
    Black start or seamless transition
  Island mode  Grid-connected mode
    Transition can cause mismatches between generation and load
Power and frequency control
  Intermittent DG power and frequent load switching cause problems in power and frequency control
Protection and safety
  Major issue is in island operation, because fault currents are so small that traditional protection techniques fail to detect them
Notes: Many components, there can be challenges to specific elements, which can then affect the whole microgrid. For example leaking coolant fluid
Black start allows a short period of outage, or seamless transition which can be difficult to achieve. Problems with energy reliability
Re-synhronizing the two grids is about choosing the right moment and usually leads to mismatches
DSO has to maintain freq and vol to ensure stable power. Issues that we have with all grids, not just microgrids

## Slide 9: Conclusions
Microgrid is a part of distribution network that is also capable of functioning independently without being connected to the main grid
Main components of microgrid are DER, PCC, network and monitoring/control system
While microgrids can have huge benefits in the future, there are still many issues that need to be solved
Notes: DER = Distributed Energy Rsources = Distributed generation + storage + active load
PCC = Point of Common Coupling

## Slide 10: Source material used
[1] Soshinskaya, Mariya, et al. "Microgrids: Experiences, barriers and success factors." Renewable and Sustainable Energy Reviews 40 (2014): 659-672.
[2] Mariam, Lubna, Malabika Basu, and Michael F. Conlon. "Microgrid: Architecture, policy and future trends." Renewable and Sustainable Energy Reviews 64 (2016): 477-489.
[3] Hatziargyriou, Nikos, et al. "Microgrids." IEEE power and energy magazine 5.4 (2007): 78-94.
[4] Planas, Estefanía, et al. "AC and DC technology in microgrids: A review." Renewable and Sustainable Energy Reviews 43 (2015): 726-749.
[5] Basak, Prasenjit, et al. "A literature review on integration of distributed energy resources in the perspective of control, protection and stability of microgrid." Renewable and Sustainable Energy Reviews 16.8 (2012): 5545-5556.
[6] Salam, A. A., A. Mohamed, and M. A. Hannan. "Technical challenges on microgrids." ARPN Journal of engineering and applied sciences 3.6 (2008): 64-69.
[7] Llaria, Alvaro, et al. "Survey on Microgrids: analysis of technical limitations to carry out new solutions." Power Electronics and Applications, 2009. EPE'09. 13th European Conference on. IEEE, 2009.