## Slide 1: ELEC-E8423 - Smart Grid Demand response of commercial loads
Pekka Holopainen
Juha Korpio
13.03.2018

## Slide 2: Introduction
  The aim of this presentation is to present different aspects specific for demand response (DR) implementation in commercial sector
    Commercial buildings
    Flexible commercial loads
    Control
    ADRALOC System
    Conclusion
FERC defines DR as “Changes in electric usage by demand side resources from their normal consumption patterns in response to changes in the price of electricity over time, or to incentive payments designed to induce lower electricity use at times of high wholesale market prices or when system reliability is jeopardized”

## Slide 3: Commercial buildings
  Demand response potential of commercial buildings
    Commercial buildings account on average for 45% of summer electric peak coincident demand in the US
    Building automation systems used for demand response can reduce peak load by 10-15%
    In Finland peak hours are in winter and commercial sector accounts for around 20% of the electricity consumption
  Commercial buildings are good providers of demand response
    Building automation controls HVAC, cooling and other electrical loads
    Predictable loads operating on repeating schedules
Kiliccote et al, 2006

## Slide 4: Flexible commercial loads
  Cooling, Cold storages, Lighting, Thermal and electrical storages, EV charging, non-critical server applications, elevator cycling…
  HVAC
    Up to 15 % of the HVAC’s rated power can be used without significant effects on room temperature
      Pump and fan variable frequency drive limits
      Cooling valve limit, etc.
  Shifting load to backup generation
    Emergency backup generators could be used in peak hours if market prices make it an attractive option
Hao et al, 2012

## Slide 5: Example of an Automated Demand Response Event
Source: http://www.buildingefficiencyinitiative.org/resources/scaling-demand-response-presentation

## Slide 6: Control
Control signals could be presented by TSO, DSO, other balance responsible party or an aggregator e.g. through Virtual power plant (VPP)
  Price-based control (based on contracts)
    Relies on customer changing their electricity consumption in response to time-varying pricing mechanism such as time of use, critical peak and real time pricing
  Transaction based control (market-based control)
    Control that uses marked mechanisms to engage self-interested responsive loads
    Could increase the peak consumption in some cases (This effect could be limited with added price-based control of peak consumption)
  Direct load control (DLC)
    Allows utilities or system operators to remotely control specific electric loads during peak demand periods and critical events
    Could be used for regulating power and reserve markets (frequency regulation)
Hao et al, 2017

## Slide 7: ADRALOC system
  Project done by research group of University of Southern Denmark, Center for Energy Informatics (2016)
  Goal was to present better system for demand response in commercial buildings to enable a higher penetration of smart grid solutions
  The system is designed to enable commercial buildings to provide Automated DR services with Assessable impact on the Load change and Occupant Comfort (ADRALOC)
  Prototype tested with the real office building in Vejle, Denmark
  It can manage both direct and indirect control of loads requested
  System integrates prediction of load consumption, occupant behavior and indoor environmental properties to assess the impact of DR events
Mikkel et al, 2016

## Slide 8: ADRALOC system
DSO/aggregator make a DR service request
Collects relevant sensor data from the building automation and external sources
The data informs a number of models that predict different aspects for the time period of the requested DR event
Looks at the type of DR request and analyzes if the building can respond to the event or not based on model predictions, comfort requirements, national building and work regulations etc.
Schedule the building infrastructures to deliver the requested response
Electricity consumption pattern changes in the requested period
Mikkel et al, 2016

## Slide 9: Conclusions
  Commercial sector is interesting target for demand response implementation
  The potential for demand response depends largely on the building where DR is integrated
    Purpose, smartness of the automation and age of the building
    Biggest challenge is how to integrate effectively different automation systems to VPPs
    DR integration planning has to be made separately for each building according to it’s specific features
  HVAC and lighting are the most important loads in commercial sector, other potential loads are e.g. EV charging (becoming more general)

## Slide 10: Source material used
  Suomen virallinen tilasto (SVT): Energian hankinta ja kulutus [online]. ISSN=1799-795X. 2016, Liitekuvio 6. Sähkönkulutus sektoreittain 1970–2016 . Helsinki: Tilastokeskus [referred to: 9.3.2018].
  Hao, He & Middelkoop, Timothy & Barooah, P & Meyn, Sean. (2012). How Demand Response from Commercial Buildings can Provide the Regulation Needs of the Grid. 2012 50th Annual Allerton Conference on Communication, Control, and Computing, Allerton 2012.
  Hao, He & Corbin, Charles D. & Kalsi, Karanjit & Pratt, Robert G. (2017). Transactive Control of Commercial Buildings for Demand Response. IEEE transactions on power systems, vol. 32, no.1.
  Mikkel Baun, Kjærgaard & Krzysztof, Arendt & Anders, Clausen & Aslak, Johansen & Muhyiddine, Jradi & Bo Nørregaard, Jørgensen & Peter, Nelleman & Fisayo Caleb, Sangogboye & Christian, Veje & Morten, Gill Wollsen. (2016). Demand Response in Commercial Buildings with an Assessable Impact on Occupant Comfort. IEEE International Conference on Smart Grid Communications 2016
  The Federal Energy Regulatory Comission FERC [online]. 2017. ”http://www.ferc.gov/industries/electric/indus-act/demand-response/dem-res-adv-metering.asp.” [referred to: 11.3.2018].