## Slide 1: ELEC-E8423 - Smart Grid Pumped hydro energy storages
Jaakko Anttila
Filip Reiskup
24.04.2018

## Slide 2: Introduction
Mechanical energy storage system
Discharge time: hours – a few days
Response time: seconds to minutes
Plant sizes: 100 – 3000 MW
Efficiency: 70 – 85 %
165 GW of total installed capacity
About 96 % of all storage capacity
3 % of global generation capacity

## Slide 3: Applications
Load leveling: night time production to peak hours
Energy balancing: draining excessive renewable production to use it in times of low production
Non-spinning reserve

## Slide 4: Bath County Pumped Storage Station
The largest operational pumped storage plant since 1985
Located in Virginia, United States
Rated power: 3 GW
Storage capacity: 31 GWh
Powers 750000 homes
Construction cost: US$1.6 billion

## Slide 5: Ocean renewable storage storage
Sea as an upper reservoir
Usage of pressure at the sea bottom
Power is needed → Water flows in
Surplus → Water is pumped out

## Slide 6: Ocean renewable storage storage
Combination with offshore wind farms
Diameter of the sphere 25 – 30 m
Depth 200 – 700 m
Construction and equipment costs: 1200 – 1500 €/kW
For commercial use connection of >80 tanks
Cmax [MWh] |  | 
Depth [m] | 25 m Di | 30 m Di
150 | 2,3 | 3,97
300 | 4,6 | 7,94
400 | 6,13 | 10,59
500 | 7,66 | 13,24
600 | 9,19 | 15,89
700 | 10,73 | 18,53
750 | 11,49 | 19,86

## Slide 7: Advanced variations
Effectiveness can be improved by having adjustable capacity
Achievable with wicket gates and by-pass configurations

## Slide 8: Sub-surface pumped hydroelectric storage
One or both reservoirs below ground (sub-surface)
Allows storing (and producing) large amounts of energy in flat regions
Abandoned mines, caverns, and man-made storage reservoirs are seen as potential project reservoir options
Underground excavation or materials-handling costs, construction risk, and time required for underground excavation and construction could make the economics of such a project difficult
Utilization of existing subsurface structures or minimize/offset underground costs
UPSH plants interact with the surrounding porous media exchanging water
In Pyhäjärvi has been used deepest metal mine in Europe (530 MWh)

## Slide 9: Conclusions
Advantages
A mature technology with long lifetime
Helps to integrate renewables into power system
Offers large emergency reserves
Disadvantages
Heavily dependent on location
Large land use
Environmental issues
Investment costs

## Slide 10: Source material used
Electrical Energy Storage: IEC. Geneva, 2011. Link: http://www.iec.ch/whitepaper/pdf/iecWP-energystorage-LR-en.pdf
Data visualization. DOE Global energy database [online]. Sandia Corporation, 2018 [cit. 2018-04-23]. Link: https://www.energystorageexchange.org/projects/data_visualization
U.S. Grid Energy storage factsheet. Center for sustainable system [online]. Michigan, 2017 [cit. 2018-04-23]. Link: http://css.umich.edu/factsheets/us-grid-energy-storage-factsheet
400 MW pumped storage hydro plan approved. Civil engineer [online]. Webvision, 2017 [cit. 2018-04-23]. Link: https://www.newcivilengineer.com/latest/400mw-pumped-storage-hydro-plan-approved/10015321.article
Bath county pumped storage station. Dominion Energy [online]. Dominion Energy, 2018 [cit. 2018-04-23]. Link: https://www.dominionenergy.com/about-us/making-energy/renewables/water/bath-county-pumped-storage-station
Ocean Renewable Energy Storage (ORES), DOI: 10.1109/JPROC.2013.2242411.
Pumped hydro storage plants with improved operational flexibility using constant speed Francis runners DOI: 10.1016/j.apenergy.2014.09.065.
Sub-surface pumped hydro storage. Energy storage association [online]. 2018 [cit. 2018-04-23]. Link: http://energystorage.org/energy-storage/technologies/sub-surface-pumped-hydroelectric-storage
Energy and Innovation Awards. Energy week [online]. Vaasa: EnergyVaasa, 2018 [cit. 2018-04-23]. Link: https://www.energyweek.fi/awards/