## Slide 1: ELEC-E8423 - Smart Grid Communication solutions for Smart Grid
Rajeetharan Sanchayan Manohar Bayyapu Reddy
10.04.2018
ELEC-E8423 - Smart Grid

## Slide 2: Introduction
An electric grid without adequate communications is simply a power distributor.
Inclusion of two-way communications that the power grid is made "smart“.
Presentation overview:
  Smart grid conceptual model and SGAM framework
  Smart grid communications architecture
  Communication technologies invloved
  Challenges & standards
  Conclusions
ELEC-E8423 - Smart Grid

## Slide 3: Conceptual model and SGAM framework for smart grid
ELEC-E8423 - Smart Grid
EU model is similar to NIST model with addition to DER
Discovers various smart grid stakeholders and also different electrical and communication interfaces
SGAM – Smart Grid Architecture Model
NIST – National Institute of Standards and Technology
Figure: Smart Grid Conceptual Model (EU)
Figure: SGAM frame work

## Slide 4: Smart grid communications architecture
ELEC-E8423 - Smart Grid
Smart grid communications network is divided into many network areas.
Smart grid end-to-end communication architecture have different domains: end-user premises, transmission grids and distribution grids and generation.

## Slide 5: Customer premises network
Customer premises network consists of big industries, small and medium business, office buildings, smart buildings and standard home users.
Due to different nature of sites, these sites are further grouped as HAN, BAN and IAN
Fig: Basic network architecture
HAN provides communications between household appliances (capable of sending & receiving signals) and smart meter, in-home displays (IHDs) and/or home energy management (HEM) systems. This facilitates controlling and managing loads and providing total electricity costs.
BAN & IAN used for commercial and industrial customers with help in building automation, HVAC, heating, ventilation and other energy management applications.
This network is connected to other parts of the network in SG via smart meter and internet gateway.
Supported Communication technologies:
Wired: PLC, Ethernet
Wireless: Bluetooth, Zigbee, Wifi, Mesh
Application | Facilitation by communication | Data (bytes) | Latency (sec) | Rel. (%)
Home automation Building automation | Bi-directional communication in home, industry and business areas | 10-100 >100 | <60 | >98

## Slide 6: Communications network in distribution grid (1)
The communications network area applies to distribution grid are NAN and FAN.
NAN/FAN networks supports information flow between WAN and consumer premises network.
Smart grid applications in NAN & FAN are
  Commercial: Meter reading, prepayment, TOU/RTP/CPP pricing, customer info and messaging
  Technical: Distribution automation (DA), Demand response (DR), electric transportation, firmware updates, program/configuration update, outage management, service switch operation, premises network administration
The data rates and coverage distance requirements for these applications are higher than premises area networks. And the exact requirements for each application are different.
Application | Facilitation by communication | Data (bytes) | Latency (sec) | Rel. (%)
Meter reading | Enables bi-directional communication between meter and centralized management site with AMI | 100-2400 | <15 | >98-99.5
Pricing | Broadcasting price information to meters and devices for customers with TOU (time of use), RTP (real time pricing) and CPP (critical peak pricing) | 100 | <60 | >98
Prepayment | Allows customer to buy services in advance. Not required to use separate prepaid meters. | 50-150 | <30 | >98
Supported Communication technologies:
Wired: DSL, Coaxial, PLC, Ethernet
Wireless: Zigbee, Wifi Mesh, WiMAX, Cellular

## Slide 7: Communications network in distribution grid (2)
Application | Facilitation by communication | Data (bytes) | Latency (sec) | Rel. (%)
Demand response (DR) | Enables utility to talk with devices at customer premises and reducing the load during peak demand periods. Direct load control can turn ON/OFF the selected devices by the utility. | 100 | <60 | >99.5
Service switch operation | Facilitates to switch the service without rolling a service man and vehicles from the utility end. Reduces service time and expenses involved in it. | 25 | <60 | >98
Distribution automation | Gives real time information of grid structure, automation, control, data communication and info management, monitor of distribution grid. | 100-1000 | <4 | >99.5
Outage management | To detect the outage immediately and reporting over & under voltage scenarios. | 25 | <20 | >98
Customer storage | Enables efficient integration of distributed renewable systems and battery systems. | 25 | <5 | >99.5
Electric transportation | Involves both way electricity between Vehicle and grid. Acquiring knowledge of battery charge state by the utility. | 255 | <15 | >98
Firmware updates | Utilities will upgrade firmware, security updates and configurations of their remote devices at the user premises. | 400k-2000k | <120 | >98
Customer info and messaging | Access to account information, consumption data and outage info by the user. These applications provided by utility/3rd party. | 50-200 | <15 | >99
Premises network management | Allow users to connect or disconnect premises network equipment to/from network using IVR or web portal. | 25 | <20 | >98

## Slide 8: Communications network in transmission grid
The communications network area applies to transmission grid is WAN.
Aids to avoid cascading outages with real-time information related to the power grid state.
Provides high data resolution and shorter response time then SCADA and EMS.
The three domains in WAN applications are
  Wide-area protection, Wide-area control and Wide-area monitoring
Application | Facilitation by communication | Other information | Data (bytes) | Latency (sec) | Rel. (%)
Wide-area protection | Facilitates fully automatic protection for protecting power system against blackouts, congestion in transmission and stressed conditions or unexpected events. Involves load-shedding, adaptive islanding and quick reaction to faults. | Typical communication protocols used MIRRORED BITS, IEC 61850 GOOSE and ETHER-CAT communications | 4-157 | <0.1 | >99.9
Wide-area control | Provides automatic self-healing intelligence with the platform to operate rapid generator tripping and reactive power compensation switching. Contains HVDC and FACTS devices. Also includes damping control, voltage and frequency stability control. |  | 4-157 | <0.1 | >99.9
Wide-area monitoring | Enables providing the real-time system data captured from IEDs and PMUs. Helps in power grid opportunities to improve voltage stability and frequency oscillations detection. | Information obtained from power system by IEEE C37.118 | >52 | <0.1 | >99.9
Supported Communication technologies:
Wired: Fibre optic; Wireless: WiMax & Cellular

## Slide 9: Communication technologies comparison
ELEC-E8423 - Smart Grid

## Slide 10: Mapping of communication networks on SGAM communication layer
ELEC-E8423 - Smart Grid

## Slide 11: Challenges and standards
Challenges
  Lack of required interoperability standards.
  The technology of existing communication networks in power grid are decade-old.
  Meeting the latency requirements for mission critical applications majorly in WAN.
  Concerns related to cyber security and data privacy.
  Meeting the requirements of various emerging models in the grid.
Standards
  IEEE P2030 - Guide for Smart Grid Interoperability of Energy Technology and Information Technology Operation with the Electric Power System (EPS), and End-Use Applications and Loads
  IEEE P1901 - Standard for high speed communication devices via electric power lines, often called broadband over power lines (BPL)
  IEC 62351 - Power systems management and associated information exchange - Data and communications security
  IEC 62056 - Electricity metering data exchange
  PLC G3 - Powerline communications standard that will enable the smart grid vision
  IEC 61850 - Communication networks and systems for power utility automation
  All the standards required for smart grid communications in various applications and domains can be traced from IEC webstore - http://smartgridstandardsmap.com/
ELEC-E8423 - Smart Grid

## Slide 12: Conclusions
Interoperability is a key element in smart grid and this can be achived by communications systems.
The communications network system is divided into three major parts according to the location and requirements.
One has to select the required communication technologies (among various available wired and wireless) based on the application requirements.
Interoperability is still a major challenge and extentensive research required.

## Slide 13: Source material used
MARKET OPPORTUNITIES IN THESMARTGRIDSECTORIN FINLAND 2016 , https://www.investinfinland.fi/documents/162753/197730/White+Paper+Smart+Grid/880e1f5b-a78f-4294-bfed-a8037cfa0a9c
ENISA, “Communication network interdependencies in smart grids”, 2015
CEN-CENELEC-ETSI Smart Grid Coordination Group, “CEN-CENELEC-ETSI Smart Grid Coordination Group Smart Grid Reference Architecture”, 2012
J. Mandic-Lukic, B. Milinkovic and N. Simic, "Communication solutions for smart grids, smart cities and smart buildings," Mediterranean Conference on Power Generation, Transmission, Distribution and Energy Conversion (MedPower 2016), Belgrade, 2016, pp. 1-7. doi: 10.1049/cp.2016.1109
Murat Kuzlu, Manisa Pipattanasomporn, Saifur Rahman, “Communication network requirements for major smart grid applications in HAN, NAN and WAN, Computer Networks”, Volume 67, 2014, Pages 74-88, ISSN 1389-1286, https://doi.org/10.1016/j.comnet.2014.03.029.
D. Baimel, S. Tapuchi and N. Baimel, "Smart grid communication technologies- overview, research challenges and opportunities," 2016 International Symposium on Power Electronics, Electrical Drives, Automation and Motion (SPEEDAM), Anacapri, 2016, pp. 116-120. doi: 10.1109/SPEEDAM.2016.7526014