## Slide 1: ELEC-E8423 - Smart Grid Power Quality Issues in Smart Grid
Marius Baranauskas
Suvi Takala
17.04.2018

## Slide 2: What is power quality?
Power quality
Regulations according to SFS-EN-50160
Power frequency
Voltage mag.
variations
Short voltage interruptions
Rapid voltage changes
Supply voltage dips
Long voltage interruptions
Temporary freq overvoltages
Transient overvoltages
Harmonic voltage
Voltage unbalance
Interharmonic voltage
Notes: Electrical energy is a product and, like any other product, should satisfy the proper quality requirements. Electric power quality, or simply power quality, involves voltage, frequency, and waveform. Good power quality can be defined as a steady supply voltage that stays within the prescribed range
If electrical equipment is to operate correctly, it requires electrical energy to be supplied at a voltage that is within a specified range around the rated value. A significant part of the equipment in use today, especially electronic and computer devices, requires good power quality (PQ)
joint responsibility for the supplier and the electricity user.

## Slide 3
Notes: More DG e.g. in LV network: grid must operate in two directions, some consumers are becoming prosumers
Customer loads will incorporate power electronics for higher efficiency, may cause emissions that weaken PQ, electronics demand a steady voltage and frequency
Reactive power: some devices e.g. LED lamps generate more reactive power than before, in case of too much reactive power, DSO have to consume it in e.g. reactors to maintain balance; and in case of too little reactive power, DSO have to produce it with condensators
Cyber attack: problems with communication may cause disturbances, reduce power quality and in worst case result in long interruptions
E.g. powerline communication (if used) may cause disturbances and interfere with radio frequencies (e.g. radio amateurs concerned)
On the other hand, smart grids create a possibility to reduce the duration of interruptions

## Slide 4: Voltage Quality
Notes: Issues in smart grids are usually related to voltage, imbalance and harmonics. Now we have a closer look at voltage;
why voltage quality is becoming increasingly important
modern electrical devices emit disturbances to grid
devices are more sensitive to voltage quality fluctuations and problems than before (e.g. operation disturbed, efficiency reduced), electronics demand steady voltage & frequency

## Slide 5: Solutions
Notes: How to overcome quality issues in SG? At first, a general look to the issue. Smart grids use higher share of intermittent renewable distributed generation,
and less fossil-fuel based conventional generation, may cause problems but with measurements, reserve power, data analysis and communication (devices, grid) those can be avoided
bidirectional: meter measures flow of electricity in two directions, how much kWh delivered from electric company, and also difference between generators production and customers load demand, how much kWh received

## Slide 6: PQ monitoring
Multilevel monitoring approach
Selection of monitoring locations and selection of equipment
Communication links and protocols
Storage and analysis of data
Notes: With the manifold increase in the distribution systems, the Power Quality (PQ) monitoring is becoming an important aspect for distribution network operators. Today, compliance of supply voltage with actual standards is rarely controlled and measured in the LV networks. Verification of product quality compliance for a large number of customers becomes more and more important with the advent of future smart grids. Close link between PQ measurements and network control is an essential requirement for an improved operation of future grids
The first step is to define the objective(s) of the Power Quality (PQ) monitoring. The second step is the conceptual phase, which has to cover a lot of aspects, like selection of locations, selection of monitors, transfer storage and processing of data and analysis and reporting of results
Generally, the selection of locations for PQ monitoring depends on utility’s objectives, the architecture of the power system, the length of the monitoring period and cost related issues. The location of monitoring equipment strongly depends on the detailed goals
fixed/mobile monitors
A powerful and cost-effective PQ system requires effective communication links, smart systems able to communicate with devices in order to download information and verify their availability, as well as robust information systems for gathering and analyzing data with minimal human intervention. The more robust communication links are, the better reliability will be achieved and the less corrective maintenance will be required. It is also recommended to oversize communication requirements
As a monitoring system grows, data storage and handling become more and more problematic. Highly aggregated indices are stored centralized, while the detailed data remains in the instrument itself (circular buffers) or a concentrator. Cloud computing
The ability of smart meters for bi directional communication of data enables the ability to collect information regarding the electricity fed back to the power grid from customer premises
http://cired.net/publications/cired2015/papers/CIRED2015_0115_final.pdf

## Slide 7: Conclusions

## Slide 8: Source material used
European Commission. Electromagnetic Compatibility (EMC) Directive. Available: http://ec.europa.eu/growth/sectors/electrical-engineering/emc-directive_fi Accessed: 15.4.2018
Finnish Standards Association SFS. (2010) Voltage characteristics of electricity supplied by public electricity networks. European Standard, SFS-EN 50160. 4. edition, 63 pp.
Bollen, M.H.J. et al. (2010) Power Quality aspects of Smart Grids. Internation Conference on Renewable Energies and Power Quality RE&PJ, vol 1, no 8. Available: http://www.icrepq.com/icrepq'10/583-Bollen.pdf Accessed 15.4.2018
Janjic, A; Stajic Z; Radovic I. (2011) Power Quality Requirements for the Smart Grid Design. International Journal of Circuits, Systems and Signal Processing, Issue 6, vol. 5. Available: http://www.naun.org/main/NAUN/circuitssystemssignal/17-290.pdf Accessed 15.4.2018
Maheswaran, D; Selvaraj, V; Paul Manjaly, D. (2015) Power Quality Monitoring Systems for Future Smart Grids. CIRED, 23rd International Conference on Electricity Distribution, paper 0115. Available: http://cired.net/publications/cired2015/papers/CIRED2015_0115_final.pdf Accessed: 15.4.2018
Pandaya, R.R; Bhavsar, F. (2018) An Overview on Power Quality Issues In Smart Grid. IOSR Journal of Electrical and Electronics Engineering (IOSR-JEEE), Issue 1, vol. 13. Available: http://www.iosrjournals.org/iosr-jeee/Papers/Vol13%20Issue%201/Version-1/A1301010104.pdf Accessed: 15.4.2018
Prathibha E., Manjunath A. (2014) An Overview of Power Quality Issues in Smart Grid. International Journal of Innovative Research in Advanced Engineering (IJIRAE). Issue 10, vol. 1. Available: http://www.ijirae.com/volumes/vol1/issue10/48.NVEE10084.pdf. Accessed 15.4.2018