## Slide 1
ELEC-E8423 - Smart Grid Demand response of HVAC loads
Marco Vivian, Trung Nguyen
13.03.2018

## Slide 2
Benefits of utilizing DR in HVAC load management
HVAC DR Potential for Up/Down Ramping
HVAC Load Management for Energy Cost Minimization
HVAC Load Management with Wind Energy Integration
Sensitivity Analysis of Wind Generation Balancing
Conclusions
Introduction
13.03.2018
Page 2
All simulations & optimizations were performed with different scopes and settings for households in Finnish conditions.
Demand Response of HVAC Loads

## Slide 3
Highest share in household demand
Large-scale implementation of AMR
Automated by BEMS
Reduce the energy cost of the buildings
Reduce peak energy consumption
Reduce energy production in the grid
Stabilize energy grid
Promote smart grid
Enhance efficiency and reliability of the system
Why HVAC demand response?
Page 3
Demand Response of HVAC Loads
13.03.2018

## Slide 4
Winter case study
HVAC DR Potential for Up/Down Ramping
Page 4
Utilize thermal inertia
The more flexible the customer, the higher the potential of DR
Demand Response of HVAC Loads
13.03.2018

## Slide 5
HVAC DR Potential for Up/Down Ramping
Page 5
Storage can be used as power sink
Full storage allows electrical supply interruption up to 12 hours
Higher potential in spring due to lower heat demand
Demand Response of HVAC Loads
13.03.2018

## Slide 6
HVAC Load Management for Energy Cost Minimization
Page 6
Larger storages = more flexible in responding to price variations
Partial storages operate close to and between extreme limits
Demand Response of HVAC Loads
13.03.2018
40% storage
10% storage

## Slide 7
HVAC Load Management for Wind Generation Balancing
Page 7
Six 50kW wind turbines, storage capacity at 50% of total daily demand
Users can set temperature preferences & thermal comfort deviation [0, 1]
Least deviation in case 3 (4 times better than case 2)
Case 1
Case 2
Case 3
Demand Response of HVAC Loads
13.03.2018

## Slide 8
Sensitivity Analysis of Wind Generation Balancing
Page 8
Deviation decreases as customers’ flexibility level increases
Larger differences between scenarios in case 2
Bigger = better
Small differences between 30% & 40% scenarios
Demand Response of HVAC Loads
13.03.2018

## Slide 9
Customers’ involvement and willingness to change are crucial
Thermal storages are essential in lowering uncertainty in cost minimization, and increasing DR potential
Incorporating thermal storages with HVAC systems increases wind integration potential significantly
Conclusions
Page 9
Demand Response of HVAC Loads
13.03.2018

## Slide 10
Ali, M., Safdarian, A. and Lehtonen, M. (2015) ‘Demand response potential of residential HVAC loads considering users preferences’, IEEE PES Innovative Smart Grid Technologies Conference Europe, 2015–January(January), pp. 1–6.
DOI: 10.1109/ISGTEurope.2014.7028883.
M. Ali, J. Jokisalo, K. Siren, and M. Lehtonen, “Combining the demand response of direct electric space heating and partial thermal storage using LP optimization,” Electric Power Systems Research, vol. 106, pp. 160-167, Jan. 2014.
DOI: 10.1016/j.epsr.2013.08.017
M. Ali, ’ Domestic Space Heating Load Management in Smart Grid - Potential Benefits and Realization’, PhD thesis, Aalto University.
URL: http://urn.fi/URN:ISBN:978-952-60-6962-3
Siano, P. (2014) ‘Demand response and smart grids - A survey’, Renewable and Sustainable Energy Reviews. Elsevier, 30, pp. 461–478.
DOI: 10.1016/j.rser.2013.10.022.
References
Page 10
Demand Response of HVAC Loads
13.03.2018