## Slide 1: ELEC-E8423 - Smart Grid Active voltage controlling (AVC) in SG
Miina-Maija Simonen Joonas Sorjamäki
03.05.2022

## Slide 2: Contents
Introduction
Non-coordinated active voltage control methods
Coordinated active voltage control methods
Obstacles
Conclusions

## Slide 3: Introduction
There are voltage quality and voltage drop standards for the network
  These limit the hosting capacity of distributed generation
Passive and active voltage control methods
  Active methods often more economically feasible
    Either local, coordinated or these two combined
  Passive methods can be physical grid strengthening
Notes: In traditional grid power flows from plants to loads and customers. The grid plänning principles have based on this. However, when the production is changing to renewable energy sources, the grid becomes distributed grid, as we have heard for example about demand response. As the network has not been planned for this kind of use, it brings up this active voltage control problem. Requirements for the voltage quality and voltage drop stantards limit the amount og DG that the network can host.
Traditionally the voltage has been controlled passively,for example as using stronger components. But if we want to have more DG in our power system, voltage has to be controlled actively. We will tell you now about active voltage controlling in smart grid. Active voltage controlling can happen in local level, coordinatedly in the whole system or using both.
Next slide, there you go Joonas

## Slide 4: Local active voltage control (LVC)
Control based on local measurements
  No need for information transfer
  E.g. power factor control based on terminal measurements
Can significantly increase DG hosting capacity
Might increase losses
In worst cases might increase the need of reactive power compensation

## Slide 5: Coordinated active voltage control (CVC) (1/2)
Control based on the state of the whole network or a large network part
CVC increases DG hosting capacity much more than LVC
Requires:
  Data transfer between nodes
  Measurements done all across the network
  Algorithms to decide on best control actions
  Control center

## Slide 6: Coordinated active voltage control (CVC) (2/2)
There are two types of CVC control methods
  Methods using control rules
    Control actions implemented when predetermined conditions are met in a network node
      Example: Substation voltage is reduced when the maximum voltage is too high
    Adequate when there are not many control possibilities in a network
  Methods using optimization
    An optimization algorithm is used to determine control actions

## Slide 7: Obstacles for active voltage control
Taking active voltage control into use changes the operational and planning principles of distribution networks substantially
In an active network, customer owned resources are used in network management
  DNO has to trust these capabilities
The network planning tools used currently are not capable of taking active voltage control into account.
Active voltage control is still somewhat at its development phase
  Practical implementations have mainly concerned microgrids
  Algorithms are still under research
The current regulative environment, at least in Finland, does not encourage DNOs to take active voltage control into use.
  Connection of DG incentivized. Making the connection in a cost effective manner is not incentivized.
Traditionally, measurement data has been available only from the primary substations
Notes: There are many obstacles for AVC:

## Slide 8: Conclusions
AVC can in many cases increase the DG hosting capacity of a network more cheaply than conventional methods
AVC is not widely used yet because of its novelty and problems
Requires change in grid operation and planning principles

## Slide 9: Source material used
Kulmala, A. 2014. Active Voltage Control in Distribution Networks Including Distributed Energy Resources. Technical university of Tampere.
Kulmala, K. Mäki, S. Repo and P. Järventausta, "Active voltage level management of distribution networks with distributed generation using on load tap changing transformers, " in Proc. Power Tech 2007, Lausanne, Switzerland, July 2007.
Kulmala, S. Repo and P. Järventausta, "Increasing penetration of distributed generation in existing distribution networks using coordinated voltage control," Int. Journal of Distributed Energy Resources, vol. 5, pp. 227-255, July 2009
H. Yujun and M. Petit. 2013. Active voltage control using distributed generation on distribution networks. 2013 IEEE Grenoble Conference, 2013, pp. 1-6, doi: 10.1109/PTC.2013.6652200.
Fusco G., Russo M., DE Santis M. 2021. Decentralized Voltage Control in Active Distribution Systems: Features and Open Issues . Energies magazine.