## Slide 1: ELEC-E8423 - Smart Grid Electric trucks and their charging solutions
Julia Kondakov & Matias Mattheiszen
19.4.2022

## Slide 2: Introduction
Globally, more than one-third of transport-related CO2-emissions, and 7% of total energy-related CO2 come from road freight transport
Only 31 000 electric trucks were on the road globally in 2020
Challenging to electrify heavy-duty transport:
  High energy requirements and low energy density of batteries
  Price and weight of massive batteries
Battery prices and battery technology are constantly evolving
Share of electric trucks must scale up from 1% to 30% by 2030
Different ways to electrify trucks: battery electric trucks (batteries with charging or swapping), hydrogen fuel cell electric vehicles and electrified road systems

## Slide 3: Electric truck charging solutions today
Batteries with wired charging
  Alternating current (AC) charging:
    On-board charger
    Power between 22-43 kW
    Overnight charging
    Relatively slow: 10h
    More cost-effective
  Direct current (DC) charging:
    Charging station
    Power starts above 20 kW and between 50-250 kW
    Fast charging: 2h
    For completing transport assignment

## Slide 4: Electric truck charging solutions in the future
Electrified road systems
  Power is transferred between a vehicle and the road that it is travelling on
  Requires route predictability
  Overhead conductive: charging power is continuously transferred from overhead lines to the vehicle through a pantograph
  Conductive power transfer from road: power is transferred to the vehicle through rails embedded in or on top of the road surface
  Inductive power transfer from road: power transfer takes place between coils embedded in the road and coils in the vehicle without any wires
  On electrified road  uses propulsion system or charges on-board batteries
  On normal road  switches to an electric or hybrid motor

## Slide 5: Electric truck charging solutions in the future
Batteries with swapping
  Batteries are removed and replaced with fully charged ones
  Time-saving
  Considerable costs
  If different battery-pack configurations  costs will increase
Hydrogen fuel cells electric trucks
  Extends the range
  Short and easy refueling process and high energy density
  High cost of building hydrogen infrastructure
  Hydrogen is difficult and costly to transport

## Slide 6: Electric truck market: Current state
The market share of Electric trucks is predicted to grow significantly
  Cost and emission reductions
Charging network
  Current state:
    Non-existent infrastructure
    Major development projects (Gothenburg)

## Slide 7: Impact on power grid
Higher market share –> increased demand of electricity
  High local loads could cause grid failures
Smart charging
  Enables cost savings and eases the stress of the Grid
  E-truck and Smart Grid integration enables:
    System flexibility
    Local flexibility
    Possibility for multiple ancillary services
(Das et al., 2020).

## Slide 8: Potential in energy reserve market
Large amount of battery capacity available
Vehicle to Grid (V2G)
  Battery capacity utilized to balance demand and supply
  Swappable batteries could form an even more centralized and controlled energy reserve
  Synergies between renewable electricity production and the increased amount of electric trucks.

## Slide 9: Conclusions
In the coming years as the technology continues to improve, we will see more charging solutions, faster charging, more charging stations and better charging infrastructure made available to electric trucks.
The increase in available battery capacity could be exploited in numerous ancillary services.
Smart charging solutions combined with the increased amount of electric trucks provides synergies between renewable electricity production, electric truck charging and reserve markets.

## Slide 10: Source material used
IEA. 2017. The Future of Trucks. https://www.iea.org/reports/the-future-of-trucks
IEA. 2021. Trucks and Buses. https://www.iea.org/reports/trucks-and-buses
Liimatainen, H., van Vliet, O. & Aplyn, D. 2019. The potential of electric trucks – An international commodity-level analysis. Applied
Energy. Vol. 236. pp. 804-814. doi:10.1016/j.apenergy.2018.12.017.
Jason Morgan. 2021. Understanding Electric Truck Charging Needs And Choice. Fleet Equipment. https://www.fleetequipmentmag.com/understanding-electric-truck-charging/
Henrik Engdahl. 2021. How a good charging strategy can extend an electric truck’s range. Volvo Trucks.
https://www.volvotrucks.com/en-en/news-stories/insights/articles/2021/nov/How-a-good-charging-strategy-can-extend-an-electric-trucks-range.html
Lars Mårtensson. 2020. Electric Roads: A niche solution for confined areas? Volvo Trucks. https://www.volvotrucks.com/en-en/news-stories/insights/articles/2020/jul/electric-roads-a-niche-solution-for-confined-areas.html
Furnari, E., Johannes, L., Pfeiffer, A. & Sahdev, S. 2020. Why most eTrucks will choose overnight charging. McKinsey & Company.
https://www.mckinsey.com/industries/automotive-and-assembly/our-insights/why-most-etrucks-will-choose-overnight-charging
Lars Mårtensson. 2020. Hydrogen fuel cells: All your questions answered. Volvo Trucks. https://www.volvotrucks.com/en-en/news-stories/insights/articles/2020/jun/hydrogen-fuel-cells-all-your-questions-answered.html
Das, H. S., Rahman, M. M., Li, S., Tan, C. W. (2020). Electric vehicles standards, charging infrastructure, and impact on grid integration: A technological review. Renewable and Sustainable Energy Reviews. Vol. 120. S. 109618. ISSN 1364-0321. Available: https://doi.org/10.1016/j.rser.2019.109618

## Slide 11: Other issues ….
Send the presentation to matti.lehtonen@aalto.fi for check latest the day before the scheduled presentation