## Slide 1: ELEC-E8423 – Smart Grid
Sami Rahkola
Juho Turunen
10.3.2020
Solar power generation variation and its modelling
Solar panel array [1]

## Slide 2
Solar panels
Solar variation
Variation in solar power generation
Modelling solar power generation
Effects on the grid
Conclusions
Introduction

## Slide 3
Solar panels
Used to produce electricity
  Needs an inverter and filter for grid connection
MPPT is needed for optimal operation
  Compensates the changing environmental factors
Typical efficiency is 15-18%
  Reflectivity
  Thermodynamic characteristics
  Component quality
Solar array connected to the grid [2]
IV-curve of solar cell [3]

## Slide 4
Solar variation
Solar radiation levels depends on
  Time of the year and day
  Geographical Location
Local variation
  Weather
    Clouds, snow, temperature
  Shadowing objects
    Trees, buildings, dirt
Installation angle
Photovoltaic power potential of the world [4]
  Forms of radiation
    Direct
    Diffused
    Reflected

## Slide 5
Yearly variation is a problem
  During winters, the generation is low, and demand is high
  During summers can cause curtailment
    Reduction of production when there is surplus of production
Daily variation
  Solar power production cycle doesn’t follow normal consumption curve
Variation in solar power generation
Daily variation of solar irradiation and modelled PV power production (blue) [6]

## Slide 6
Historical data
  Measured values from several years
  Usually location specific
Long-term forecasting
  Based on historical and astronomical data
Short-term forecasting
  Based on weather forecasts
Modelling solar power generation
Recent study of time series forecasting for solar power generation using artificial neural network. [7]

## Slide 7
Power reserves
  Needed when PV production is low
  To react to the variations
    Power balance and frequency
Can cause voltage rises in the distribution network
Grids inertia will weaken due the loss of rotating mass
Modelling helps to compensate the variations of production
  Controlling of battery storages and other power reserves
  Demand response
Effects on the grid
Photo by Fingrid

## Slide 8
Modelling is needed in order to
  Smooth generation variation
  Preserve grid balance
Power generation’s variation is mainly caused by
  Solar radiation/weather
  Panel temperature
  Technical properties
Conclusion
Photo by Zbynek Burival on Unsplash

## Slide 9
Thank you

## Slide 10
Photo by New Paltz University. Available: https://solarliberty.com/learn-about-this-colleges-new-solar-microgrid-project-at-july-17-open-house/.
Marko Hinkkanen. Course material of controlling of electric drives and converter techniques. 2020
Photo by PVEducation.org . Available: https://www.pveducation.org/pvcdrom/solar-cell-operation/iv-curve.
Solargis. Available: https://solargis.com/maps-and-gis-data/download/world
Solar panel efficiency. solar.com. Available: https://www.solar.com/learn/solar-panel-efficiency/
Hellman Hannu-Pekka, Koivisto Matti, Lehtonen Matti. 2014. Photovoltaic Power Generation Hourly Modelling
Hyssein Sharadga, Shima Hajimirza, Robert S. Balog. 2019. Time series forecasting of solar power generation for large-scale photovoltaic plants
Source materials