## Slide 1: Thermal Energy Storage Systems
Jhatial Tarique Ali
Tetteh Sampson

## Slide 2
CONTENT
Introduction
SHE Storage
LHE Storage
TCE Storage
TES in Smart Grid

## Slide 3: Introduction
Classification
Material
System
Increasing popularity of thermal energy storages
Definition:
TES is the system of storing energy in the form of heat energy for later usage

## Slide 4: Sensible Heat Storage Systems
Sensible heat storage is based on raising the temperature of a liquid or solid to store heat and releasing it with the decrease of temperature when it is required
Attributes
large volumes
High Temperatures
Mostly low efficiencies
Less complicated systems compared to others
Low cost of thermal storage materials
Underground TES Methods
Most common TES Method

## Slide 5: TES develop by Aalto University Research group of Energy Conversion
(A novel Electric grid storage system)
Schematic view
View of the 3D Model
Stores electricity in thermal energy
Uses variety of TES materials
( thermal oils, Molten salts, Sands)
No critical material involved
Low cost in electric grid storage
High efficiency with sand as storage material
Time and power discharge profile for a 1 𝑚^3
thermal oil and molten salt heat storage materials.
Comparing two different thermal energy storage materials used in the system; Therminol VP1 (Oil) and
Molten salt (Salt).
• Passive solar heat
• Heat source for heat pumps
• 300 000 m3, old oil storages
• 2 – 24 ºC
• 6 – 7 GWh (Helen total 6600 GWh)
• 3 MW
Helen Oy, Thermal storage in Seawater storage
https://www.hel.fi/uutiset/en/helsinki/the-kruunuvuorenranta-rock-caverns

## Slide 6: Latent Heat Storage Systems
Latent heat storage is a direct storage system which has the advantage of high storage density and ability to store energy with only a small temperature variation
Materials used for latent heat storage are called phase change materials (PCM)
Attributes
They require low storage volume
Less on-off cycles
High investment cost
High risk of leakage
Operational mode of ventilated faced with PCM
Classification of PCM
Clay bricks including PCM macrocapsules

## Slide 7
PCM Developed in Aalto University
Research group of Energy Conversion
Dr. Roza Yazdani
b) our novel thermal materials with shape stable and leakage preventive properties above melting point
a) pure PCM above melting point
Under scanning electron microscope
Crystallization of novel PCM by Aalto University
Click to play video

## Slide 8
Thermochemical Heat Energy
The TCS uses thermochemical materials (TCMs) that store and release heat by a reversible endothermic/exothermic reaction process.
During the charging process, heat is applied to the material A, resulting in a separation of two parts B + C.
Product B and C are stored separately
Product B and C are mixed which releases energy during the chemical reaction
Storage capacity depending on temperature for TES.

## Slide 9
Schematic drawing of a thermo-chemical energy store integrated in a solar thermal combisystem.
Solar thermochemical energy storage system using manganese-oxide based redox cycling
TCES Hybrid System

## Slide 10
The Role of TES in Smart Grid
In conclusion
TES accounts for emission reduction
Storing waste heat from process
Long term seasonal storages
Promoting the rapid use of renewables
Available for both domestic and commercial usage
Available for both heating and electrification
Adaptable to supply and demand in short, medium and long term

## Slide 11
Some extra reading materials and references
Sarbu (2012) Thermal Energy Storage. https://doi.org/10.1016/B978-0-12-811662-3.00004-9
Fang (2018) An overview of thermal energy storage systems. https://doi.org/10.1016/j.energy.2017.12.037
Prof Hywel (online) WP9 Smart Thermal Energy Grid. https://www.flexis.wales/research-item/wp9-smart-thermal-energy-grid-prof-hr-thomas/
Wojciech (online) Thermal energy storage via manganese-oxide based redox cycling. http://stg.anu.edu.au/research/storage/manganese-oxide.php
S. Tetteh, A. Santasalo-Aarnio and K. Saari: “Electric grid-scale energy storage system” Aalto invention application IPID 2370 (2019).
Barbara (2013) Thermochemical Energy Storage as an Element for the Energy Turnaround. https://www.researchgate.net/publication/260255602_Thermochemical_Energy_Storage_as_an_Element_for_the_Energy_Turnaround/figures?lo=1
Refer to student presentations 2018 & 2019 (MyCourses materials) for topics in TES not covered in this presentation
Thank You