Name:

Student number:

0) Evaluate this exercise

| Grade [0,5]+comments |  |
| --- | --- |
| Challenge (0 easy, 5 too hard) |  |
| Usefulness (0 none, 5 very) |  |

1) LO buffer ac analysis

- Perform “ac” analysis from 500MHz to 2Ghz by placing and AC source at the vin node.  Plot the gain and input impedance magnitude of first stage vs frequency. [Hint] gain is defined as vm(vout_first)/vm(vin) and input impedance can be plotted with .plot ac zm(1,1).

| What is the purpose of resistor R1? |  |
| --- | --- |
| Why the input impedance magnitude is not exactly 50Ω? |  |

Please add the following figure

Figure 1: LO buffer Gain and input impedance magnitude response

- Sweep the feedback resistor R0 from 100Ω to 10KΩ. Plot the gain and input impedance when the R0 value is swept.

| Gain and input impedance will change. Can you explain why this happens? |  |
| --- | --- |

Please add the following figure

Figure 2: LO buffer Gain and input impedance magnitude when R0 is swept

2) LO buffer transient analysis

- Do the transient analysis till 20ns with an input sine wave source of 100mV and 1.5GHz frequency.  Plot the results at vin, vout_first and vout nodes.

Please add the following figure

Figure 3: LO buffer transient response

- Sweep the value of load capacitor C0 from 80 fF to 2.8 pF with 10 steps.  Plot the results.

| Output waveform will change for bigger values of C0. Can you explain why? |  |
| --- | --- |
| Capacitor C0 models the input capacitance of next stage which will be driven by LO generation circuit. If the next stage is a passive switching mixer, will the mixer work properly if its input gate capacitance is 2.8pF? Explain your answer. |  |
| Find how you can measure vout waveform risetime from tools present in Ezwave window. Find out risetime value for C0=2.8pF. |  |
| How can the gain of the LO-buffer be increased for C0 = 2.8 pF? |  |

Please add the following figure

Figure 4: LO buffer transient response for C0 sweep