## Slide 1: Course Assignment: Marine risks and safety 2023 Section B: Hazard analysis using System’s Theoretical Process Analysis (STPA) Section C: Discussion and comparison

## Slide 2: Assignment aim
The main aim of the presentation is to describe the STPA process for identifying unsafe causes and hazards in the system for the assignment purpose.
The students should demonstrate that they can successfully execute the STPA process in software intensive systems.
As the identification of unsafe causes and safety controls require support from the system experts, the main focus in this assignment will be in the process and the method.

## Slide 3: Process overview
1. Define the losses
2. Identify the system level hazards
3. Developing safety constraints
6. Identify causes of unsafe control actions
5. Identify unsafe control actions
4. Develop control structure
7. Identify the safety control
8. Present the results

## Slide 4: 1. Defining the losses
L-1 = Loss or damage to the vessel
L-2 = Loss of life
L-3 = Loss of mission
L-4 = Loss or damage to external objects
“A loss involves something that is of value to the stakeholders”
Tip to prevent common mistake:
Losses should not reference individual components or specific causes like “human error” or “sensor failure”.

## Slide 5
2. Identifying the system-level hazards
H-1 = The vessel operates in low depth (shallow) water area resulting into grounding. (L-1)
H-2 = The vessel collides with other objects during the voyage. (L-1)
<Hazard specification> = <System> & <Unsafe condition> & <Link to losses>
“A hazard is a system state or set of conditions that, together with a particular set of worst-case environmental conditions, will lead to loss.”
“A system is a set of components that act together as a whole to achieve some common goal, objective or end.”
Tips to prevent common mistakes:
Hazards should not refer to individual components of the system.
All hazards should describe system-level conditions to be prevented.

## Slide 6
3. Developing safety constraints requirements
“A system-level constraint specifies system conditions or behaviors that need to be satisfied to prevent hazards (and ultimately prevent losses)”
<Hazard specification> = <System> & <Unsafe condition> & <Link to losses>
<Safety constraint specification> = <System> & <condition to enforce> & <Link to hazards>
H-1 = The vessel operates in low depth (shallow) water area resulting into grounding. (L-1)
SC-1 = The vessel must not operate in low depth water area. (H-1)
H-2 = The vessel collides with other objects during the voyage. (L-1)
SC-2 = The vessel must identify and avoid obstacles when navigating. (H-2)
Tip: Check ISO/IEC/IEEE 29148:2018

## Slide 7
4. Develop a control structure
Tip: Check other publications on
STPA

## Slide 8: 5. Identifying unsafe control actions
Controller – DP control unit |  |  |  | 
Control action | Not providing causes hazard | Providing causes hazard | Too early, too late, out of order | Applied too long or stopped too soon.
Thruster speed | UCA-1: DP control unit doesn’t provide thruster speed to maintain its position resulting into a potential collision. (H-1, H-2) | UCA-2: DP control unit provides incorrect thruster speed to maintain its position resulting into a potential collision. (H-1, H-2) | UCA-3 DP control unit provides thruster speed late than required resulting into a potential collision. | 
Rudders / Pods angle | UCA-4: DP control unit doesn’t provide rudders/pods angle to maintain its heading and position resulting into a potential collision (H-1, H-2) | .. | ... | 
(At least for 3 controllers and 3 control actions, more than 15 UCAs)
“An Unsafe Control Action (UCA) is a control action that, in a particular context and worst-case environment, will lead to a hazard.” There are 4 ways a control action can be unsafe (guidewords as represented in the columns below)
<UCA spec> = <Source> <Guideword> <Control action> <Context> & <Link to Hazards>
UCA-1 = Management doesn’t provide crew training, which is required for the safe operation during a voyage. (H-1, H-2)

## Slide 9: 6. Identifying causes of unsafe control actions:
UCA-1 = DP control unit does not provide thruster speed to maintain its position resulting into a potential collision. (H-2,H-3)
‘The motion reference units (MRU) fail to provide required input to calculate the thruster speed.
The servo actuators or controllers fail to implement the thruster speed.
The DP control unit and Kalman filters are not able to process the data from the motion reference units
The DP system is not able to calculate the required thruster speed to maintain the vessel positioning
Two types of causes must be considered:
a) Why would Unsafe Control Actions occur?
b) Why would control actions be improperly executed or not executed, leading to hazards?
Tip: Check STPA handbook
3 per UCA

## Slide 10: 7. Identifying the safety controls
Secondary MRU should be available in emergency situations
Failsafe options should be implemented in case of emergency situations
Alarms should be generated
Etc.

## Slide 11: 8. Presenting the results
Part C:
Compare the results from A and B based on what you see and know from the lectures
1 A4 page of text.
Advantages - disadvantages
All outcome of the analysis in a clear format in the report.
The report format was presented in the previous lecture

## Slide 12: 9. Grading
Task | Grading
Task 1 – Define the losses | 2
Task 2 – System level hazards | 2
Task 3 – Safety constraints | 3
Task 4 – Control structure | 8
Task 5 – UCAs | 8
Task 6 – Causal factors | 5
Task 7 – Safety controls | 5
Task C | 20

## Slide 13: Questions
You can ask your questions at the following emails: victor.bolbot@aalto.fi
ahmad.bahootoroody@aalto.fi
osiris.valdez.banda@aalto.fi
Tip: Check other publications with
STPA for the same system