## Slide 1: AspenPlus Group A Final Presentation

## Slide 2: Agenda
Base case
Alternative Fuel
Improvements
Sensitivity Analysis
Conclusion, Outlook and Question

## Slide 3: Base case

## Slide 4: Base case
Combustion Unit
Heating Unit
Power – and district heating unit

## Slide 5: Base case
Combustion Unit
Heating Unit
Power – and district heating unit

## Slide 6: Combustion Unit
Design Spec:
O2 output should be at least 0,5 mol-%
→ vary air mass flow

## Slide 7: Heating Unit
Design Spec:
Flue gas temperature after the boiler should be 650 °C → vary live steam mass flow

## Slide 8: Power and district heating unit
Design Spec: net additional duty should be 0 → vary flow split percentage
Design Spec:
DH water supply temperature should be 85°C→ vary DH water flow

## Slide 9: Alternative Fuel

## Slide 10: Second fuel case – Municipal Solid Waste MSW (ECN classification)
Change in composition from the base case (Proximate analysis) |  | 
 | Wood fuel | MSW
FC (dry) | 20.83 | 26
VM (dry) | 78.37 | 18
Ash (dry) | 0.8 | 56
Moisture | 51 | 6.4
 | Wood fuel | MSW
LHV (MJ/kg) | 7.96 | 7.72
Boiler fuel input power (MW) | 11.5 | 11.5
Mass flow rate (kg/s) | 1.44 | 1.48

## Slide 11: Changes from the base case
High losses to ash content
Reduction in flue gas flow rate to the evaporator
Combustion side
Lower heat duties in all the heat exchangers than the base case
+Changes in other attributes of the streams (Temp)

## Slide 12: Power and district heating unit using MSW
 | Wood fuel case | MSW case
Power output (MW) | 2.06 | 1.64
Heat output (MW) | 8.15 | 6.50
Overall efficiency (%) | 88.7 | 70.8
More MSW fuel requirement

## Slide 13: Improvements

## Slide 14: Improvements: Trading DH for electricity
Added 1 reheat cycle
Optimization: increased FWT pressure to 5 bar

## Slide 15: Reheating
Carnot theoretical efficiency
Decreased steam mass flow -> decreased DH output
Increased work done per cycle -> increased total electricity output

## Slide 16: Optimizing: regeneration
Raising the FWT pressure -> reducing the condensate flow at the DH HEX.
Less heat is consumed in the economizer -> more heat available for evaporator and superheater.
Larger water mass flow -> larger electricity output.

## Slide 17: Sensitivity Analysis

## Slide 18: Case 1: Biomass Mass Flow Rate
Vary the mass flow rate of the fuel
Increase of steam production
Chart: Mass Flow Rate Biomass [kg/s]
| 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3
MASSFLOW LIVESTEAM (kg/sec) | 2.5535 | 3.0634 | 3.573 | 4.0828 | 4.593 | 5.1056 | 5.6161 | 6.1275 | 6.6386 | 7.1458 | 7.6584

## Slide 19: Case 1: Biomass Mass Flow Rate
Case | Results with
1,0 | Errors
1,2 | Errors
1,4 | Warnings
1,43 | OK
1,6 | OK
1,8 | OK
2,0 | Warnings
2,2 | OK
2,4 | OK
2,6 | Warnings
2,8 | Errors
3,0 | Errors
Chart: Mass Flow Rate Biomass [kg/s]
| 1 | 1.2 | 1.4 | 1.4442999999999999 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3
LP | 1354.1248 | 1624.4964 | 1894.7159 | 1954.6969 | 2165.1155 | 2435.6618 | 2707.4756 | 2978.247 | 3249.4712 | 3520.5542 | 3789.3774 | 4061.273
MP | 33.1425 | 39.7764 | 46.4132 | 47.8482 | 52.9905 | 59.6167 | 66.2931 | 72.9042 | 79.5108 | 86.1113 | 92.7934 | 99.4205
HP | 39.8126 | 47.7623 | 55.7078 | 57.4702 | 63.6565 | 71.611 | 79.6033 | 87.5638 | 95.537 | 103.5059 | 111.413 | 119.4061
CONDENSER | 5292.4976 | 6766.3439 | 7898.8131 | 8148.8656 | 9026.0721 | 10153.9427 | 11287.0976 | 12415.907 | 13546.6038 | 14676.7117 | 14887.3367 | 13413.4904

## Slide 20: Case 1: Biomass Mass Flow Rate
Chart: 
| 1 | 1.2 | 1.4 | 1.4442999999999999 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3
Efficiency | 0.84313 | 0.88655 | 0.88693 | 0.88694 | 0.88682 | 0.88678 | 0.88717 | 0.88718 | 0.88731 | 0.88738 | 0.8461 | 0.73993

## Slide 21: Case 2: Air Mass Flow Rate
Chart: Mass Flow Rate Air [kg/s]
| 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8
LP | 1056.3272 | 1451.575 | 1808.9653 | 1989.779 | 1977.1291 | 1963.7779 | 1949.6588 | 1936.364 | 1921.8591 | 1908.5478 | 1894.4991
MP | 25.8629 | 35.524 | 44.2468 | 48.6928 | 48.3971 | 48.0286 | 47.7295 | 47.3662 | 47.048 | 46.7168 | 46.4
HP | 31.0574 | 42.6776 | 53.1844 | 58.5012 | 58.1297 | 57.7358 | 57.3223 | 56.9301 | 56.5049 | 56.1133 | 55.7012
CONDENSER | 1525.0938 | 2998.9401 | 4472.7865 | 5946.6328 | 7420.4791 | 8186.7229 | 8127.8623 | 8072.4381 | 8011.9691 | 7956.4763 | 7897.9092
O2 | 1.5812e-10 | 2.2373e-08 | 2.3251e-06 | 0.0088236 | 0.025897 | 0.040718 | 0.053604 | 0.064895 | 0.074857 | 0.083712 | 0.09163
Vary the mass flow rate of the air inlet
&
Deactivate the Design Spec to fix the oxygen content
Different Optimums for DH and Turbine Output

## Slide 22: Case 2: Air Mass Flow Rate
Chart: Mass Flow Rate Air [kg/s]
| 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8
Efficiency | 0.22899 | 0.39321 | 0.55398 | 0.69864 | 0.82565 | 0.89106 | 0.88466 | 0.87862 | 0.87204 | 0.866 | 0.85963
The efficiency optimum is therefore at 5,5 kg/s with an ox content of 4,07 %.

## Slide 23: Case 2: Air Mass Flow Rate
Chart: Air Mass Flow [kg/s]
| 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8
CO | 0.058157 | 0.035854 | 0.01254 | 0.00024745 | 7.2061e-05 | 2.9094e-05 | 1.3677e-05 | 6.7777e-06 | 3.6226e-06 | 2.0068e-06 | 1.1606e-06
CO2 | 0.20303 | 0.20827 | 0.22057 | 0.21966 | 0.20284 | 0.18829 | 0.17565 | 0.1646 | 0.15485 | 0.14619 | 0.13845
O2 | 1.5812e-10 | 2.2373e-08 | 2.3251e-06 | 0.0088236 | 0.025897 | 0.040718 | 0.053604 | 0.064895 | 0.074857 | 0.083712 | 0.09163
Chart: Air Mass Flow [kg/s]
NO | 2.99e-08 | 6.9107e-07 | 1.0682e-05 | 0.00071407 | 0.0010146 | 0.0010566 | 0.0010246 | 0.00095386 | 0.0008794 | 0.00080204 | 0.0007301
NO2 | 0 | 1.0549e-12 | 1.3075e-10 | 5.1967e-07 | 1.4387e-06 | 2.132e-06 | 2.6591e-06 | 3.0484e-06 | 3.3449e-06 | 3.5623e-06 | 3.7234e-06
O2 | 1.5812e-10 | 2.2373e-08 | 2.3251e-06 | 0.0088236 | 0.025897 | 0.040718 | 0.053604 | 0.064895 | 0.074857 | 0.083712 | 0.09163

## Slide 24: Conclusion, Callenges and Questions

## Slide 25: What we did so far...
Simulation of both fuel cases
Inclusion of multiple improvements (only one improved something)
Sensitivity analyis of the mass-flow of the air and of the fuel

## Slide 26: Challenges on the way
Errors (Convergence, Zero-Streams, Massimbalances)
Sensitivity of Aspen Plus
Overview over different versions

## Slide 27: Open Questions
Did we understood everthing correctly?
Is our improvement sufficient for the final report?
Is the sensitivity analysis sufficient for the final report?

## Slide 28: Thanks!
Any questions or advice ?