## Slide 1: Experiment on control communication from Raspberry Pi over to a CNC machine
Jouni Hannonen Sanchayan Rajeetharan Quoc Huynh

## Slide 2: Overview
Introduction Motivation Game
Interconnection between two systems
  GPIO ( General-Purpose Input/Output)
  OPC UA ( Open Platform Communications Unified Architecture)
Results
Conclusion

## Slide 3: Introduction

## Slide 4: Game in action

## Slide 5: Raspberry pi to CNC interconnection
GPIO Method
OPC UA
Profinet

## Slide 6: GPIO method
Utilize GPIO Pins - 12 digital signals
Electrical Switching mechanism
Profinet Interface Module + Digital input module
Average 4 ms data update cycle is monitored
X axis – time , Y axis – CNC system variable value

## Slide 7: OPC UA method
Communication protocol
Synchronous data exchange based control
No additional hardware required
Modify 3 CNC system variables
Average 14 ms data update cycle monitored
X axis – time , Y axis – CNC system variable value

## Slide 8: Results & Conclusion
Average data update cycle in GPIO is 4 ms and OPC UA is 14 ms.
CNC system have less data update cycle in GPIO than OPC UA.
OPC UA is easy to implement
GPIO requires additional hardware
Data Type , through GPIO integer only
GPIO implementation is limited due to number of pins

## Slide 9: Questions
?