Name_______________________ Student number________________

Home assignment 2

Beam structure of the figure is loaded by a point moment acting on node 2. Determine the rotations  and  by using two beam elements. Displacements are confined to the XZ-plane. The cross-section properties of the beam A, I and Young’s modulus of the material E are constants.

Solution template

Virtual work expression for the displacement analysis consists of parts coming from internal and external forces  and . For the beam bending mode in xz-plane and cubic interpolation of the nodal values, the element contributions are

,  ,

The element contribution of the point force/moment follows from the definition or work and is given by

.

For beam 1,  is given by

For beam 2,  is given by  (when written in a form which is compatible with the first element contribution)

Virtual work expression of the point moment (written in a form which is compatible with the other element contributions)

.

Virtual work expression of structure is sum of the element contributions

.

Principle of virtual work and the fundamental lemma of variation calculus imply that

.

Solution to the linear equations system is given by

and  .       (

# Text boxes

L

1

3

M

z,Z

x,X

1

L

2

2