Name_______________________ Student number________________

Home assignment 2

The XZ-plane structure shown consists of two beams of equal properties. Assuming that the beams are inextensible in the axial directions, derive the angular speed of free vibrations. Young’s modulus  and density  of the beam material and the second moment of area  are constants. Assume that the inertia term due to rotation is negligible.

Solution template

As the beams are inextensible in the axial directions, the active degree of the structure is . Let us start with the element contributions. Only the virtual work expressions of the internal and inertia forces (available in the formulae collection) are needed.

,

,

Virtual work expressions of internal and inertia forces for beam 1 simplify to

,

,

giving

.

Virtual work expressions of internal and inertia forces for beam 2 simplify to

,

,

giving

.

Virtual work expression of structure is the sum of element contributions.

.

Finally, principle of virtual work and the fundamental lemma of variation calculus implies the ordinary differential equation of the form

.

Therefore, the angular speed of the free vibrations  is given by

.       (

# Text boxes

1

2

L

Z

L

1

2

X

x

z

L

3

x

z