## Slide 1
Fluid Power Basics - Assignments 2019
Assignment 1
Exercises 1-4
Version official
1.0
Calculation exercises
Exercises
Input prameters
Tables for results

## Slide 2: Instructions:
Form the research group (maximum 4 people) via MyCourses.
This file contains instructions for completing calculation exercises.
  Assignments explained
  Input parameters to be used. Different for each group (A-J).
Prepare 2 files
  This template with Results (use the existing tables in the document)
  Calculation file (pdf) inluding equations used. Electronic formats (Mathcad, Matlab, Excel, etc.). Also clear hand-written (and scanned) documents possible!
Submit your a) numerical results (this file) and b) calculation file (pdf) to MyCourses calculation assignment mailbox before the deadline!
  Deadline 31.1.2019

## Slide 3: Group identification (fill in)
Group code (A-J)
Group members

## Slide 4: 1. Cylinder: Flow rate
Fluid Power Basics
vMEAN
v1
v2
qvA
qvB1
qvA2
qvTANK
Inputs
D1 cylinder diameter, cylinder 1 [m]
d1 piston rod diameter, cylinder 1 [m]
v1 piston 1 velocity [m/s]
D2 cylinder diameter, cylinder 2 [m]
d2 piston rod diameter, cylinder 2 [m]
Dpipe pipe outer diameter [m], e.g. pipe 12x2  12 mm O.D. and 2 mm wall
epipe pipe wall thickness [m]
Outputs
AA,1 effectice piston area A (piston side), cylinder 1 [m2]
AB,1 effectice piston area B (rod side), cylinder 1 [m2]
AA,2 effectice piston area A (piston side), cylinder 2 [m2]
AB,2 effectice piston area B (rod side), cylinder 2 [m2]
qvA flow rate in pipe 12 [m3/s], SI units
qvA flow rate in pipe 12 [l/min], engineering units
vMEAN average flow velocity in pipe 12 [m/s]
qvA2 flow rate from cylinder chamber A2 [m3/s], SI units
qvA2 flow rate from cylinder chamber A2 [l/min], engineering units
qvB1 flow rate to cylinder chamber B1 [m3/s], SI units
qvB1 flow rate to cylinder chamber B1 [l/min], engineering units
qvTANK flow rate from tank [m3/s] (sign +  from tank, sign —  to tank), SI units
qvTANK flow rate from tank [l/min] (sign +  from tank, sign —  to tank), engineering units
v2 piston 2 velocity [m/s]
B
B
A
CYLINDER 1
CYLINDER 2
A
Pipe 12
Flow rates – Continuity equation

## Slide 5: 1. Input parameters
Input parameters for Groups A-J

## Slide 6: 1. Results
Outputs | Value | Unit | Definition
AA,1 |  | [m2] | effectice piston area A (piston side), cylinder 1
AB,1 |  | [m2] | effectice piston area B (rod side), cylinder 1
AA,2 |  | [m2] | effectice piston area A (piston side), cylinder 2
AB,2 |  | [m2] | effectice piston area B (rod side), cylinder 2
qvA |  | [m3/s] | flow rate in pipe 12, SI units
qvA |  | [l/min] | flow rate in pipe 12, engineering units
vMEAN |  | [m/s] | average flow velocity in pipe 12
qvA2 |  | [m3/s] | flow rate from cylinder chamber A2, SI units
qvA2 |  | [l/min] | flow rate from cylinder chamber A2, engineering units
qvB1 |  | [m3/s] | flow rate to cylinder chamber B1, SI units
qvB1 |  | [l/min] | flow rate to cylinder chamber B1, engineering units
qvTANK |  | [m3/s] | flow rate from tank (sign + Þ from tank, sign — Þ to tank), SI units
qvTANK |  | [l/min] | flow rate from tank (sign + Þ from tank, sign — Þ to tank), engineering units
v2 |  | [m/s] | piston 2 velocity

## Slide 7: 2. Cylinder: Force & Power
F1
F2
B
B
A
CYLINDER 1
CYLINDER 2
A
Pipe 12
Inputs
F1 piston 1 force [N]
pACCU1 accumulator= ”tank”, pressure=0 [Pa], gauge pressure
pACCU2 accumulator (constant) pressure [Pa], gauge pressure
Cylinder dimensions from Exercise 1
Piston velocity v1 from Exercise 1 ( Power calculations)
Flow rates from Exercise 1 ( Power calculations)
Outputs
CASE 1 WITH TANK
pA1.1 pressure in cylinders’ 1 and 2 A chambers [Pa], SI units, with tank
pA1.1 pressure in cylinders’ 1 and 2 A chambers [bar], engineering units, with tank
F2.1 piston force (for LIFTING mass M) of cylinder 2 [N], with tank
P1.1 mechanical power IN (Fv), with tank
P2.1 mechanical lifting power OUT (Fv), with tank
Paccumulator,1 hydraulic power from accumulator (pACCUqvACCU)
CASE 2 WITH ACCUMULATOR
pA1.2 pressure in cylinders’ 1 and 2 A chambers [Pa], SI units, with accumulator
pA1.2 pressure in cylinders’ 1 and 2 A chambers [bar], engineering units, with accumulator
F2.2 piston force (for LIFTING mass M) of cylinder 2 [N], with accumulator
P1.2 mechanical power IN (Fv), with accumulator
P2.2 mechanical lifting power OUT (Fv), with accumulator
Paccumulator,2 hydraulic power from accumulator (pACCUqvACCU)
pACCU
qvB1
qvA2
qvACCU
M
Two cases (1 and 2)
Pressure accumulator (gauge) pressure= 0 (”tank”)
Pressure accumulator (gauge) pressure= 50 bar (”accumulator”)

## Slide 8: 2. Input parameters
Input parameters | A | B | C | D | E | F | G | H | I | J | Unit | Definition
F1 | 9000 | 12600 | 19600 | 31200 | 50300 | 78500 | 78500 | 122700 | 122700 | 201100 | [N] | iston 1 force
pACCU1 (TANK, CASE 1) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | [bar] | accumulator= ”tank”
pACCU1 (CASE 2) | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | [bar] | accumulator (constant) pressure
Cylinder dimensions from Exercise 1 |  |  |  |  |  |  |  |  |  |  |  | 
Piston velocity v1 from Exercise 1 (Þ Power calculations) |  |  |  |  |  |  |  |  |  |  |  | 
Flow rates from Exercise 1 (Þ Power calculations) |  |  |  |  |  |  |  |  |  |  |  | 
Input parameters for Groups A-J

## Slide 9: 2. Results
Outputs | Value | Unit | Definition
CASE 1 WITH TANK |  |  | 
pA1.1 |  | [Pa] | pressure in cylinders’ 1 and 2 A chambers, SI units, with tank
pA1.1 |  | [bar] | pressure in cylinders’ 1 and 2 A chambers, engineering units, with tank
F2.1 |  | [N] | piston force (for LIFTING mass M) of cylinder 2, with tank
P1.1 |  | [W] | mechanical power IN (Fv), with tank
P2.1 |  | [W] | mechanical lifting power OUT (Fv), with tank
Paccumulator,1 |  | [W] | hydraulic power from accumulator (pACCUqvACCU)
CASE 2 WITH ACCUMULATOR |  |  | 
pA1.2 |  | [Pa] | pressure in cylinders’ 1 and 2 A chambers [Pa], SI units, with accumulator
pA1.2 |  | [bar] | pressure in cylinders’ 1 and 2 A chambers [bar], engineering units, with accumulator
F2.2 |  | [N] | piston force (for LIFTING mass M) of cylinder 2 [N], with accumulator
P1.2 |  | [W] | mechanical power IN (Fv), with accumulator
P2.2 |  | [W] | mechanical lifting power OUT (Fv), with accumulator
Paccumulator,2 |  | [W] | hydraulic power from accumulator (pACCUqvACCU)

## Slide 10: 3. Cylinder: stiffness
Inputs
Cylinder with blocked flow channels, dimensions
  D=0.100 m cylinder diameter
  d= 0.060 m rod diameter
  xmax= 1.000 m maximum stroke of piston
  x= 0.001 m small change in position from the initial positions x0
    xA=+x and xB=-x for spring constant calculations
  9 initial piston positions (before force load)
    x0 = [0.1 0.2 0.3 0.4 0.5 0.6 0.7 0.8 0.9] m
  Kf= 1.2109 Pa effective bulk modulus of fluid
Outputs
AA and AB cylinder piston areas (piston side and rod side) [m2] (1 +1 results)
VA and VB fluid volume changes in chambers A and B, include signs (+/-) [m3] (1 + 1)
VA and VB initial fluid volume in chambers A and B [m3] (9 + 9)
VA/ VA and VB/ VB relative volume changes, include signs (+/-) [-] (9 + 9)
pA and pB pressure changes, include signs (+/-), SI units [Pa] (9 + 9)
FA and FB force changes, include signs (+/-), [N] (9 + 9)
kspringA= FA/ xA mechanical spring constant of chamber A [N/m] (9 results)
kspringB= FB/ xB mechanical spring constant of chamber B [N/m] (9 results)
kspring= kspringA + kspringB cylinder’s mechanical spring constant [N/m] (9)
x
qvA=0
x0
VB
VA
Remark! You can consider in this case the fluid volumes VA and VB before and after the loading (F) the same!
qvB=0
xmax -x0

## Slide 11: 3. Results
Output variables | Value | Unit | Definition
AA |  | [m2] | cylinder piston area A (piston side)
AB |  | [m2] | cylinder piston area B (rod side)
DVA |  | [m3] | fluid volume change in chamber A
DVB |  | [m3] | fluid volume change in chamber B
Output variables | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | Unit | Definition
VA |  |  |  |  |  |  |  |  |  | [m3] | Cylinder chamber A volume
VB |  |  |  |  |  |  |  |  |  | [m3] | Cylinder chamber B volume
DVA/ VA |  |  |  |  |  |  |  |  |  | [-] | Relative volume changes A
DVB/ VB |  |  |  |  |  |  |  |  |  | [-] | Relative volume changes B
DpA |  |  |  |  |  |  |  |  |  | [Pa] | Pressure changes A
DpB |  |  |  |  |  |  |  |  |  | [Pa] | Pressure changes B
DFA |  |  |  |  |  |  |  |  |  | [N] | Hydraulic force changes A
DFB |  |  |  |  |  |  |  |  |  | [N] | Hydraulic force changes B
kspringA |  |  |  |  |  |  |  |  |  | [N/m] | Spring constant of fluid spring A
kspringB |  |  |  |  |  |  |  |  |  | [N/m] | Spring constant of fluid spring B
kspring |  |  |  |  |  |  |  |  |  | [N/m] | Overall spring constant of cylinder

## Slide 12: 4. Cylinder: Force
pA,3
pB,3
v= ’up’
v= ’down’
Fload
pACCU
F
Use pressure transformers 1 and 2 (cylinders)
to lift and lower the load on cylinder 3. Operate Pressure Transformer 1 with on/off valve 1 and Pressure Transformer 2 with on/off valve 2.
Calculate pressure pA,3 caused by Fload
Calculate the accumulator pressure (pACCU, MIN) with which pressure transformer 1 in is hydraulic force balance
Choose setting pressure for accumulator pACCU, which is between 5 bars and 10 bars higher than pACCU, MIN to ensure lifting, use 5 bar resolution (e.g. balance pressure 17 bar  >22 bar  setting pressure 25 bar)
Choose the smallest rod diameter from the list below for pressure transformer 2, which enables lowering of LOAD on cylinder 3. The cylinder diameter is fixed.
Standard rod diameters available
[10 20 22 25 28 32 36 40 45 50 56 63 70 80 90 100 110 125 140 160] mm
PT1
PT2
VALVE1
VALVE2
ACCUMULATOR
PRESSURE TRANSFORMERS
No external load! (No load on rod)
CYLINDER3
pA,2
pB,2
pA,1
pB,1

## Slide 13: 4. Input parameters
Input parameters | A | B | C | D | E | F | G | H | I | J | Unit | Definition
D1 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | 0.08 | [m] | Cylinder 1 diameter
D2 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | [m] | Cylinder 2 diameter
d1 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | 0.04 | [m] | Cylinder 1 rod diameter
D3 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | [m] | Cylinder 3 diameter
FLOAD | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000 | [N] | Load force
Input parameters for Groups A-J
Available standard side rod diameter parameters for Cylinder 2

## Slide 14: 4. Results
Input parameters | Value | Unit | Definition |  |  |  |  |  | 
D1 |  | [m] | Cylinder 1 diameter |  |  |  |  |  | 
D2 |  | [m] | Cylinder 2 diameter |  |  |  |  |  | 
d1 |  | [m] | Cylinder 1 rod diameter |  |  |  |  |  | 
D3 |  | [m] | Cylinder 3 diameter |  |  |  |  |  | 
FLOAD |  | [N] | Load force |  |  |  |  |  | 
Output values |  |  |  |  |  |  |  |  | 
AA,3 |  | [m2] | Cylinder 3 piston side area |  |  |  |  |  | 
pA,3 |  | [bar] | Cylinder 3 piston side pressure |  |  |  |  |  | 
AA,1 |  | [m2] | Cylinder 1 piston side area |  |  |  |  |  | 
AB,1 |  | [m2] | Cylinder 1 rod side area |  |  |  |  |  | 
pACCU,MIN |  | [bar] | Force balance pressure for rod side chamber of cylinder 1 |  |  |  |  |  | 
pACCU |  | [bar] | Pressure accumulator setting pressure |  |  |  |  |  | 
AA,2 |  | [m2] | Cylinder 2 piston side area |  |  |  |  |  | 
AB,2,MAX |  | [m2] | Cylinder 2 rod side force balance area |  |  |  |  |  | 
d2, MIN |  | [m] | Cylinder 2 theoretical rod diameter for force balance |  |  |  |  |  | 
d2 |  | [m] | Cylinder 2 standard rod diameter from the list (minimum diameter which enables lowering with selected accumulator pressure) |  |  |  |  |  | 
AB,2 |  | [m2] | Cylinder 2 rod side area with selected standard diameter rod |  |  |  |  |  | 
F3,LIFT |  | [N] | Cylinder 3 force (for lifting) with cylinder 1 as pressure transformer |  |  |  |  |  | 
F3,LOWER |  | [N] | Cylinder 3 force (for lowering) with cylinder 2 as pressure transformer (standard rod) |  |  |  |  |  | 
Fill in the Table on the right