## Slide 1
Fluid Power Basics - Assignments 2019
Assignment 2
Exercises 5-8
Version official
1.2
Calculation exercises
Exercises
Input prameters
Tables for results

## Slide 2: Instructions:
Form the research group (maximum 4 people) via MyCourses.
This file contains instructions for completing calculation exercises.
  Assignments explained
  Input parameters to be used. Different for each group (A-J).
Prepare 2 files
  This template with Results (use the existing tables in the document)
  Calculation file (pdf) inluding equations used. Electronic formats (Mathcad, Matlab, Excel, etc.). Also clear hand-written (and scanned) documents possible!
Submit your a) numerical results (this file) and b) calculation file (pdf) to MyCourses calculation assignment mailbox before the deadline!
  Deadline 28.2.2019

## Slide 3: Group identification (fill in)
Group code (A-J)
Group members

## Slide 4: Updates
Page 13, correction (10.2.2019)
  0.45 l/min leakage @ 35 bar  0.45 l/min leakage @ 50 bar
Pages 8 and 11 (12.2.2019)
  New output tables for both loads (m1 and m2)

## Slide 5: Hydraulic cylinder system performance
Cylinder system with 4/3 proportional control valve
Cylinder system with equivalent circuit for 4/3 proportional control valve
U> 0 V PA, BT open
U< 0 V PB, AT open

## Slide 6: 5. Hydraulic cylinder system - lifting
Fluid Power Basics
Inputs
D cylinder diameter [m]
d piston rod diameter [m]
m1 & m2 two load masses, two cases [kg]
U valve command [V]
pP pump pressure [bar], pressure compensated pump
Kvalve valve capacity, full opening (40 l/min @ 35 bar)
qvpump pump’s flow rate is adapted for the motion, pressure relief valve is closed!
Outputs
AA effective piston area A (piston side) [m2]
AB effective piston area B (rod side) [m2]
v piston velocity [m/s]
qvA flow rate to cylinder chamber A [l/min], engineering units
qvB flow rate from cylinder chamber B [l/min], engineering units
pA cylinder chamber A pressure [bar], engineering units
pB cylinder chamber B pressure [bar], engineering units
PPA power loss in orifice PA [W]
PBT power loss in orifice BT [W]
PLIFT power needed for lifting (Fv) [W]
PP pump’s output power, hydraulic power [W]
For lifting consider control edges
PA and BT partially open, defined by valve voltage U
PB and AT closed (no leakage)
U> 0 V PA, BT open
U< 0 V PB, AT open
The flow rate in each of the control edges (throttles) can be calculated with equation
Pressure relief valve (PRV) is closed
Hint!
Use
Force equation (cylinder)
Continuity equations (cylinder chamber flows and piston velocity)
Turbulent throttle equation(s)
Boundary conditions are pump and tank pressure: describe throttle flows as functions of pressures (pressure differences) to solve for the piston velocity.
Other solution methods also possible!

## Slide 7: 5. Input parameters
Input parameters for Groups A-J

## Slide 8: 5. Results
Outputs | Value | Unit | Definition
AA |  | [m2] | effective piston area A (piston side)
AB |  | [m2] | effective piston area B (rod side)
LOAD 1 |  |  | 
v1 |  | [m/s] | piston velocity
qv,A.1 |  | [l/min] | flow rate to cylinder chamber A, engineering units
qv,B.1 |  | [l/min] | flow rate from cylinder chamber B, engineering units
pA.1 |  | [bar] | cylinder chamber A pressure, engineering units
pB.1 |  | [bar] | cylinder chamber B pressure, engineering units
PPA.1 |  | [W] | power loss in orifice PA
PBT.1 |  | [W] | power loss in orifice BT
PLIFT.1 |  | [W] | power needed for lifting (Fv)
PPUMP.1 |  | [W] | pump’s output power, hydraulic power
LOAD 2 |  |  | 
v2 |  | [m/s] | piston velocity
qv,A.2 |  | [l/min] | flow rate to cylinder chamber A, engineering units
qv,B.2 |  | [l/min] | flow rate from cylinder chamber B, engineering units
pA.2 |  | [bar] | cylinder chamber A pressure, engineering units
pB.2 |  | [bar] | cylinder chamber B pressure, engineering units
PPA.2 |  | [W] | power loss in orifice PA
PBT.2 |  | [W] | power loss in orifice BT
PLIFT.2 |  | [W] | power needed for lifting (Fv)
PPUMP.2 |  | [W] | pump’s output power, hydraulic power
VALVE |  |  | 
KVALVE |  | [m^3/𝑠 1/√Pa] | valve capacity parameter for each control edge, full opening

## Slide 9: 6. Hydraulic cylinder system - lowering
Fluid Power Basics
Inputs
The same as in exercise 5, except
U valve command [V]
Outputs
v piston velocity [m/s]
qvA flow rate from cylinder chamber A [l/min], engineering units
qvB flow rate to cylinder chamber B [l/min], engineering units
pA cylinder chamber A pressure [bar], engineering units
pB cylinder chamber B pressure [bar], engineering units
PAT power loss in orifice AT [W]
PPB power loss in orifice PB [W]
PLOWER power from lowering (Fv ) [W]
PP pump’s output power, hydraulic power [W]
For lifting consider control edges
PB and AT partially open, defined by valve voltage U
PA and BT closed (no leakage)
U> 0 V PA, BT open
U< 0 V PB, AT open
The flow rate in each of the control edges (throttles) can be calculated with equation
Pressure relief valve (PRV) is closed

## Slide 10: 6. Input parameters
Input parameters for Groups A-J

## Slide 11: 6. Results
Outputs | Value | Unit | Definition
LOAD 1 |  |  | 
v1 |  | [m/s] | piston velocity
qv,A.1 |  | [l/min] | flow rate from cylinder chamber A, engineering units
qv,B.1 |  | [l/min] | flow rate to cylinder chamber B, engineering units
pA.1 |  | [bar] | cylinder chamber A pressure, engineering units
pB.1 |  | [bar] | cylinder chamber B pressure, engineering units
PPAT.1 |  | [W] | power loss in orifice AT
PPB.1 |  | [W] | power loss in orifice PB
PLIFT.1 |  | [W] | mechanical power from lowering (ïFvï)
PPUMP.1 |  | [W] | pump’s output power, hydraulic power
LOAD 2 |  |  | 
v2 |  | [m/s] | piston velocity
qv,A.2 |  | [l/min] | flow rate from cylinder chamber A, engineering units
qv,B.2 |  | [l/min] | flow rate to cylinder chamber B, engineering units
pA.2 |  | [bar] | cylinder chamber A pressure, engineering units
pB.2 |  | [bar] | cylinder chamber B pressure, engineering units
PAT.2 |  | [W] | power loss in orifice AT
PPB.2 |  | [W] | power loss in orifice PB
PLIFT.2 |  | [W] | mechanical power from lowering (ïFvï)
PPUMP.2 |  | [W] | pump’s output power, hydraulic power

## Slide 12: 7. Hydraulic cylinder system - leakage
Fluid Power Basics
Inputs
The same as in exercise 5, except
U= 0 valve command [V]
KLEAK leakage flow parameter [m3/s/Pa]
v= 0 piston velocity [m/s]
Outputs
qvPA flow rate through orifice PA [l/min], engineering units
qvPB flow rate through orifice PB [l/min], engineering units
qvAT flow rate through orifice AT [l/min], engineering units
qvBT flow rate through orifice BT [l/min], engineering units
qvP pump’s flow rate [l/min], engineering units
pA cylinder chamber A pressure [bar], engineering units
pB cylinder chamber B pressure [bar], engineering units
PPA power loss in orifice PA [W]
PPB power loss in orifice PB [W]
PAT power loss in orifice AT [W]
PBT power loss in orifice BT [W]
PP pump’s output power, hydraulic power [W]
F force needed to stop the cylinder movement [N]
The leakage flow in each of the control edges (throttles) is laminar and the flow rate can be calculated with equation
v= 0
M
PA
BT
AT
PB
A
B
P
T
T
F
Pressure relief valve (PRV) is closed

## Slide 13: 7. Input parameters
Input parameters for Groups A-J
*
Calculate parameter KLEAK
by using parameters
qv= 0.45/60000 m3/s
p= 50105 Pa
(0.45 l/min leakage @ 50 bar)

## Slide 14: 7. Results
Outputs | Value | Unit | Definition
KLEAK |  | [m3/s/Pa] | leakage flow rate parameter
qv,A |  | [l/min] | flow rate through orifice PA [l/min], engineering units
qv,B |  | [l/min] | flow rate through orifice PB [l/min], engineering units
qvAT |  | [l/min] | flow rate through orifice AT [l/min], engineering units
qvBT |  | [l/min] | flow rate through orifice BT [l/min], engineering units
qvP |  | [l/min] | pump’s flow rate [l/min], engineering units
pA |  | [bar] | cylinder chamber A pressure [bar], engineering units
pB |  | [bar] | cylinder chamber B pressure [bar], engineering units
PPA |  | [W] | power loss in orifice PA
PPB |  | [W] | power loss in orifice PB
PAT |  | [W] | power loss in orifice AT
PBT |  | [W] | power loss in orifice BT
PP |  | [W] | pump’s output power, hydraulic power
F |  | [N] | force needed to stop the cylinder movement

## Slide 15: 8. Hydraulic cylinder system – leak + movement
Fluid Power Basics
Inputs
The same as in exercise 7, except
F= 0 no external piston force [N]
Outputs
qvPA flow rate through orifice PA [l/min], engineering units
qvPB flow rate through orifice PB [l/min], engineering units
qvAT flow rate through orifice AT [l/min], engineering units
qvBT flow rate through orifice BT [l/min], engineering units
qvP pump’s flow rate [l/min], engineering units
pA cylinder chamber A pressure [bar], engineering units
pB cylinder chamber B pressure [bar], engineering units
PPA power loss in orifice PA [W]
PPB power loss in orifice PB [W]
PAT power loss in orifice AT [W]
PBT power loss in orifice BT [W]
PP pump’s output power, hydraulic power [W]
v piston velocity [m/s]
The leakage flow in each of the control edges (throttles) is laminar and the flow rate can be calculated with equation
F= 0
M
PA
BT
AT
PB
A
B
P
T
T
v
Hint!
Use
Force equation (cylinder)
Continuity equations (cylinder chamber flows and piston velocity)
Boundary conditions are pump and tank pressure: describe throttle flows as functions of pressure differences to solve for the piston velocity.
Other solution methods also possible!
Pressure relief valve (PRV) is closed

## Slide 16: 8. Input parameters
Input parameters for Groups A-J
*
Calculate parameter KLEAK
by using parameters
qv= 0.45/60000 m3/s
p= 50105 Pa
(0.45 l/min leakage @ 35 bar)

## Slide 17: 8. Results