## Slide 1
Fluid Power Basics - Assignments 2019
Assignment 3
Exercises 9-10
Version official
1.0
Calculation exercises
Exercises
Input prameters
Tables for results

## Slide 2: Instructions:
Form the research group (maximum 4 people) via MyCourses.
This file contains instructions for completing calculation exercises.
  Assignments explained
  Input parameters to be used. Different for each group (A-J).
Prepare 2 files
  This template with Results (use the existing tables in the document)
  Calculation file (pdf) inluding equations used. Electronic formats (Mathcad, Matlab, Excel, etc.). Also clear hand-written (and scanned) documents possible!
Submit your a) numerical results (this file) and b) calculation file (pdf) to MyCourses calculation assignment mailbox before the deadline!
  Deadline 24.3.2019

## Slide 3: Group identification (fill in)
Group code (A-J)
Group members

## Slide 4: 9. Hydrostatic transmission – pump - pipe - motor
M
Tmotor
pT = 0
pT = 0
npump
Vr,p
vol,p
hm,p
Vr,m
vol,m
hm,m
Tpump
Outputs
Motor pressure and flow rate
Pipe flow (laminar or turbulent) Case 1 and Case 2
Pipe pressure losses, Case 1 and Case 2
Pump pressure and torque
Motor (OUTPUT) power
Pump (INPUT) power
Pipe friction information on the next slide
Inputs |  |  |  |  |  | 
nmotor | rotational speed of motor [r/s] |  |  |  |  | 
Vr,m | motor’s swept volume [m3/r] |  |  |  |  | 
hvol,m | volumetric efficiency of motor [-] |  |  |  |  | 
hhm,m | hydromechanical efficiency of motor [-] |  |  |  |  | 
hvol,p | volumetric efficiency of pump [-] |  |  |  |  | 
hhm,p | hydromechanical efficiency of pump [-] |  |  |  |  | 
Vr,p | pump’s swept volume [m3/r] |  |  |  |  | 
Tmotor | motor's torque [Nm] |  |  |  |  | 
Lpipe | pipe length [m] |  |  |  |  | 
Dpipe | pipe's internal diameter [m] |  |  |  |  | 
1 | kinematic viscosity of hydralic fluid, case 1 [cSt] |  |  |  |  | 
2 | kinematic viscosity of hydralic fluid, case 2 [cSt] |  |  |  |  | 
 | density of hydraulic fluid [kg/m3] |  |  |  |  | 
Rz | pipe's internal surface roughness [m] |  |  |  |  | 
Two cases:
Two different fluid viscosities

## Slide 5: Pipe – pressure losses
Input
L pipe length
D pipe inner diameter
 fluid density
Rz pipe surface roughness
Case 1 and Case 2, two cases
1 fluid kinematic viscosity, Case 1
2 fluid kinematic viscosity, Case 2
Use Reynolds number (Re) for friction factor
Laminar friction factor
lam= 64/Re
Use Approximation below for turbulent friction factor check your value by using Moody chart (in the literature)
Avci, A & Karagoz, I. A Novel Explicit Equation for Friction Factor in Smooth and Rough Pipes
D
p2
p
qv
L
p1

## Slide 6: Input parameters
Input parameters for Groups A-F,H,J

## Slide 7: Output values

## Slide 8: 10. Systems’ Performance Comparison
M
PA
BT
AT
PB
A
B
P
T
T
v
F
F
M
A
B
v
T
Direct Drive Hydraulics (DDH) system
Directional Proportional Control Valve operated system
Focus:
Pump leakages defined by separate laminar leakage orifices for
internal leakage
external leakage (case drain)
Main question:
Power consumption of systems

## Slide 9
F
M
4
1
2
3
A
B
M
qvp.AB
qvp.BT
qvp.0
qv.cvA
qv.cvB
pACCU
qvp.0
v
”Ideal pump” flow rate qvp.0
qvp.A
qvp.B
qvp.AT
T
T
A
B
Hydraulic (symmetric) cylinder
Hydraulic pump-motor
Electric motor
Pressure accumulator (as tank)
Check valves (spring loaded), qv.cvA and qv.cvB
Pump motor’s internal and external leakage pathts
  qvp.AB internal (throttle)
  qvp.AT and qvp.BT external (throttles, case drain)
5
6
qv.cyl
qv.cyl
DDH system

## Slide 10: Directional Proportional Control Valve operated system
M
qvp.AB
qvp.BT
qvp.0
pTANK= 0
qvp.0
qvp.AT
T
qv.cyl
1
Ideal pump
Leakage models
  Internal
  External
2
The flow rate in each of the control edges (throttles) can be calculated with equation
Orifices
PA and BT open
AT and PB closed
PRV closed
M
PA
BT
AT
PB
A
B
P
T
T
v
F

## Slide 11: For both systems
No cylinder friction
No leakage in cylinder seals
No pump friction (hm= 1)
Pump’s flow rate to/from the system is ”ideal pump flow rate” minus ”leakages in pump”
Volumetric efficiency defined by laminar leakage orifices
  not by v this time

## Slide 12: Parameters – DDH system
Inputs
Vp pump’s swept volume [m3/r]
F load force [N]
v piston velocity [m/s]
D piston diameter [m]
d piston rod diameter [m]
R laminar resistance of leakage throttles [Pa/(m3/s)]
 pcrack cracking (open) pressure difference of check valve [Pa]
K laminar resistance of check valves [Pa/(m3/s)]
pACCU accumulator’s pressure [gauge pressure - Pa]
Outputs
A cylinder pistons’ effective area [m2]
p pressure difference (pA-pB) [bar]
pA cylinder chamber A pressure [bar]
pB cylinder chamber B pressure [bar]
qv.cyl cylinder flow rate (A and B chambers) [m3/s]
qvp.AB flow through internal leak throttle AB [m3/s]
qvp.AT flow through external leak throttle AT [m3/s]
qvp.BT flow through external leak throttle BT [m3/s]
qv.cvA flow through check valve ACCU  A [m3/s]
qv.cvB flow through check valve ACCU  B [m3/s]
qvp.0 ”ideal pump” flow rate [m3/s]
npump pump’s rotational speed [r/s]
Tpump pump shaft torque [Nm]
Pout cylinder’s mechanical power (Fv) [kW]
Pin pump’s mechanical power (shaft power) [kW]
qv.cv
pcv=pcrack+ Kqv.cv
Check valve pressure difference
qv
pthrottle=Rqv
Leakage orifice pressure difference

## Slide 13: Parameters – proportional control valve system
Inputs
U valve command [V]
Kvalve
valve’s orifices’ capacity,
full opening 10 V  40 l/min @ p= 35 bar)
qvpump pump’s flow rate is adapted for the motion,
pressure relief valve is closed!
Outputs
pA cylinder chamber A pressure [bar]
pB cylinder chamber B pressure [bar]
qvp.AB flow through internal leak throttle AB [m3/s]
qvp.AT flow through external leak throttle AT [m3/s]
qvp.BT flow through external leak throttle BT [m3/s]
qvp.0 ”ideal pump” flow rate [m3/s]
npump pump’s rotational speed [r/s]
Tpump pump shaft torque [Nm]
Power in and out
Pin pumps mechanical power (shaft power) [kW]
Pout cylinder’s mechanical power (Fv) [kW]
Proportional valve
PPA power loss in orifice PA [kW]
PBT power loss in orifice BT [kW]
Pump leakage
Pori.AB power loss in pump’s orifice AB [kW]
Pori.AT power loss in pump’s orifice AT [kW]
Pori.BT power loss in pump’s orifice BT [kW]

## Slide 14: System parameters
Input parameters for Groups A-F,H,J
Kvalve
valve’s orifices’ capacity,
full opening 10 V  40 l/min @ p= 35 bar)

## Slide 15: DDH system outputs

## Slide 16: Proportional valve system outputs

## Slide 17: Updates
  Input parameter table on page 14 corrected, parameter R is common for proportional valve operated and DDH systems (20.3.)