Name________________________ Student number________________

Home assignment 3

A thin triangular slab is loaded by a point force at node 3. Nodes 1 and 2 are fixed. Derive the equilibrium equations of the structure according to the large displacement theory in terms of the dimensionless displacement components  and . Approximation is linear and material parameters C and  are constants. Assume plane-stress conditions. When , side length and thickness of the slab are L and , respectively. Find also the solution to a small displacement problem by simplifying the equilibrium equations with the assumptions  and  .

# Text boxes

F

1

X

Y

1

2

3

L

L

x

y

2