Name_______________________ Student number________________

Home assignment 1

Electric current causes heat generation in element 2 of the bar shown. Calculate the temperature  at the center point, if the wall temperature (nodes 1 and 3) is . Cross sectional area and thermal conductivity  are constants. Heat production rate per unit length vanishes in element 1 and it is constant  in element 2

Solution template

In a pure heat conduction problem, density expressions of the bar model are given by

and

in which  is the temperature,  the thermal conductivity, and  the rate of heat production (per unit length).

For bar 1, the nodal temperatures are  and  of which the latter is unknown. With a linear interpolation to temperature (notice that variation of  vanishes)

,

.

When the approximation is substituted there, density expression  simplifies to

,

Virtual work expression is the integral of the density over the element domain

.

The nodal temperatures of bar 2 are  and . Linear interpolation gives (variations of the given quantities like  vanish)

,

.

When the approximation is substituted there, density expression  simplifies to

.

Element contribution to the variational expressions is the integral of density over the element domain

.

Variational expression is sum of the element contributions

.

Variation principle   and the fundamental lemma of variation calculus give

.    (

# Text boxes

1

X,x

3

2

Z,z

2

1