## Slide 1: Fundamentals of Sprays
AAE-E3030 Numerical Modeling of Multiphase Flows
25.2.2019
D.Sc. (Tech) Ossi Kaario

## Slide 2: Motivation
Why learn about sprays ?
Sprays are used in many industrial applications: engines (diesel & gasoline), furnaces, gas turbines, rockets and in many other applications: aerosols, water taps…
Therefore, understanding concepts related to sprays might be beneficial
This lesson is about sprays: general topics of sprays in order to better understand what sprays are and how they form and interact with their surroundings

## Slide 3: Course related phenomena
Wehrfritz et al., Comb. Flame 2016.

## Slide 4: Optical Spray Investigations
Pictures by Harri Hillamo, 2010
Fuel injection pressure is 1400bar
Gas density is 35 kg/m3
Nozzle diameter d=0.34mm
What does a fuel spray look like ?

## Slide 5
Field of optical view (~10 cm)
Nozzle hole (0.34 mm)
Nozzle tip

## Slide 19: Spray Angle

## Slide 20: Spray penetration & opening angle
spray tip penetration
opening
angle
Hillamo et al., 2010.
nozzle

## Slide 21
Dent (1971)
Hiroyasu & Kadota (1980)
Spray penetration correlations
:
:
OK/Aalto 2015
Gas density (kg/m3)
Liquid density (kg/m3)
Pressure difference (Pa)
Time (s)
Nozzle diameter (m)

## Slide 22
Hillamo et al., SAE 2008
Spray penetration &
opening angle
Opening angle
Heywood, 1988

## Slide 23
Nozzle types
Engines:
hole diameter D ~ 0.1-0.5mm
Furnaces:
diameter ~ 1m

## Slide 24: Some liquid fuel properties
Fuel | HVO | Fischer-Tropsch diesel | FAME (RME) | EN 590
Density at +15C° (kg/m3) | 775-785 | 770-785 | 885 | 835
Viscosity at +40C° (mm2/s) | 3.0-3.5 | 3.2-4.5 | 4.5 | 3.5
Cetane number | 80-99 | 73-81 | 51 | 53
Distillation range (C°) | 180-320 | 180-360 | 350-370 | 180-360
Heating value (MJ/kg) | 44 | 43 | 37.5 | 43

## Slide 25
Fuel | Methanol | DME
Density at +15C° (kg/m3) | 722.1 | 612
Viscosity at +40C° (mm2/s) | 0.45 | 0.22
Cetane number | ~ 5 | 55
Heating value (MJ/kg) | 22.7 | 29
Some liquid fuel properties

## Slide 26
Y. Gong et al., SAE 2010.
HEP = Heptane (C7 H16)
DF2= U.S. Diesel fuel
EN590=Standard Diesel in EU
HVO=Hydrotreated vegetable oil
Some liquid fuel properties

## Slide 27
Topics on Spray Velocity

## Slide 28: Sprays are pressure driven Cavitation
Liquid

## Slide 29: Cavitation

## Slide 30: Sprays are pressure driven Calculating the theoretical fuel exit velocity
Theoretical fuel exit velocity from nozzle
Velocity in practice

## Slide 31: Discharge coefficient Cd
Discharge coefficient
‘velocity coefficient’, used when calculating real injection velocity
used when calculating mass flow
‘area contraction coefficient’, used when calculating effective nozzle hole diameter

## Slide 32
Intact Liquid Core
Additional material

## Slide 33: Intact liquid core ?
Smallwood, G., and Gulder, O., Atom & sprays, 2000.
Additional material

## Slide 34: Intact liquid core ?
Hillamo et al. 2010, Atom. Sprays
6dn
or 2mm
Reynolds number compared to real high-pressure sprays.
DNS done with Uexit~100m/s
Desjardins et al, 2010
Chesnel et al. 2011
Additional material

## Slide 35: Intact liquid core ?
Turbulence inside the nozzle has bigger effect than previously thought of.
Taken the experimental and numerical evidence, it seems very likely that in modern high-pressure injection systems, the intact liquid core is either very short or even non-existent.
Desjardins et al, 2013, Atom. Sprays
Additional material

## Slide 36
Spray Equations

## Slide 37: Lagrangian spray modeling
Discrete computational points are tracked
Spray equations (Ordinary differential equation (ODE)):
  Parcel position
  Eq. (1) can be used to calculate the particle position at each time instant.

(1)
Droplet position,

## Slide 38: Lagrangian spray modeling
  Parcel equation of motion


## Slide 39: Lagrangian spray modeling
  or
  Eq. (2) can be used to update the particle velocity for each time instant, and then use Eq. (1) to update the position.
dt
(2)
Droplet velocity,
Droplet position,

## Slide 40: Droplet Drag
The resistance a droplet/particle encounters, is due to shear and form drag
Droplet drag coefficient Cd is calculated from
Droplet Reynolds number is
Boiko et al., 2013

## Slide 41: Lagrangian spray modeling (Matlab)
Constant Cd=0.424 and constant gas phase velocity (0 m/s)
Droplet size is constant d=100micro-m
Gas density is 2 kg/m3 and liquid density is 800kg/m3.
Constant gas phase velocity may be a strong assumption.

## Slide 42
Dispersed and continuous phase coupling

## Slide 43
Stokes number
    Stokes number
    Ratio of the characteristic particle time scale (or the momentum relaxation time scale)
    To the characteristic flow time scale
droplet diameter
D nozzle diameter
U0 flow velocity

## Slide 44: Stokes number & Turbulent dispersion
Figure by G. Stiesch

## Slide 45: Coupling regimes
Figure by Elghobashi, 1994.
One-way coupling  Gas phase only interacts with particles
Two-way coupling  Gas phase and particles both interact with each other
Four-way coupling  Additionally, particles interact with each other

## Slide 46
If Particles will have plenty of time to adjust to changes in flow field velocity. Particle and fluid velocities nearly equal.
If Particle velocity will be little affected by flow velocity.
Stokes number
St number
effect
St ~
Kaario, 2012

## Slide 47: Source term in N-S Eqs.
The flow field ’sees’ the droplets via source terms in the N-S eqs. In the 2-way coupling regime, the source term Md accounts for the coupling. Droplets ’see’ the flow field effect from the velocity difference.

## Slide 48: Group Work
Discuss in pairs for about 10 min:
What information is needed to calculate droplet/particle Stokes number ?
What information is not needed ?
What does a particle St number mean ?
If you would be given a task to design a spray configuration that would give a homogeneous mixture (of droplets and air / vapor and air), what kind of a St number would you aim for and why ?

## Slide 49
What is dense ?

## Slide 50: What is dense ?
~ 52%
~ 8%
b
d
b=d

## Slide 51: What is dense ?
Typically assumed dense if Vp/Vf > 10-3
Assuming spray mass is divided homogenously in a cone –like volume
From the schematic spray opening angle picture, the
area ratio:
α
D
S
r
r
assuming
nozzle diameter
spray penetration
spray opening angle
If D=90µm, S<8.1mm

## Slide 52: Nozzle Hole Size vs Average Fuel Concentration
Average concentration
Assumed constant injection rate
The spray volume evolves as a cone
Bottom area of the cone
Spray penetration assumes well known correlation
We obtain
Vuorinen, V., thesis 2010
Additional material

## Slide 53: Nozzle Hole Size vs Average Fuel Concentration
D=0.12mm, α=15º or 20º
D=0.12mm or 0.36mm, α=20º
Calculated result from the previous slide final result
Additional material

## Slide 54: Turbulence in flow
Turbulent flow consists of vortices (eddies) of different size
The biggest vortices are of the size of the flow geometry
The eddies are breaking up into smaller eddies. At the same time kinetic energy is transported from the bigger eddies to smaller ones
At the smallest turbulent scale (Kolmogorov scale) kinetic energy is dissipated into heat
Fluctuations
Convection

## Slide 55: Turbulence in flow
Turbulence  Shear
Turbulence is characterized by the following:
  Three dimensional
  Unsteady
  Random
  Strong vorticity
  Dissipative
  Strongly diffusive
Turbulence = increased mixing !

## Slide 56: Jet development
Potential core
~ 4-6D
Developing flow
~15-20D
Self-preserving flow
D
Nozzle
Potential core
Mixing area
Developing flow
Self-preserving flow

## Slide 57: Jet development: Kelvin Helmholtz Instability and Spray Mixing
Spray and jet turbulence is initiated by a Kelvin Helmholtz instability at the near nozzle region
Growth rate of KH instability is related to the velocity difference of the fluids and to the wavelength.

## Slide 58: KH Instability

## Slide 59: KH Instability and Mixing
Figure V. Vuorinen

## Slide 60: Additional Reading
Crowe, C.T., Schwarzkof, J.D., Sommerfeld, M., and Tsuji, Y., Multiphase Flows with Droplets and Particles, 2nd edition, CRC Press, ISBN 978-1-4398-4050-4, 2012.
Wehrfritz Armin, Kaario Ossi, Vuorinen Ville, and Bart Somers, Large Eddy Simulation of n-dodecane spray flames using flamelet generated manifolds, Combustion and Flame, Vol. 167, pp. 113-131, 2016.
Vuorinen, V., Hillamo, H., Kaario, O., Larmi, M., and Fuchs, L., Large Eddy Simulation of droplet stokes number effects on turbulent spray shape, Atomization and Sprays, vol. 20, no. 2, pp. 93–114, 2010.
Kaario Ossi, Vuorinen Ville, Hulkkonen Tuomo, Keskinen Karri, Nuutinen Mika, Larmi Martti, and Tanner Franz, Large Eddy Simulation of High Gas Density Effects in Fuel Sprays, Atomization and Sprays, Vol. 23, Issue 4, pp. 297-325, 2013.
Eaton, J. and Fessler, J., Preferential concentration of particles by turbulence, Int. J. Multiphase Flow, vol. 20, pp. 169–209, 1994.
Elghobashi, S., Particle-laden turbulent flows: Direct simulation and closure models, Appl. Sci. Res., vol. 52, pp. 309–329, 1994.
G. J. Smallwood and Ö. L. Gulder, Views on the structure of transient diesel sprays, Atomization and sprays, Vol. 10, pp.-355-386, 2000.
J. Naber and D. L. Siebers, Effects of gas density and vaporization on penetration and dispersion of diesel sprays, SAE paper 960034, 1996.
D.L. Siebers, Scaling liquid-phase fuel penetration in diesel sprays based on mixing-limited vaporization, SAE paper 1999-01-0528, 1999.
Harri Hillamo, Teemu Sarjovaara, Ossi Kaario, Ville Vuorinen, and Martti Larmi, Diesel spray visualization and shockwaves, Atomization and Sprays, Vol. 20, Issue 3, pp. 177-189, 2010.