## Slide 1: Probabilistic Robotics Bayes Filter Implementations FastSLAM
ELEC-E8111 Autonomous Mobile Robots
Arto Visala
13. 3.2019

## Slide 2: The SLAM Problem
SLAM stands for simultaneous localization and mapping
The task of building a map while estimating the pose of the robot relative to this map
Why is SLAM hard? Chicken and egg problem: a map is needed to localize the robot and a pose estimate is needed to build a map

## Slide 3: The SLAM Problem
Given:
  The robot’s controls
  Observations of nearby features
Estimate:
  Map of features
  Path of the robot
A robot moving though an unknown, static environment

## Slide 4: Why is SLAM a hard problem?
SLAM: robot path and map are both unknown!
Robot path error correlates errors in the map

## Slide 5: Why is SLAM a hard problem?
In the real world, the mapping between observations and landmarks is unknown
Picking wrong data associations can have catastrophic consequences
Pose error correlates data associations
Robot pose
uncertainty

## Slide 6: Data Association Problem
A data association is an assignment of observations to landmarks
In general there are more than (n observations, m landmarks) possible associations
Also called “assignment problem”

## Slide 7: Particle Filters
Represent belief by random samples
Estimation of non-Gaussian, nonlinear processes
Sampling Importance Resampling (SIR) principle
  Draw the new generation of particles
  Assign an importance weight to each particle
  Resampling
Typical application scenarios are tracking, localization, …

## Slide 8
Particle Filter algorithm 1/3

## Slide 9
Particle Filter algorithm 2/3

## Slide 10
Particle Filter algorithm 3/3

## Slide 11: Localization vs. SLAM
A particle filter can be used to solve both problems
Localization: state space < x, y, >
SLAM: state space < x, y, , map>
  for landmark maps = < l1, l2, …, lm>
  for grid maps = < c11, c12, …, c1n, c21, …, cnm>
Problem: The number of particles needed to represent a posterior grows exponentially with the dimension of the state space!

## Slide 12: Dependencies
Is there a dependency between the dimensions of the state space?
If so, can we use the dependency to solve the problem more efficiently?

## Slide 13: Dependencies
Is there a dependency between the dimensions of the state space?
If so, can we use the dependency to solve the problem more efficiently?
In the SLAM context
  The map depends on the poses of the robot.
  We know how to build a map given the position of the sensor is known.

## Slide 14: Factored Posterior (Landmarks)
Factorization first introduced by Murphy in 1999
poses
map
observations & movements

## Slide 15: Factored Posterior (Landmarks)
SLAM posterior
Robot path posterior
landmark positions
Factorization first introduced by Murphy in 1999
Does this help to solve the problem?
poses
map
observations & movements

## Slide 16: Mapping using Landmarks
Knowledge of the robot’s true path renders landmark positions conditionally independent
. . .
Landmark 1
observations
Robot poses
controls
x1
x2
xt
u1
ut-1
l2
l1
z1
z2
x3
u1
z3
zt
Landmark 2
x0
u0

## Slide 17: Factored Posterior
Robot path posterior (localization problem)
Conditionally independent landmark positions

## Slide 18: Rao-Blackwellization
This factorization is also called Rao-Blackwellization
Given that the second term can be computed efficiently, particle filtering becomes possible!

## Slide 19: FastSLAM
Rao-Blackwellized particle filtering based on landmarks [Montemerlo et al., 2002]
Each landmark is represented by a 2x2 Extended Kalman Filter (EKF)
Each particle therefore has to maintain M EKFs
Landmark 1
Landmark 2
Landmark M
…
x, y, 
Landmark 1
Landmark 2
Landmark M
…
x, y, 
Particle
#1
Landmark 1
Landmark 2
Landmark M
…
x, y, 
Particle
#2
Particle
N
…

## Slide 20: FastSLAM algorithm, feature = landmark

## Slide 21: FastSLAM – Action Update
Particle #1
Particle #2
Particle #3
Landmark #1
Filter
Landmark #2
Filter

## Slide 22: FastSLAM – Sensor Update
Particle #1
Particle #2
Particle #3
Landmark #1
Filter
Landmark #2
Filter

## Slide 23: FastSLAM – Sensor Update
Particle #1
Particle #2
Particle #3
Weight = 0.8
Weight = 0.4
Weight = 0.1

## Slide 24: FastSLAM Complexity
Update robot particles based on control ut-1
Incorporate observation zt into Kalman filters
Resample particle set
N = Number of particles
M = Number of map features
O(N)
Constant time per particle
O(N•log(M))
Log time per particle
O(N•log(M))
O(N•log(M))
Log time per particle
Log time per particle

## Slide 25: Data Association Problem
A robust SLAM must consider possible data associations
Potential data associations depend also on the pose of the robot
Which observation belongs to which landmark?

## Slide 26: Multi-Hypothesis Data Association
Data association is done on a per-particle basis
Robot pose error is factored out of data association decisions

## Slide 27: Per-Particle Data Association
Was the observation
generated by the red
or the blue landmark?
P(observation|red) = 0.3
P(observation|blue) = 0.7
Two options for per-particle data association
  Pick the most probable match
  Pick an random association weighted by the observation likelihoods
If the probability is too low, generate a new landmark

## Slide 28: Results – Victoria Park
4 km traverse
< 5 m RMS position error
100 particles
Dataset courtesy of University of Sydney
Blue = GPS
Yellow = FastSLAM

## Slide 29: Results – Data Association

## Slide 30: Results – Accuracy

## Slide 31: Grid-based SLAM
Can we solve the SLAM problem if no pre-defined landmarks are available?
Can we use the ideas of FastSLAM to build grid maps?
As with landmarks, the map depends on the poses of the robot during data acquisition
If the poses are known, grid-based mapping is easy (“mapping with known poses”)

## Slide 32: Rao-Blackwellization
Factorization first introduced by Murphy in 1999
poses
map
observations & movements

## Slide 33: Rao-Blackwellization
SLAM posterior
Robot path posterior
Mapping with known poses
Factorization first introduced by Murphy in 1999
poses
map
observations & movements

## Slide 34: Rao-Blackwellization
This is localization, use MCL
Use the pose estimate from the MCL part and apply mapping with known poses

## Slide 35: MCL Monte Carlo Localization

## Slide 36: A Graphical Model of Rao-Blackwellized Mapping
m
x
z
u
x
z
u
2
2
x
z
u
...
t
t
x
1
1
0
1
0
t-1

## Slide 37: Rao-Blackwellized Mapping
Each particle represents a possible trajectory of the robot
Each particle
  maintains its own map and
  updates it upon “mapping with known poses”
Each particle survives with a probability proportional to the likelihood of the observations relative to its own map

## Slide 38: Particle Filter Example
map of particle 1
map of particle 3
map of particle 2
3 particles

## Slide 39
Occupancy grid Fast SLAM

## Slide 40: Problem
Each map is quite big in case of grid maps
Since each particle maintains its own map
Therefore, one needs to keep the number of particles small
Solution: Compute better proposal distributions!
Idea: Improve the pose estimate before applying the particle filter

## Slide 41: Pose Correction Using Scan Matching
Maximize the likelihood of the i-th pose and map relative to the (i-1)-th pose and map
robot motion
current measurement
map constructed so far
Notes: To compute consistent maps, we apply a recursive scheme.
At each point in time we compute the most likely position of the robot, given the map constructed so far.
Based on the position hat l-t, we then extend the map an incorporate the scan obtained at time t.

## Slide 42: Motion Model for Scan Matching
Raw Odometry
Scan Matching

## Slide 43: FastSLAM with Improved Odometry
Scan-matching provides a locally consistent pose correction
Pre-correct short odometry sequences using scan-matching and use them as input to FastSLAM
Fewer particles are needed, since the error in the input in smaller
[Haehnel et al., 2003]

## Slide 44: Graphical Model for Mapping with Improved Odometry
m
z
k
x
1
u'
0
u
z
k-1
...
1
z
...
u
k-1
...
k+1
z
u
k
z
u
2k-1
2k-1
...
x
0
k
x
2k
z
2k
...
u'
2
u'
n
...
x
n·k
z
u
u
(n+1)·k-1
n·k
n·k+1
...
(n+1)·k-1
z
...
n·k
z
...
...

## Slide 45
FastSLAM with Scan-Matching

## Slide 46: FastSLAM with Scan-Matching
Loop Closure

## Slide 47: Further Improvements
Improved proposals will lead to more accurate maps
They can be achieved by adapting the proposal distribution according to the most recent observations
Flexible re-sampling steps can further improve the accuracy.

## Slide 48: Improved Proposal
The proposal adapts to the structure of the environment

## Slide 49: Selective Re-sampling
Re-sampling is dangerous, since important samples might get lost (particle depletion problem)
In case of suboptimal proposal distributions re-sampling is necessary to achieve convergence.
Key question: When should we re-sample?

## Slide 50: Conclusion
The ideas of FastSLAM can also be applied in the context of grid maps
Utilizing accurate sensor observation leads to good proposals and highly efficient filters
It is similar to scan-matching on a per-particle base
The number of necessary particles and re-sampling steps can seriously be reduced
Improved versions of grid-based FastSLAM can handle larger environments than naïve implementations in “real time” since they need one order of magnitude fewer samples

## Slide 51: More Details on FastSLAM
M. Montemerlo, S. Thrun, D. Koller, and B. Wegbreit. FastSLAM: A factored solution to simultaneous localization and mapping, AAAI02
D. Haehnel, W. Burgard, D. Fox, and S. Thrun. An efficient FastSLAM algorithm for generating maps of large-scale cyclic environments from raw laser range measurements, IROS03
M. Montemerlo, S. Thrun, D. Koller, B. Wegbreit. FastSLAM 2.0: An Improved particle filtering algorithm for simultaneous localization and mapping that provably converges. IJCAI-2003
G. Grisetti, C. Stachniss, and W. Burgard. Improving grid-based slam with rao-blackwellized particle filters by adaptive proposals and selective resampling, ICRA05
A. Eliazar and R. Parr. DP-SLAM: Fast, robust simultanous localization and mapping without predetermined landmarks, IJCAI03